Gene, Danny:

This is my recommendation for the MEX bistatic radar operation tomorrow evening (Monday, Pacific Time).

I have a flight scheduled to arrive at Burbank at 15:40 PDT; I'll probably stop to get something to eat, which should still get me to JPL before the pre-cal starts at 17:55 PDT.

Dick

- - - - - - - - - - - - - - - - - - - - - - - - - - - - -

2006/150 (UTC)

- - - - - - -

00:55  Begin Pre-cal at DSS 14

FGAIN = 60 dB (all channels)

FRO_X = 0; FRO_S = 0 (changes later)

Start 4-channel 25 kHz recordings after Step 4

Stop 25 kHz recording after Step 18

02:55  Begin track

03:08  Begin 4-channel 25 kHz recordings (SCHAN 3)

03:09  DL = S+X unmodulated 1-way

03:25  Begin SLEW #1

03:35  FRO_X = -21000 Hz (SCHAN 3,4) (puts carrier at +18 kHz)

FRO_S =  -4200 Hz (SCHAN 3,4) (puts carrier at  +3 kHz)

03:37  Begin MiniCal #1

03:52  End MiniCal #1 (end of Step 5)

03:56  Begin 4-channel 100 kHz recordings (SCHAN 4)

03:57  End SLEW #1

Begin BSR (weak surface echoes; LCP > RCP, if visible)

04:58  End BSR

Begin SLEW #2

04:59  End 100 kHz recordings (SCHAN 4)

05:04  Begin MiniCal #2

05:19  End MiniCal #2 (end of Step 5)

05:20  FRO_X = 0  (SCHAN 3,4)

FRO_S = 0  (SCHAN 3,4)

05:25  End of track

Begin Post-Cal

06:25  End Post-cal (if not before)

End 25 kHz recordings

End of Activity