Mars Express Bistatic Radar Experiment

Operations Plan and Report

10 August 2006

Summary

=======

DSN Antenna:                                                     43

Pass:                                                          1167

Orbit:                                                         3320

Orbit Start Time:                               2006-08-10T03:59:33

HGA Pointing:                                              Specular

Start   Phoenix B      End

--------  ----------  --------

Specular Condition (ERT):            06:32:00   07:17:00   07:32:00

Target Latitude (deg N):                35.11      69.19      73.76

Longitude (deg E):              134.72     134.70     214.76

Rp (km):                         3394.      3394.      3394.

Incidence/Reflection Angle (deg):       75.57      62.57      48.51

Slant Range (km):                       7564.      2672.       872.

Slew Angle (deg):                       28.86      54.86      82.98

Doppler (carrier, fd; Hz):              47385      70418      55678

Doppler (echo, fr; Hz):                 43642      75358      72797

Doppler Difference (fdd; Hz):            3744      -4940     -17119

Earth-Mars Distance (m):            3.783E+11  3.783E+11  3.783E+11

Experiment Set Up

=================

This experiment was conducted using Canberra's DSS 43.  Danny Kahan, Aseel Anabtawi, Sami Asmar, and Dick Simpson were in the Radio Science Support Area at JPL; Jesse Velasco was in the NOPE area through the pre-cal.

Performance Problems and Notes

==============================

S-LCP and S-RCP inputs to the RSR's were in their normal configuration.  For the past several months, they have usually been swapped; but for the first time in many months they came up correct.

During the pre-cal the S-LCP and X-LCP noise diodes came on while their respective DTT's were being configured.  This meant they were on for about 10 minutes rather than the expected 5.

X-Band echoes were seen throughout the experiment with RCP being the stronger except for the last 10 minutes.  The X-Band carrier (direct) signal was intermittent, usually stronger on RCP when present.  No S-Band signals were seen.

Data Acquisition

================

RSRs were configured as in Table 1.  Note that the S-Band polarizations are swapped compared with the nominal configuration; but this has been the case for several months at DSS 43.

Table 1

----------------------------------------------------

RSR  Channel Mode  ATT FGAIN        Operator

dB

----- ------- ---- ---- ----- ----------------------

RSR1A  S-LCP   1-W auto   60    Kahan

RSR1B  X-LCP   1-W auto   60    Kahan

RSR2A  S-RCP   1-W auto   60    Kahan

RSR2B  X-RCP   1-W auto   60    Kahan

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   backup (not recorded)

2          8 ksps   backup (not recorded)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  "Steps" are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-LCP  X-LCP  S-RCP  X-RCP  Notes / Comments

RSR1A  RSR1B  RSR2A  RSR2B

-------- ----- --------- -----  -----  -----  -----  ------------------------

2006/175

--------

Pre-Cal  03:48     1      -9.7   -9.8   -9.9   -9.6  All to sky (dB)

15.0   13.5   10.5   12.5  ATT settings

03:51     2      -9.7   -0.1  -10.0    0.0  X-Band to AMB

03:53     3      -0.3   -0.2  -10.0    0.1  S-RCP to AMB

03:54     4      -0.3   -0.2   -0.2    0.0  S-LCP to AMB

03:55                                       AMB load physical temps:

S1=21.38

S2=22.56

X1=21.31

Weather conditions:

T=11.6C

H=41.1 percent

sky = light clouds

03:56            -9.8   -9.8  -10.1   -9.6  ADC amp after AUTO reset

26.5   25.5   22.5   25.0  ATT settings

04:00:01                                    Begin 25 kHz recording

04:02     5      -9.8   -9.8  -10.0   -9.6  Configure DTT's

04:05     6      -9.8   -9.9  -10.1   -8.9  X-RCP ND ON

04:10     7      -9.7  -21.9  -10.0  -15.8  X-Band to sky

04:15     8      -9.9  -17.0  -10.1  -22.0  X-RCP ND OFF; XL ND ON?

04:20     9      -9.8  -17.1  -10.0  -22.1  XL ND ON (again?)

04:25    10      -9.7   -9.3  -10.0   -9.7  X-Band to AMB

04:26                                       AMB physical temps:

S1=21.69

S2=22.62

X1=21.25

04:30    11      -9.8  -10.0  -10.0   -9.7  X-LCP ND OFF

04:35    12      -9.8  -22.1  -10.0  -22.1  X-Band to sky

04:40    13      -9.8  -22.1   -9.8  -22.1  S-RCP ND ON

04:45    14      -9.8  -22.1  -19.5  -22.1  S-RCP to sky

04:50    15      -9.5  -22.1  -22.0  -22.1  S-RCP ND OFF; SL ND ON?

04:55    16      -9.6  -22.0  -21.8  -22.0  S-LCP ND ON (again?)

05:00    17     -18.6  -22.1  -22.0  -22.0  S-LCP to sky

05:05    18     -21.1  -22.1  -22.0  -22.1  S-LCP ND OFF

05:10                                       Stop recording

AMB physical temps:

S1=21.88

S2=22.62

X1=20.81

05:30   BOT                                 X-Band in lock

MEX MOCC requests TLM

05:32            18.3   32.4   42.2   57.3  Carrier to noise (dB/Hz)

05:38                          -987  -1623  Carrier offset (Hz)

05:46           -20.9  -21.7  -21.7  -20.6  TLM OFF (ADC amp, dB)

--    40.0   42.0   64.5  Carrier to noise (dB/Hz)

-1056  -1873  Carrier offset (Hz)

05:49                                       Start 25 kHz recording

06:01           -20.9  -21.6  -21.5  -20.6  ADC amplitude (dB)

--    40.2   42.0   64.6  Carrier to noise (dB/Hz)

-1135  -2164  Carrier offset (Hz)

06:13           -20.8  -21.4  -21.5  -20.7  ADC amplitude (dB)

--    40.6   41.8   64.5  Carrier to noise (dB/Hz)

-1210  -2439  Carrier offset (Hz)

06:15                                       Begin Slew #1

06:24           -20.7  -21.4  -21.5  -20.7  ADC amp (dB)

--     29.1   23.1   32.0  Carrier to noise (dB/Hz)

MiniCal1 06:25     1     -20.7  -21.3  -21.5  -15.2  XR ND ON

06:28     2     -20.6  -21.4  -19.4  -20.7  XR ND OFF; SR ND ON

06:31     3     -20.7  -17.0  -21.5  -20.6  SR ND OFF; XL ND ON

06:34     4     -18.5  -21.3  -21.5  -20.6  XL ND OFF; SL ND ON

06:37     5     -20.7  -21.2  -21.4  -20.6  SL ND OFF

BSR      06:41                                       X-RCP echo at -7500 Hz

06:43                                       X-LCP echo at -7000 Hz

06:44                                       Begin 100 kHz recording

06:45                                       End Slew #2; Begin BSR

06:53                   20.0          29.0  Echo to noise (dB/Hz)

-6500  Echo offset (Hz)

07:15                   5000          5000  X-Band FRO (Hz)

21.0  Echo to nolise (dB/Hz)

-3000  Echo offset (Hz)

07:20                   20.0          20.0  Echoes ~equal (dB/Hz)

0             0  Echoes at center

07:25                  12000         12000  X-Band FRO (Hz)

07:26                   27.0          29.0  Echo to noise (dB/Hz)

-2000         -2000  Echo offsedt (Hz)

07:29                                       X-LCP now dominant

07:31                   23.0                Echo to noise (dB/Hz)

07:32                                       End 100 kHz recording

07:33                      0             0  X-Band FRO

07:34           -20.3  -20.8  -21.0  -20.2  ADC amp (dB)

MiniCal2 07:35     1     -20.3  -20.7  -20.9  -15.1  XR ND ON

07:38     2     -20.4  -20.8  -19.0  -19.9  XR ND OFF; SR ND ON

07:41     3     -20.2  -16.7  -20.7  -20.0  SR ND OFF; XL ND ON

07:44     4     -18.0  -20.5  -20.9  -19.8  XL ND OFF; SL ND ON

07:47     5     -20.2  -20.5  -20.8  -19.8  SL ND OFF

07:53                   13.0          17.0  Carrier to noise (dB/Hz)

-3324  Carrier offset (Hz)

08:09           -19.8  -20.2  -20.4  -19.4  ADC amplitude (dB)

--    23.0   18.5   31.3  Carrier to noise (dB/Hz)

-1443  -3300  Carrier offset

08:16             --    39.2   40.5   62.5  Carrier to Noise (dB/Hz)

Post-Cal 08:25   EOT                                 DSS 43 to zenith

08:35     1      -9.8  -10.2  -10.2   -9.7  All to AMB

AMB phys temps:

S1=20.56

S2=21.31

X1=19.50

08:38     2      -9.9  -10.1  -10.1   -8.8  XR ND ON

08:41     3      -9.8  -10.1   -9.9   -9.8  XR ND OFF; SR ND ON

08:44     4      -9.8   -9.8  -10.0   -9.7  SR ND OFF; XL ND ON

08:47     5      -9.5  -10.2  -10.2   -9.7  XL ND OFF; SL ND ON

08:50     6     -18.5  -22.0  -22.1  -22.0  All to sky

08:53     7     -21.2  -17.2  -21.9  -22.1  SL ND OFF; XL ND ON

08:56     8     -21.1  -22.2  -19.5  -22.1  XL ND OFF; SR ND ON

08:59     9     -21.1  -22.1  -21.8  -15.7  SR ND OFF; XR ND ON

09:02    10     -21.2  -22.0  -22.0  -22.1  XR ND OFF

AMB physical temps:

S1=20.31

S2=21.12

X1=19.44

Weather conditions:

T=6.8C

H=60.4 percent

sky=clear

EOA      09:06                                       Stop 25 kHz recording

AMB = ambient load

BOT = Beginning of Track

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Dick Simpson

Original: 2006-08-10

Editorial corrections: 2006-08-14

Minor edits: 2006-08-16