Mars Express Bistatic Radar Experiment

Operations Plan and Report

20 February 2010

Summary

=======

DSN Antenna:                                                     14

Pass:                                                           N/A

Orbit:                                                         7865

Orbit Start Time:                              2010-02-20T09:11:06

HGA Pointing:                                              Specular

Start    Mid Point      End

--------  ----------  --------

Specular Condition (ERT):               09:07      09:43      10:20

Target Latitude (deg N):               -26.30     -32.04     -38.54

Longitude (deg E):               10.18       2.83     355.91

Rp (km):                         3394.      3394.      3394.

Incidence/Reflection Angle (deg):       39.03      44.68      51.17

Slant Range (km):                      10959.     11007.     10453.

Slew Angle (deg):                      101.95      90.63      77.65

Doppler (carrier, fd; Hz):            -28748.    -32484.    -33830.

Doppler (echo, fr; Hz):                -7082.       -41.      6768.

Doppler Difference (fdd; Hz):         -21666.    -32443.    -40598.

Earth-Mars Distance (m):            1.084E+11  1.084E+11  1.084E+11

NB: The DSN is no longer routinely using pass numbers; so this entry in the

summary will not be maintained in this and future reports.

Experiment Set Up

=================

This experiment was conducted using the Goldstone DSS 14.  Danny Kahan and Gene Goltz were in the Radio Science Support Area (RSSA) at JPL.

Performance Problems and Notes

==============================

The S-RCP maser had been red for the experiment on 2010/041.  It was repaired about a week later, but the cool-down failed; so it was red again for this experiment (DR #G110058), and no S-RCP data were collected.

Strong interference was noted on both X-Band channels over the time interval 09:52-10:36.  Danny Kahan believed it was from another spacecraft.

Real-time monitoring during Mini-Cal #2 indicated that the X-LCP noise diode was not turned off at the end of Mini-Cal 2 step 3.

Data Acquisition

================

RSRs were configured as in Table 1.

Table 1

----------------------------------------------------

RSR  Channel Mode  ATT FGAIN        Operator

dB

----- ------- ---- ---- ----- ----------------------

RSR3A  S-LCP   1-W auto   60    UNK

RSR3B  X-LCP   1-W auto   60    UNK

RSR2A   N/A

RSR2B  X-RCP   1-W auto   63    UNK

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   Occultation bandwidth (not recorded for BSR)

2          8 ksps   Occultation backup (not recorded for BSR)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  "Steps" are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-LCP  X-LCP  S-RCP  X-RCP  Notes / Comments

2010/051       (new NOP) RSR3A  RSR3B   N/A   RSR2B

-------- ----- --------- -----  -----  -----  -----  ------------------------

FGAIN                       60     60            63  Set FGAIN

Pre-Cal  05:15     1     -10.1  -10.0   n/a   -10.1  ADC amplitude (dB)

21.5   11.5          10.0  ATTEN settings (dB)

05:18 att auto  -10.1  -10.4   n/a   -10.2  ADC amplitude (dB)

21.5   12.0          11.5  ATTEN settings (dB)

05:20     2     -10.1   -0.4   n/a    -0.7

05:21     3      -5.6   -0.4   n/a    -0.8

05:24    4,5     -5.6   -0.4  -0.7    -0.7

05:25 att auto   -9.9   -9.8   n/a   -10.0  ADC amplitude (dB)

26.0   23.5   n/a    22.5  ATTENB settings (dB)

AMB physical temps:

S1=11.62

S2=15.12

X1=11.75

Local weather:

T=7.6C

H=68.6 percent

Sky=overcast

05:27 rec 3 e                               Begin 25 kHz recording

05:30     6      -9.8   -9.8   n/a    -9.9  All to AMB

05:35     7     -10.0   -9.9   n/a    -9.8  XR ND ON

05:42     8     -10.0  -22.0   n/a   -20.2  X-Band to sky

05:47     9     -10.1  -21.9   n/a   -22.6  XR ND OFF

05:52    10     -10.0  -19.6   n/a   -22.6  XL ND ON;

confirmed 12.5K ND

05:57   11,12   -10.0   -9.7   n/a   -10.0  X-Band to AMB

AMB load physical temps:

S1=11.44

S2=14.75

X1=11.69

06:02    13     -10.0   -9.8   n/a   -10.0  XL ND OFF

06:07    14     -10.1  -21.9   n/a   -22.6  X-Band to sky

06:12    15     -10.0  -22.1   n/a   -22.6

06:17    16     -10.1  -21.9   n/a   -22.6

06:22    17     -10.0  -21.9   n/a   -22.6  Confirmed 12.5K ND

06:27    18      -9.9  -21.7   n/a   -22.5  SL ND ON

06:32    19     -13.4  -21.9   n/a   -22.6  SL to sky

06:37    20     -14.1  -21.9   n/a   -22.6  SL ND OFF

AMB load physical temps:

S1=11.25

S2=14.50

X1=11.62

06:42   end     -14.5  -21.9   n/a   -22.5  Pause 25 kHz recording

BOT      07:05           -14.9  -21.7   n/a   -17.6  ADC amplitude (dB)

07:50                                       X-Band TX ON

08:14                                       S-Band TX ON

08:30 rec 3 e   -18.6  -21.5   n/a   -18.3  Resume 25 kHz recording

X-TLM OFF

08:45           -17.0  -21.4         -18.3  DSS switch to Mars

pointing predicts

08:47 sfro 3/SX   +5K   +25K          +25K Rcvr tuning offset (Hz)

MiniCal1 08:48     1     -16.7  -21.5   n/a   -17.6  XR ND ON

Confirmed 12.5 K ND

08:51     2     -15.9  -21.5   n/a   -18.8  XR ND OFF

08:54     3     -16.3  -19.4   n/a   -18.5  XL ND ON

08:57     4     -17.3  -21.5   n/a   -17.9  XL ND OFF; SL ND ON

09:00     5     -15.2  -21.5   n/a   -17.7  SL ND OFF

09:03    end    -17.5  -21.5   n/a   -17.9  ADC amplitude (dB)

BSR      09:07 rec 4 e   -17.3  -21.4   n/a   -17.7  Begin 100 kHz recording

09:40 sfro 3/X          +35K          +35K  Rcvr tuning offset

09:52                                       Non-MEX signal appears

10:20 rec 4 d   -18.3  -21.2   n/a   -17.9  End 100 kHz recording

MiniCal2 10:21     1     -18.6  -21.1   n/a   -16.6  Confirmed 12.5 ND

10:24     2     -19.3  -21.2   n/a   -17.9

10:27     3     -17.5  -19.3   n/a   -17.9

10:30     4     -16.1  -19.2   n/a   -18.0

10:33     5     -16.6  -19.2?  n/a   -17.7

10:36    end                                DSS 14 switch to s/c

pointing predicts

Non-MEX signal gone

sfro 3/SX     0      0             0  Rcvr tuning offset (Hz)

10:40                                       repeat steps 2 and 4

EOT/stow 10:55           -17.3  -20.9   n/a   -17.4

Post-Cal 11:09     1     -10.1   -9.8   n/a    -9.9  AMB load physical temps:

S1=10.62

S2=12.25

X1=11.00

11:12     2     -10.0   -9.7   n/a    -9.7

11:15     3      -9.9   -9.7   n/a   -10.0

11:18     4     -10.0   -9.6   n/a    -9.9

11:21     5      -9.8   -9.7   n/a   -10.0

11:24     6     -13.3  -21.9   n/a   -22.4

11:27     7     -14.6  -19.5   n/a   -22.4

11:30     8     -14.6  -21.9   n/a   -22.5

11:33     9     -14.4  -21.8   n/a   -20.1

11:36    10     -14.7  -21.8   n/a   -22.5  AMB load physical temps:

S1=10.50

S2=12.31

X1=11.00

Local weather:

T=5.4C

H=80.7 percent

sky=partly cloudy

11:40   end     -12.5  -21.9   n/a   -22.4  End 25 kHz recording

AMB = ambient load

BOT = Beginning of Track

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOA = End of activity

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

NOP = Network Operations Plan

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

s/c = spacecraft

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Post Analysis Summary

X-Band 10-s Average Data:  The table below summarizes the time division for capturing the echo power as the signal drifted through the 25 kHz X-Band receiving pass band.  There was a single FRO at 09:40.  A strong signal (Kahan guessed from MRO) interfered with the surface echo at various times after 09:52:50; the X-RCP interference was much stronger, especially relative to the weaker echo in that polarization.

Int       Times       Spectra   Noise  Bins   Carrier     Echo Bins    Notes

Bins

--- ----------------- ------- --------------- ------- ---------------- ------

A  09:07:00-09:40:00 001-198 104:160,425:916 588:605 165:300->275:420

AB 09:40:00-09:40:10   199   104:160.425:916 588:605     180:695       [1]

B  09:40:10-09:52:50 200-275 104:160,425:916 588:605 165:300->275:420

C  09:52:50-09:55:20 276-290     450:916     308:358 323:400->363:422  [2,3]

D  09:55:20-10:05:40 291-352     550:916     335:355 355:423->416:530  [3,6]

E  10:05:40-10:10:30 353-381     104:350     556:916 416:542->471:560  [4]

F  10:10:30-10:17:20 382-422     625:916     100:460 471:575->513:620  [5,6]

G  10:17:20-10:20:00 423-438     104:512     650:916 513:635->525:645  [4]

Notes: [1] FRO at 09:40; spectrum 199 has split echo

[2] strong interference at lower edge of passband

[3] echo power may be underestimated because interference is too close

[4] alias of interference moves in from high side of passband

[5] spectra 382-388 are contaminated by alias of interference

[6] alias of interference exits via low side of passband

The interference appeared in spectrum 276 (09:52:53) and persisted through the remainder of the experiment.  Spurs from the interference infringed on the X-RCP echo window over spectra 280-295 (09:53:30-09:56:10); the echo power may be underestimated by as much as 10 percent in attempts to exclude the interfering signal from the echo power calculation, but the same error should have affected the X-LCP echo power calculation in the same way and perhaps the ratio is still good.  An alias of the interference walked through the echo during spectra 381-388 (10:10:20-10:11:40), corrupting the X-RCP echo power calculations.  The interference was much weaker in X-LCP and its effect on X-LCP echo power calculation is negligible.

S-Band 10-s Average Data:  The S-LCP data were processed using a single set of parameters.  There were no S-RCP data.

Int       Times       Spectra   Noise  Bins   Carrier     Echo Bins    Notes

Bins

--- ----------------- ------- --------------- ------- ---------------- ------

A  09:07:00-10:20:00 001-438 104:240,760:916 243:249 456:551->650:755

Dick Simpson

Original: 2010-02-23

Added Post-Analysis Summary: 2010-03-10

Updated post-analysis summary: 2011-03-11

Corrected headings in Table 3: 2010-04-02

Minor edits to remove problematical characters: 2011-05-11