Mars Express Bistatic Radar Experiment

Operations Plan and Report

02-03 April 2005

Summary

=======

DSN Antenna:                 43

Pass:                        672

Orbit:                       1555

Orbit Start Time:            2005-04-03T00:52:18 (SCET)

HGA Pointing:                Inertial

Specular Condition:          2005-04-03T03:04:00 (ERT)

Target:                      (50.58S, 70.14W, 3386 km)

(southern highlands)

Incidence/Reflection Angle:  51.11 deg

Slant Range:                 7426 km

Slew Angle:                  77.67 deg

Doppler (carrier, fd):       -23808 Hz

Doppler (echo, fr):           22806 Hz

Doppler Difference (fdd):    -44614 Hz

Earth-Mars Distance:         2.37078E11 m

Data Acquisition

================

The experiment was supported by DSS 43 staff at the Canberra DSN complex.  The support team at JPL included Gene Goltz, Danny Kahan, John Klose, and Dick Simpson.  In  the NOPE area were Jose Valencia and Jesse Velasco.

The experiment began with pre-calibration activities starting on 02 April at 22:30; the pre-cal was completed more than an hour ahead of schedule.  The bistatic surface observations were collected in the interval 02:30-03:30, but echoes were seen during only about 20 minutes centered in that interval.  The post-calibration was completed and the RSR's stopped recording at 04:50 on 03 April.

Valencia had improved the calibration procedure and briefing message compared with the version which had been used in the previous experiment on 25-26 February.  There were only two minor problems, which he planned to address in future briefing messages.  At one point in the pre-calibration, there were two configuration changes rather than the customary one.  In the post-calibration, there was an Operator Directive to set the noise diode frequency explicitly to ON; this conflicted with the default value of 20 used by the station.

RSRs were configured as follows.

Table 1

--------------------------------------

RSR  Channel Mode  ATT FGAIN Operator

dB

----- ------- ---- ---- ----- --------

RSR1A  S-LCP   1-W auto   60    Kahan

RSR1B  X-LCP   1-W auto   60    Kahan

RSR2A  S-RCP   1-W auto   60    Goltz

RSR2B  X-RCP   1-W auto   60    Goltz

Subchannels were defined as follows:

Table 2

---------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          1 ksps   Used for seeking weak carrier signals

2          8 ksps

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording (able to capture both X-band

residual carrier and surface echo)

Predicts were provided by NSS and were for one-way operation.

Table 3 lists ADC RMS levels read from RSR displays during the experiment.  Times in hh:mm are in UTC from the RSSG wall clock, which was reset prior to the experiments.  During the 26-27 February experiment, the wall clock appeared to be about 2 minutes fast.  For more accurate times, see the next section of this report on Amplitude Calibration.  Acronyms/abbreviations are explained below Table 3; "steps" are explained in more detail in the accompanying "procedures" document.

Table 3

-----------------------------------------------------------------------------

TIME (ERT) RSR1A RSR1B RSR2A RSR2B                COMMENTS

2005-04-02 S-LCP X-LCP S-RCP X-RCP

RMS   RMS   RMS   RMS

---------- ----- ----- ----- -----  -----------------------------------------

22:30                              Voice net established (MEX MOC, MEX NOPE,

DSS 43, and RSSG)

22:53       28    28    28    28   DSS 43 reported it was configured per

Item 7b of the Briefing Message (BM)

22:56                              DSS 43 confirmed BM Item 7d Step-1

22:59       28    88    28    89   X-band to ambient load (AMB)

23:01       84    88    28    89   S-LCP to AMB

23:03       84    88    86    89   S-RCP to AMB

23:04                              Reset all RSR attenuators using AUTO

23:05       28    30    29    28   Begin recording, all RSR's (SCHAN=3)

23:09       28    30    29    28   DSS 43 reports AMB physical temperatures:

S1=21.00,

S2=22.19,

X1=21.06

23:10                   29    30   DSS 43 confirms ND set to 12.5K

23:15       28     7    29    11   X-band to sky (RCP ND still on)

23:20       28     7    29     7   X-RCP ND OFF

23:26       28    10    29     7   X-LCP ND ON

23:30       28    31    29    28   X-band to AMB

23:31                              DSS 43 reports AMB physical temperatures:

S1=21.12,

S2=22.06,

X1=20.88

23:34                              DSS 43 current weather conditions:

Humidity     32%

Temperature  23C

Sky          light cloud cover

23:35       28     7    29     7   X-band to sky; X-LCP ND OFF

23:43       28     7    30     7   S-RCP ND ON

23:46       27     7     9     7   S-RCP to sky (ND still ON)

23:51       28     7     7     7   S-RCP ND OFF

23:54                              DSS 43 reports they have reset the ND to

12.5K; it apparently defaulted to 0.25,

but we may not have seen it in the RSR

because it was disabled

23:57       29     7     7     7   S-LCP ND ON

00:02        9     7     7     7   S-LCP to sky

00:07        7     7     7     7   S-LCP ND OFF

00:12                              Stop all RSR recordings

-----------------------------------------------------------------------------

TIME (ERT) RSR1A RSR1B RSR2A RSR2B                COMMENTS

2005-04-03 S-LCP X-LCP S-RCP X-RCP

RMS   RMS   RMS   RMS

---------- ----- ----- ----- -----  -----------------------------------------

01:20                              Carrier visible; SNR=45 dB at -8800 Hz

S-RCP RSR 25 kHz bandwidth and SNR=44 dB

at -30 kHz in 100 kHz X-RCP window.

01:25                              Weak carriers visible in S-LCP and X-LCP

01:30        8     7     8     7   All RSRs begin recording subchannel 3;

X-LCP SNR=29 dB at -35 kHz, S-RCP SNR=44

at -9.5 kHz

01:36        8     7     8     7   S-RCP SNR=46 at -1253 Hz,

X-RCP SNR=69 at -2600 Hz (TLM OFF)

02:00        8     7     8     7   Insert FRO on all channels. S-LCP SNR=21

at -6327 Hz, X-LCP SNR=32 at -46 kHz,

S-RCP SNR=46 at -6332 Hz, X-RCP SNR=61

at -45387 Hz

02:13                              Slew in progress; S-LCP SNR=0,

X-LCP SNR=0,

S-RCP SNR=42,

X-RCP SNR=23

02:14                          7   DSS 43 reports LOS

02:15        8     8     8     7

02:16        8     8     8    12   X-RCP ND ON

02:19        8     8     9     7   X-RCP ND OFF; S-RCP ND ON

02:22                              DSS 43 reports they disconnected the

wrong receiver (for controlling noise

diode); they will go back to do it again

02:24        8    11     8     7   X-LCP ND ON; S-RCP ND OFF

02:28        9     8     8     8   S-LCP ND ON; X-LCP ND OFF

02:30                              Begin recording all RSRs (SCHAN=4)

02:31        8     8     8    12   X-RCP ND ON (accident)

02:33        8     8     8     8   X-RCP ND OFF

02:58                              Hints of X-LCP echo near -2000 Hz

03:00                              X-LCP echo moved to near 0 Hz

03:03                              X-LCP echo SNR=25 dB peaking at 1315 Hz;

intermittent X-RCP echo near 1500 Hz

03:05                              X-LCP echo SNR=27 at 2107 Hz;

X-RCP echo peak at 1714 Hz

03:08                              X-LCP echo peaks at 3222 Hz, weaker

03:10                              Echoes gone

03:30                              Stop RSR recordings (SCHAN=4)

03:35        9     9     9     9

03:36        9     9     9    12   X-RCP ND ON

03:39        9     9    10     9   S-RCP ND ON; X-RCP ND OFF

03:42        9    12     9     9   X-LCP ND ON; S-RCP ND OFF

03:45       10     9     9     9   S-LCP ND ON; X-LCP ND OFF

03:48        9     9     9     9   S-LCP ND OFF

03:50                              All FRO set to 0

03:58                              DSS 43 going to zenith

04:01        8     8     8     8

04:05       27    29    29    28   All channels to AMB; DSS 43 reports

S1=21.56,

S2=22.44,

X1=18.69

04:10       27    29    29    30   X-RCP ND ON

04:13       28    29    29    28   X-RCP ND OFF

04:15                              S-RCP ND did not come on correctly;

DSS 43 will toggle it.

04:16                              DSS 43 confirms S-RCP ND is ON and its

value is 12.5K

04:17       28    29    28    28

04:20       28    30    29    28   X-LCP ND ON, S-RCP ND OFF

04:23       28    29    29    28

04:25                              DSS 43 halted and re-enabled S-LCP ND

04:26       29    29    29    28   S-LCP ND ON

04:28                              DSS 43 recommends removing last line in

Step-04 of procedure (MFQ=ON)

04:31        9     7     7     7   All channels to sky (S-LCP ND still ON)

04:33        8    10     7     7   X-LCP ND ON, S-LCP ND OFF

04:36        7     7     9     7   S-RCP ND ON, X-LCP ND OFF

04:39        7     7     8    11   X-RCP ND ON, S-RCP ND OFF

04:42        7     7     7     7   All ND OFF

04:43                              DSS 43 reports "deep cloud cover, much

dust"

04:46                              All RSR's stop recording (subchannel 3)

04:50                              DSS 43 reports AMB physical temperatures:

S1=21.56,

S2=21.9,

X1=18.81

AMB = ambient load

CONSCAN = conical scan tracking

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

Pc = carrier power

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

SL = S-LCP

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP