From GHewitt@jftl.jpl.nasa.gov Wed Oct 26 15:34:01 2005

Return-Path: <GHewitt@jftl.jpl.nasa.gov>

Received: from jftl.jpl.nasa.gov (jftl.jpl.nasa.gov [128.149.207.22])

by magellan.stanford.edu (8.11.7p1+Sun/8.11.7) with SMTP id j9QMXxr29927

for <rsimpson@magellan.Stanford.EDU>; Wed, 26 Oct 2005 15:33:59 -0700 (PDT)

Received: from jftl.jpl.nasa.gov (Not Verified[128.149.207.21]) by jftl.jpl.nasa.gov with MailMarshal (v5,0,3,100)

id <B000321dd2>; Wed, 26 Oct 2005 15:35:04 -0700

Received: by jftl-mm.jpl.nasa.gov with Internet Mail Service (5.5.2657.72)

id <VNY9Q025>; Wed, 26 Oct 2005 15:33:46 -0700

Message-ID: <12373B687CF8324F843BE0CA103AA6F402EAFCA4@jftl-mm.jpl.nasa.gov>

From: "Hewitt, Greg" <GHewitt@jftl.jpl.nasa.gov>

To: DSN-NOCC <dsn-nocc@jjpl.jpl.nasa.gov>,

"Asmar, Sami W" <asmar@mail.jpl.nasa.gov>,

"Goltz, Gene L" <ggoltz@mail.jpl.nasa.gov>,

DSN-PREDICTS <DSN-PREDICTS@jjpl.jpl.nasa.gov>,

DSN-RMDCT <DSN-RMDCT@jjpl.jpl.nasa.gov>,

"'John.Reynolds@esa.int'" <John.Reynolds@esa.int>,

"Kahan, Daniel S" <kahan@mail.jpl.nasa.gov>,

DSNO&M-DSOT <DSNO&M-DSOT@jftl.jpl.nasa.gov>,

"'Dick Simpson 650-723-3525'" <rsimpson@magellan.stanford.edu>,

MDSCC-Operations <MDSCC-Operations@mdscc.nasa.gov>

Cc: "Holmes, Dwight P" <dholmes@mail.jpl.nasa.gov>,

"Thompson, Thomas W" <twt@ampersand.jpl.nasa.gov>,

"Angold, Nigel G" <nangold@mail.jpl.nasa.gov>,

DSN-MPSETD <DSN-MPSETD@jjpl.jpl.nasa.gov>,

"'Gary.Whitehead-esa.int'" <Gary.Whitehead@esa.int>,

"'Alan.Moorhouse@esa.int'" <Alan.Moorhouse@esa.int>,

"Wallick, Jack" <JWallick@jftl.jpl.nasa.gov>,

"Landon, Arthur J" <ALandon@jftl.jpl.nasa.gov>,

"Berman, Allen L" <alberman@mail.jpl.nasa.gov>,

"Hodder, James A" <jahodder@mail.jpl.nasa.gov>,

"Beyer, Patrick E" <pbeyer@mail.jpl.nasa.gov>,

"Williams, Raymond C" <rcw@mail.jpl.nasa.gov>,

"Medina, Margaret" <MMedina@jftl.jpl.nasa.gov>,

"Berner, Jeff B" <jbberner@mail.jpl.nasa.gov>,

"Guerrero, Anamaria P" <ana@mail.jpl.nasa.gov>,

"Buck, Robert D" <rbuck@mail.jpl.nasa.gov>,

"Klose, J C" <cklose@mail.jpl.nasa.gov>,

"Recce, David J" <drecce@mail.jpl.nasa.gov>,

"Marina, Miguel" <mmarina@mail.jpl.nasa.gov>,

"Hodgin, Wendy K" <whodgin@mail.jpl.nasa.gov>,

"Hodder, James A" <jahodder@mail.jpl.nasa.gov>,

"Eaton, Curtis A" <ceaton@mail.jpl.nasa.gov>,

"Davis, Esker B" <eskerb@mail.jpl.nasa.gov>,

"Kurtik, Susan C" <skurtik@mail.jpl.nasa.gov>,

"'Daniel S Kahan'" <Daniel.S.Kahan-121461@jpl.nasa.gov>

Subject: Briefing Message for MEX Bi-Static Radar support on DOY 303 with DSS-63

Date: Wed, 26 Oct 2005 15:33:32 -0700

MIME-Version: 1.0

X-Mailer: Internet Mail Service (5.5.2657.72)

Content-Type: multipart/alternative;

boundary="----_=_NextPart_001_01C5DA7D.47D344D0"

Content-Length: 273559

Status: RO

This message is in MIME format. Since your mail reader does not understand

this format, some or all of this message may not be legible.

------_=_NextPart_001_01C5DA7D.47D344D0

Content-Type: text/plain

Mars Express

Briefing Message

Level-3

DSS-63 Bi-Static Radar Experiment Support

Prepared by: G Hewitt / MEX NOPE / MPSETD

Origination Date: DOY 299 / 22:30 UTC

Revision: Original

DSS-63 DOY 303 / 2010 UTC

ROUTING: JFTL / JJPL / LRID

FROM: MPSETD G Hewitt

SUBJECT: DSS-63 Mars Express Bi-Static Radar Support

NOP: 871-049-041, REV.C

SCHEDULE: Refer to DSN 7-Day Schedule for actual support times.

LEVEL / TYPE: Level 3 Bi-Static Radar

DOY  Start  BOT  EOT  End  Facility  User      Activity       Pass

---  ----- ---- ---- ----  --------  ----  -----------------  ----

303   2010 2310 0210 0310   DSS-63    MEX  T/P BI STATIC R/S  0883

1. OVERVIEW:

Bi Static Radar (BSR) experiment employs the MEX spacecraft's transmitter and a DSN 70-m antenna to receive weak S-band and X-band dual polarized RF signals and Radio Science Receivers (RSRs) to simultaneously receive and record these four signals. At a predetermined time during the pass, the spacecraft slews toward Mars so that its transmitted S-band and X-band RCP signals illuminate the planet's surface. As these RCP signals bounce off the surface, part of the signals change polarization to Left Circular Polarization (LCP) effectively creating four signals; 1) S-band RCP, 2) S-band LCP, 3) X-band RCP and 4) X-band LCP.

DSN Mars Express Bi-Static Radar (BSR) calibration procedures are performed in three parts: 1) Pre-calibration, 2) Mini- calibration and 3) Post-calibration. Section-8 details the pre-calibration procedures, section-9 details mini-calibration procedures, and section-10 details post calibration procedures.

2. SUPPORT DOCUMENTATION:

a. Mars Express NOP 871-049-041, Rev. A

b. This briefing message

c. Bi-Static Radar SOE (see attachment) supersedes DSN SOE. Radio Science

shall provide start/stop times of BSR mini-pre-calibrations near

real-time.

3. SUPPORT REQUIREMENTS:

NOTE:  Do not use Time Stacked Directives.  We have experienced problems with certain time stacked directives slow to execute causing the next directive in the queue to be rejected.  Consequently, this leads to configuration errors and the need to repeat steps.

a. DOWNLINK SUPPORT ONLY

b. DTTS (DOWNLINK TRACKING AND TELEMETRY) RECEIVERS:

* One DTT shall be configured with table 7041HRX to support X-band, and

to control the 12.5k noise diode on/off at predetermined times during

pre-pass calibrations, real-time BSR activities and post calibrations

activities.

* A second DTT shall be configured with table 7041HRXS to support S-band

carrier only and to control the 12.5 k noise diode on/off at

predetermined times during pre-pass calibrations, real-time BSR

activities and post calibrations activities.

c. UPLINK:

* There are NO uplink requirements

d. COMMAND:

*  There are NO command requirements

e. RADIO SCIENCE RECEIVERS (RSR):

NOTE: For remote operations the FSPR MUST NOT be assigned to the DSS link.

The RSRs are controlled and configured remotely by the Radio Science group

located at JPL. The RSR operator will configure four radio science

receivers to simultaneously receive and record S-band and X-band RCP and

LCP polarized signals. The RSR equipment requires both S-band and X-band

1-way and 2-way downlink predicts. The actual RSR resources configured for

support will depend on availability.

* R1B IFS 63_S_RCP

* R2A IFS 63_S_LCP

* R1A IFS 63_X_RCP

* R2B IFS 63_X_LCP

4. NOCT:

Transmit X-band up/down, and X-up/S-band down predicts to the station

5. GCF:

Voice: DSS /AMMOS/MEX MOC/ RS

6. DSOT

There is NO SLE telemetry return link services required

7. SPACECRAFT CONFIGURATION:

The spacecraft shall be reconfigured for X-band and S-band downlink carrier only in accordance with the BSR SOE (see attachment).

8. PRE-CALIBRATION PROCEDURES AND CONFIGURATION

The times shown below in step-1 through step-18 are to illustrate event chronology and event duration:

a. Pre-calibration requires configuring the 70m-antenna microwave subsystem

so that each receiving downlink channel (S-RCP, S-LCP, X-RCP, X-LCP) can

be cycled in sequence through the four configurations listed below.  The

antenna must be pointed to zenith for pre-calibration.

1. Receiving channel into ambient load with noise diode off

2. Receiving channel into ambient load with noise diode on

3. Receiving channel into sky (zenith) with noise diode on

4. Receiving channel into sky (zenith) with noise diode off

NOTE: DTT01 is used for X-band and DTT02 is used for S-band, but any

available DTT resource can be used.

b. Link controller perform the procedures in step 1 and advise radio science

when completed; wait at this point until directed by radio science to

proceed to step 2.

Step-01  00:00:00  US63 MOD 102 A         Confirm dichroic reflector in place

US63 CNF XRA1O1        X-RCP (LNA-1) to Sky

US63 CNF XLA2O2        X-LCP (LNA-2) to Sky

US63 CNF SLLA2C2O2     S-LCP (LNA-2) low noise to sky

US63 CNF SRDA1C1O1     S-RCP (LNA-1) via diplexer to sky

AP SCAN OFF            CONSCAN Off

AP SRC TRK             Sub-reflector in Tracking Mode

c. NOPE use the connection log display to verify DSS-63's microwave switches

are configured in accordance with step-01

d. Radio science operator set each RSR attenuator using the AUTO feature.

After checking for proper signal levels (about -10.0 dB ADC amplitude on

each RSR), direct the link controller to proceed to step 2.

Step-02  00:04:00  US63 CNF XA1A2O2       LNA-2 to ambient load-1 (X-LCP)

US63 CNF XA1A1O1       LNA-1 to ambient load-1 (X-RCP)

Step-03  00:06:00  US63 CNF SA2A2C2O2     LNA-2 to ambient load-2 (S-LCP)

Step-04  00:08:00  US63 CNF SA1A1C1O1     LNA-1 to ambient load-1 (S-RCP)

e. *Link controller and radio science operator after completing steps 2

through 4, perform the following procedures, (1) through (5):

1. Link Controller report ambient load temperatures (S1, S2, and X1)

from the PRFREA display and report current weather conditions,

(temperature, humidity, and sky conditions) to the Radio Science

operator.

2. Radio Science operator set each RSR attenuator using AUTO feature

3. RSR operator run radio science recorders

4. RSR operator report to Link Controller when radio science recorders

are recording

5. Link controller execute the following procedures at 5 min intervals

and report the completion of each step to the RSR operator:

Step-05  00:10:00  DC01 DISC

DC01 CONN DSS63XO1     Configure DTT 01 to X-RCP

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

DC02 DISC

DC02 CONN DSS63SO1     Configure DTT 02 to S-RCP

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Step-06  00:15:00  DC01 SNT E             Enable X-RCP noise diode

Step-07  00:20:00  US63 CNF XRA1O1        X-RCP to sky

US63 CNF XLA2O2        X-LCP to sky

Step-08  00:25:00  DC01 SNT D             Disable X-RCP noise diode

DC01 DISC              Reconfigure DTT 01 for X-LCP

DC01 CONN DSS63XO2

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

Step-09  00:30:00  DC01 SNT E             Enable X-LCP noise diode

Confirm noise diode selection is 12.5

Step-10  00:35:00  US63 CNF XA1A1O1       X-RCP (LNA-1) to ambient load

US63 CNF XA1A2O2       X-LCP (LNA-2) to ambient load

00:36:00  Link controller report ambient load temp (S1, S2, X1) from

the PRFREA display to the RS operator.

Step-11  00:40:00  DC01 SNT D             Disable X-LCP noise diode

Step-12  00:45:00  US63 CNF XRA1O1        X-RCP (LNA-1) to sky

US63 CNF XLA2O2        X-LCP (LNA-2) to sky

Step-13  00:50:00  DC02 SNT E             Enable S-RCP noise diode

DC01 DISC              Reconfigure DTT 01 for X-RCP

DC01 CONN DSS63XO1

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

Step-14  00:55:00  US63 CNF SRDA1C1O1     S-RCP (LNA-1) via diplexer to sky

Step-15  01:00:00  DC02 SNT D             Disable S-RCP noise diode

DC02 DISC              Reconfigure DTT 02 for S-LCP

DC02 CONN DSS63SO2

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Confirm noise diode is 12.5

Step-16  01:05:00  DC02 SNT E             Enable S-LCP noise diode

Step-17  01:10:00  US63 CNF SLLA2C2O2     S-LCP (LNA-2) to sky

Step-18  01:15:00  DC02 SNT D             Disable S-LCP noise diode

DC02 DISC              Reconfigure DTT 02 for S-RCP

DC02 CONN DSS63SO1

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Link controller report ambient load physical temperatures

(S1,S2, and X1) from PRFREA display to the RS operator.

01:20:00  End of BSR noise measurement pre-cal procedure

9. MINI CALIBRATION PROCEDURES AND TIMELINE

a. Link controller, shortly after MEX begins its slew and before the BSR

surface observations begin, confirm DTT 01 and DTT 02 configurations.

b. Link controller confirm DTT 01 is configured for X-RCP; if not, perform the following operator directives:

1. DC01 DISC

2. DC01 CONN DSS63XO1

3. DC01 SET SNT NDS=12.5

4. DC01 SET SNT MFQ=ON

c. Link controller confirm DTT 02 is configured for S-RCP; if not, perform

the following operator directives:

1. DC02 DISC

2. DC02 CONN DSS63SO1

3. DC02 SET SNT NDS=12.5

4. DC02 SET SNT MFQ=ON

d. RSR operator ensure all radio science Recorders are recording.

e. Link controller, at direction from RSR operator, begin the BSR mini-noise

calibration procedures. The times shown are to illustrate event chronology

and event duration:

Step-01  00:00:00  DC01 SNT E             Enable X-RCP noise diode

Confirm noise diode value is 12.5

Step-02  00:03:00  DC01 SNT D             Disable X-RCP noise diode

DC02 SNT E             Enable S-RCP noise diode

DC01 DISC              Reconfigure DTT 01 for X-LCP

DC01 CONN DSS63XO2

US63 D XMAP            Verify configuration

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

Step-03  00:06:00  DC02 SNT D             Disable S-RCP noise diode

DC01 SNT E             Enable X-LCP noise diode

DC02 DISC              Reconfigure DTT 02 for S-LCP

DC02 CONN DSS63SO2

US63 D SMAP            Verify configuration

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Step-04  00:09:00  DC01 SNT D             Disable X-LCP noise diode

DC02 SNT E             Enable S-LCP noise diode

DC01 DISC              Reconfigure DTT 01 for X-RCP

DC01 CONN DSS63XO1

US63 D XMAP            Verify configuration

DC01 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Step-05  00:12:00  DC02 SNT D             Disable S-LCP noise diode

DC02 DISC              Reconfigure DTT 02 for S-RCP

DC02 CONN DSS63SO1

US63 D SMAP            Verify configuration

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

00:15:00  End of BSR Mini-Noise Cal.

Step-06            Link controller, repeat the BSR mini-noise calibration

procedures steps 01-05 after MEX has completed its

surface observations and before it returns to Earth point.

The start time will be provided by radio science.

10. POST CALIBRATION PROCEDURES AND TIMELINE:

Step-01  00:00:00  Link controller move antenna to zenith

US63 CNF SA1A1C1O1     S-RCP (LNA-1) to ambient load

US63 CNF SA2A2C2O2     S-LCP (LNA-2) to ambient load

US63 CNF XA1A1O1       X-RCP (LNA-1) to ambient load

US63 CNF XA1A2O2       X-LCP (LNA-2) to ambient load

DC01 DISC              Confirm DTT 01 for X-RCP

DC01 CONN DSS63XO1

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

DC02 DISC              Confirm DTT 02 for S-RCP

DC02 CONN DSS63SO1

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

a. Link controller advise the RSR operator when the antenna is at zenith and

the configurations listed above have been completed.

b. Link controller report physical temperatures of each ambient load (S1, S2,

and X1) from the downlink PRFREA display.

c. RSR operator run all radio science Recorders and record ambient loads for

3 min. At completion, advise the link controller to proceed with the

following steps:

Step-02  00:03:00  DC01 SNT E             Enable X-RCP noise diode

Step-03  00:06:00  DC01 SNT D             Disable X-RCP noise diode

DC02 SNT E             Enable S-RCP noise diode

DC01 DISC              Reconfigure DTT 01 for X-LCP

DC01 CONN DSS63XO2

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

Step-04  00:09:00  DC02 SNT D             Disable S-RCP noise diode

DC01 SNT E             Enable X-LCP noise diode

DC02 DISC              Reconfigure DTT 02 for S-LCP

DC02 CONN DSS63SO2

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Step-05  00:12:00  DC01 SNT D             Disable X-LCP noise Diode

DC02 SNT E             Enable S-LCP noise diode

Step-06  00:15:00  US63 CNF SRDA1C1O1     S-RCP (LNA-1) to sky

US63 CNF SLLA2C2O2     S-LCP (LNA-2) to sky

US63 CNF XRA1O1        X-RCP (LNA-1) to sky

US63 CNF XLA2O2        X-LCP (LNA-2) to sky

Step-07  00:18:00  DC02 SNT D             Disable S-LCP noise diode

DC01 SNT E             Enable X-LCP noise diode

DC02 DISC              Reconfigure DTT 02 for S-RCP

DC02 CONN DSS63SO1

DC02 SET SNT NDS=12.5

DC02 SET SNT MFQ=ON

Step-08  00:21:00  DC01 SNT D             Disable X-LCP noise diode

DC02 SNT E             Enable S-RCP noise diode

DC01 DISC              Reconfigure DTT 01 for X-RCP

DC01 CONN DSS63XO1

DC01 SET SNT NDS=12.5

DC01 SET SNT MFQ=ON

Step-09  00:24:00  DC02 SNT D             Disable S-RCP noise diode

DC01 SNT E             Enable X-RCP noise diode

Step-10  00:27:00  DC01 SNT D             Disable X-RCP noise diode

00:30:00  End

d. Link Controller report physical temperatures of each ambient load (S1, S2, and X1) from the downlink PRFREA display and report the current weather (temperature, humidity, and sky conditions) to radio science.

e. Radio Science operator stop RSRs.

f. End of BSR noise post-calibration procedures.

g. Link Controller proceed with normal tear-down procedures.

h. Re-initialization of the DTTs is recommended.

MPSETD POINTS OF CONTACT: DSN-MPSETD@jjpl.jpl.nasa.gov

<mailto:DSN-MPSETD@jjpl.jpl.nasa.gov>

MPSETD              OFFICE     OPS WORK STATION

Jose Valencia (LEAD)  (626) 305-6308   (626) 305-6370

(626) 305-6368

Jesse Velasco (NOPE)  (626) 305-6315

Romy Paredes (NOPE)   (626) 305-6309

Greg Hewitt (NOPE     (626) 305-6292

RADIO SCIENCE WORK STATION             (818) 393-0666

Regards,

Gregory W. Hewitt

(626) 305-6292 (Office)

(626) 491-0017 (Pager)

(626) 305-6389 (Fax)

ghewitt@jftl.jpl.nasa.gov