From JVelasco@jftl.jpl.nasa.gov Fri Oct 17 11:38:46 2003

Received: from jftl-mm.jpl.nasa.gov (jftl.jpl.nasa.gov [128.149.117.25])

by magellan.stanford.edu (8.11.6/8.11.6) with ESMTP id h9HIcjx05613

for <rsimpson@magellan.stanford.edu>; Fri, 17 Oct 2003 11:38:45 -0700 (PDT)

Received: from jftl.jpl.nasa.gov (not verified[128.149.117.23]) by jftl-mm.jpl.nasa.gov with MailMarshal (4,2,5,0)

id <B00011dec5>; Fri, 17 Oct 2003 11:42:13 -0700

Received: by jftl-mm.jpl.nasa.gov with Internet Mail Service (5.5.2656.59)

id <TYCWN6Y0>; Fri, 17 Oct 2003 11:38:13 -0700

Message-ID: <12373B687CF8324F843BE0CA103AA6F4019510E4@jftl-mm.jpl.nasa.gov>

From: "Velasco, Jesse" <JVelasco@jftl.jpl.nasa.gov>

To: "Velasco, Jesse" <JVelasco@jftl.jpl.nasa.gov>,

"Asmar, Sami W" <asmar@mailhost4.jpl.nasa.gov>,

"Anabtawi, Aseel" <Aseel@barugon.jpl.nasa.gov>,

"Abbate, Salvatore F" <SAbbate@jftl.jpl.nasa.gov>,

"Angold, Nigel G" <nangold@mailhost4.jpl.nasa.gov>,

DSN-MPSETD <DSN-MPSETD@jjpl.jpl.nasa.gov>,

"'Dick Simpson 723-3525'" <rsimpson@magellan.stanford.edu>,

"Holmes, Dwight P" <dholmes@mailhost4.jpl.nasa.gov>,

CDSCC-Operations <CDSCC-Operations@anbe.cdscc.nasa.gov>,

"GDSCC Operations," <GDSCCOperations@jgld.gdscc.nasa.gov>,

CDSCC <CDSCC@anbe.cdscc.nasa.gov>, DSN-NOCC <dsn-nocc@jjpl.jpl.nasa.gov>

Cc: "'Marco Lanucara (E-mail)'" <Marco.Lanucara@esa.int>,

"Hewett, Susan" <SHewett@jftl.jpl.nasa.gov>,

"Nguyen, Peter H" <PNguyen@jftl.jpl.nasa.gov>,

DSN-PREDICTS <DSN-PREDICTS@jjpl.jpl.nasa.gov>,

"Thompson, Thomas W" <twt@ampersand.jpl.nasa.gov>

Subject: Corrected copy Briefing Message for Mars Express Radio Science Test Supports DOY 291

Date: Fri, 17 Oct 2003 11:38:08 -0700

MIME-Version: 1.0

X-Mailer: Internet Mail Service (5.5.2656.59)

Content-Type: text/plain;

charset="iso-8859-1"

Content-Length: 9001

ROUTING: 	JFTL / JJPL / JOCC / ANBE  /  JGTS

FROM:      	MPSET(D)/  J. Velasco

SUBJECT:	Mars Express (MEX) Radio Science Test Supports

SCHEDULE:	Refer to DSN 7-Day Schedule for actual support times.

291 0640 0810 1630 1700  DSS-43  MEX    R/S BI-STATIC    0139 N621

291 2245 0015 0915 0945  DSS-24  MEX    R/S OCC          0139 N70T

1. PURPOSE:

To exercise spacecraft and station configurations for activities such as;

Bistatic Radar measurements, and occultations.

2. OBJECTIVE:

a. Demonstrate that the DSN can support the various configurations required

for successful Bistatic Radar measurement activities.

b. Exercise spacecraft configuration to be used for planned radio science

experiments.

3. SUPPORT DOCUMENTATION

a.  NOP 871-049-041

b.  This briefing message

c.  Sequence of Events

4. SUPPORT REQUIREMENTS:

General

a. The Radio Science Systems Group will remotely control the Radio Science

Receiver(RSR)for all scheduled supports.

b. X-Band and S-Band ranging will be performed.

c. The spacecraft will be transmitting XRCP and/or SRCP.

d. Nominal predictions for X/X, S/S X/S X/X are to be generated.

e. X-Band Telemetry will be prime for all supports.

f. Enable prime data stream to line as required.

g. The NOPE will be on duty in the ROSA for these activities.

h. All stations are required to acquire S-Band carrier lock only. S-Band

Telemetry will not be present on the downlink.

i. Station is required to configure for support in accordance with Table-2.

j. Configure both receiver(s) with the configuration table listed below in

table-2.

Bistatic Radar Measurement Test Support Requirements. (DSS-43 Only)

a. 70-Meter antenna support is required.

b. Closed-loop and Open-Loop receivers are required.

c. For X-Band, the fixed channel HEMT are configured LCP/RCP at all times.

d. For S-Band, the HEMT in MOD-III will be configured for low noise path.

e. The cone TWM will be configured for the diplex path.

f. Record Noise Diode on and off times and report to Radio Science Group.

g. Configure Receivers for (1) XRCP (2) SRCP Closed-Loop during real-time

support.

h. Perform Y-Factor measurements for all receiver channels and perform noise

diode calibrations during the Setup periods. During set up perform

Y-factor measurement with the two receivers configured for XLCP and SLCP.

Then perform the Y-factor measurement again with the receivers configured

for XRCP and SLCP. The receivers will be configured for XRCP and SRCP

during real-time supports. No noise cal for tear down.

i. Configure receiver with the configuration table listed below in table-2.

Configure-one receiver for XRCP and the other receiver for SRCP.

j. Turn on/off all the noise diodes at the same time and switch in/out the

ambient loads simultaneously whenever the the RSR is running. Provide a

listing of the on/off/in/out times after each set of measurements is

completed.

k. Provide a physical temperature of the ambient loads.

RADIOMETRIC

Table-1. DSS-43 Microwave Configuration

S-Band               S-Band LNA

Low Noise Path       HEMT

Diplex Mode          TWM

X-Band               X-Band LNA

XTR Cone             HEMT

XTR Cone             HEMT

Table-2. Spacecraft/Receiver Configuration

DOY    DSS           BAND             RCV CONFIG TABLE

---    ---   ---------------------    ----------------

291	  43   X-Band Up/X-Band Down      7041hrx.cfg

S-Band Down                7041hrxs.cfg

291     24   X-Band Up/X-Band Down      3441hrx.cfg

S-Band Down                3441hrsx.cfg

Table-3.  Ranging Configuration

DOY    DSS    RANGING CONFIG         MOD INDEX (RAD)

X-BAND      S-BAND

---    ---    ------------------   -------------------

291     43    X-Up/Down + S-Down   (X = 0.2) (S= 0.1)

291     24    X-Up/Down + S-Down   (X = 0.2) (S = 0.1)

TELEMETRY

a. The telemetry system should be configured in accordance with (IAW)

section 7 of the MEX NOP.

b. The telemetry data rate will be 209715.2sps.

c. The telemetry Mod index will be 1.25 rad.

d. Enable the out put from the telemetry channel that is configured for

the D/L path with the polarization  X-Band RCP.

e. X-Band will be prime for all supports.

f. There is no telemetry modulation on the S-band downlink. (Carrier Only)

COMMAND

a. The command system should be configured IAW section 8 of the MEX NOP.

b. The command data rate will be 2000bps.

c. The command index : S-Band =0.8 rad, X-Band=1.0 rad.

MONITOR & CONTROL

N/A

RADIO SCIENCE

Noise Diode Calibration Procedure.

Setup:

1) Antenna at zenith

2) Verify RSR recording (Remotely controlled by RSR Team)

3) Antenna on Cold sky (5 Min)

4) Antenna/UWV cold sky and 12K Noise Diode ( 5 Min ).

5) Antenna/UWV Ambient Load  (5 Min).

6) Perform Y-factor measurements for all channels. Perform Y-Factor

measurements for all receiver channels and perform noise diode

calibrations during the Setup. During set up perform Y-factor

measurement with the two receivers configured for XLCP and SLCP.

Then perform the Y-factor measurement again with the receivers

configured for XRCP and SRCP.

THE Y-FACTOR MEASUREMENTS NEED TO BE PERFORMED TO ACHIEVE THE

OBJECTIVES OF THE R/S TEST.

Experiment:

The NMC Link controller will need to manually turn the 12K Noise Diode

on and off during the support on DOY 291 at the following times:

START          STOP

------------   ------------   --------------------------------

291/10:00:00   291/10:05:00   Turn on X-RCP 12 deg noise diode

291/10:00:00   291/10:05:00   Turn on S-RCP 12 deg noise diode

291/10:00:00   291/10:05:00   Turn on X-LCP 12 deg noise diode

291/10:00:00   291/10:05:00   Turn on S-LCP 12 deg noise diode

291/11:00:00   291/11:05:00   Turn on X-RCP 12 deg noise diode

291/11:00:00   291/11:05:00   Turn on S-RCP 12 deg noise diode

291/11:00:00   291/11:05:00   Turn on X-LCP 12 deg noise diode

291/11:00:00   291/11:05:00   Turn on S-LCP 12 deg noise diode

291/12:00:00   291/12:05:00   Turn on X-RCP 12 deg noise diode

291/12:00:00   291/12:05:00   Turn on S-RCP 12 deg noise diode

291/12:00:00   291/12:05:00   Turn on X-LCP 12 deg noise diode

291/12:00:00   291/12:05:00   Turn on S-LCP 12 deg noise diode

Teardown:

1) Antenna at zenith

2) Antenna on Cold sky (2 Min)

3) Antenna/UWV cold sky and 12K Noise Diode ( 2 Min ).

4) Antenna/UWV Ambient Load  (2Min).

5) Perform y-factor measurements for all channels. XRCP/XLCP and

SRCP/SLCP

6) RSR recording stopped by RSR Team .

Note: 1) Record of Ambient Load Temp Date .

2) Record of 12K Noise Diode on / off times.

3) Record of Ambient Load switching times .

4) Do not perform noise cal for tear down.

GCF

a. Voice: DSS / JPL / ROSA MOPS/AMMOS/MEMOC

b. Data:  DSS / JPL /AMMOS/ESA/MEMOC

NOCT

Prior to each scheduled  support, NOCT personnel are requested to transmit

the following  predictions to supporting station as depicted below.

Note: reference table-2

DOY    DSS    PREDICTS       SUPPORT CONFIGURATION    PASS NO.

---    ---    ------------   ---------------------    --------

291     43    MEX_031010_X        x-up x-down           0139

MEX_031010XS        x-up s-down

291     24    MEX_031010_X        x-up x-down           0139

MEX_031010XS        x-up s-down

5. DELIVERABLES:

a. The Radio Science Systems Group will  record data at the RSR beginning

at setup through the end of teardown activities.

6. MISCELLANEOUS:

N/A

7. SEQUENCE OF EVENTS:

8. POINTS OF CONTACT:

DSN-MPSETD@jjpl.jpl.nasa.gov):

PSD Team  Office  Pager

Rick nevarez (MSE)       626-584-4440

Jose Valencia(Lead NOPE) 626-584-4554

Jesse Velasco(NOPE)      626-584-4448

Khanh Ly (NOPE)          626-584-4690

Romy Paredes(NOPE)       626-584-4635

Remote Operations Support Area:   626-584-4412

626-584-4411

Radio Science Operations Room:    818-393-0666

Regards,

Jesse Velasco