Mars Express Bistatic Radar Experiment

Operations Plan and Report

30 May 2006

Summary

=======

DSN Antenna:                                                   14

Pass:                                                        1094

Orbit:                                                       3062

Orbit Start Time:                             2006-05-29T22:19:27

HGA Pointing:                                            Specular

Start          End

--------      --------

Specular Condition (ERT):            03:57:00      04:48:20

Target Latitude (deg N):               -12.77          3.33

Longitude (deg E):             -129.40       -146.04

Rp (km):                                3394.

Incidence/Reflection Angle (deg):       55.03         51.07

Slant Range (km):                       9496.        10969.

Slew Angle (deg):                       69.94         77.87

Doppler (carrier, fd; Hz):              7777.         9462.

Doppler (echo, fr; Hz):                -16925         -3309

Doppler Difference (fdd; Hz):           24702         12770

Earth-Mars Distance (m):                     3.213E+11

Experiment Set Up

=================

This experiment was conducted using Goldstone's DSS 14.  Gene Goltz, Danny Kahan, and Dick Simpson were in the Radio Science Support Area at JPL; Jesse Velasco was in the NOPE area, at least at the beginning.  For the most part, Kahan operated the RSR's and Goltz handled communications.

There was a delay in the pre-cal as DSS 14 waited for some resources to become available.

Performance Problems and Notes

==============================

The X-LCP noise diode appeared to come on shortly after the X-RCP noise diode was turned off (both within Step 8 of the pre-cal).  There was no change in levels at Step 9, when it should have been enabled.  But it did go off at Step 11, as per the procedure.

S-LCP ADC amplitude levels at the end of the pre-cal were not stable, ranging from -18.3 to -20.6 dB.  The same thing happened in the second half of the post-cal (levels -16.9 to -18.5 dB).

Predicts ended at 05:50; this generates an RSR warning message, but does not affect operation.

Steps 5-6 were combined in the post-cal; but the station recognized this, backed up, and corrected the error (at a small loss in time).

The NMC log does not contain  DSS 14 azimuth and elevation readings after about 03:09.  Danny Kahan was able to generate these independently.

Data Acquisition

================

RSRs were configured as in Table 1:

Table 1

----------------------------------------------------

RSR  Channel Mode  ATT FGAIN        Operator

dB

----- ------- ---- ---- ----- ----------------------

RSR3A  S-LCP   1-W auto   60    Kahan

RSR3B  X-LCP   1-W auto   60    Kahan

RSR2A  S-RCP   1-W auto   60    Kahan

RSR2B  X-RCP   1-W auto   60    Kahan

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   backup (not recorded)

2          8 ksps   backup (not recorded)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  "Steps" are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-LCP  X-LCP  S-RCP  X-RCP  Notes / Comments

-------- ----- --------- -----  -----  -----  -----  ------------------------

2006/150

--------

Pre-Cal  01:36     1

01:36  att auto  -9.5   -9.8  -10.2   -9.9  All to sky

01:39     2     -10.0   -0.1  -10.0   -0.0  X-Band to AMB

01:40     3      -0.9   -0.1  -10.1    0.0  S-LCP to AMB

01:41     4      -0.9   -0.2   -0.4   -0.1  S-RCP to AMB

AMB physical temps:

S1=17.88C

S2=24.12C

X1=16.06C

att auto  21.5   23.5   15.5   23.0  Reset ATT (prop to dB)

-10.0   -9.9  -10.7   -9.7  Weather confitions:

T=76F,

H=12 percent

sky=clear and calm

01:45  rec 3 e                              Begin 25 kHz recording

01:47     5      -9.9   -9.8  -10.0   -9.6  Configure DTT's

01:50     6     -10.0   -9.9  -10.0   -9.5  XR ND ON

01:55     7     -10.0  -21.9  -10.1  -20.1  X-Band to sky

02:00     8     -10.0  -19.7  -10.0  -22.6  XR ND OFF

DSS14 confirms XL ND off

02:05     9     -10.0  -19.7  -10.1  -22.4  XL ND ON (no change)

DSS14 confirms 12.5K ND

02:10    10     -10.0   -9.6  -10.0   -9.9  X-Band to AMB

AMB physical temps:

S1=17.69C

S2=23.88C

X1=16.3C

02:15    11     -10.0   -9.7  -10.1   -9.8  XL ND OFF

02:20    12     -10.0  -21.8  -10.1  -22.5  X-Band to sky

02:25    13     -10.0  -21.9   -9.7  -22.5  SR ND ON

02:30    14      -9.9  -21.9  -19.2  -22.4  SR to sky

02:35    15     -10.0  -21.9  -21.8  -22.5  SR ND OFF

DSS14 confirms 12.5K ND

02:40    16      -9.8  -21.8  -21.7  -22.4  SL ND ON

02:45    17     -18.3  -21.9  -21.9  -22.4  SL to sky

02:50    18     -19.3  -21.8  -21.7  -22.5  SL ND OFF

AMB physical temps:

S1=18.56C

S2=23.88C

X1=16.31C

02:55   end                                 Move antenna to point

BOT/AOS  03:04           -20.4  -21.4  -21.5  -21.8  S-Band AOS (ADB amp, dB)

03:05           -20.6  -21.4  -21.4  -21.6  X-Band AOS

03:08            N/A    29.7   44.3   58.8  C/N (dB/Hz)

N/A   -2093  -1116  -2098  Carrier offset (Hz)

DSS14 carrier lock S+X

03:19            15.2   35.6   43.6   65.9  C/N (dB/Hz)

-1188  -2361  -1190  -2368  Carrier offset (Hz)

SLEW#1   03:29            11.9   33.3   43.2   55.9  C/N (dB/Hz)

03:30             3.8   32.6   41.0   46.2  C/N (dB/Hz)

03:35                                       DSS 14 S-Band LOS

FRO     -4200 -21000  -4200 -21000  RSR FRO (SCHAN 3,4; Hz)

-20.1  -21.2  -21.4  -20.8  ADC amp (dB)

MiniCal1 03:37     1     -20.3  -21.1  -21.3  -19.0  XR ND ON

DSS 14 X-Band LOS

03:40     2     -20.4  -21.2  -18.9  -20.8  XR ND OFF; SR ND ON

03:43     3     -20.5  -19.3  -21.3  -21.2  SR ND OFF; XL ND ON

03:46     4     -18.8  -21.1  -21.4  -20.7  XL ND OFF; SL ND ON

03:49     5     -20.5  -21.0  -21.3  -20.7  SL ND OFF

03:52   end

BSR      03:56 rec 4 e                               Begin 100 kHz recording

03:57                                       Begin spec point track

04:00           -20.4  -21.0  -21.2  -20.7  ADC ampl (dB)

04:18           -20.3  -20.9  -21.1  -20.6  ADC ampl (dB)

no    yes    yes    yes   carrier detect (SCHAN 2)

04:24-04:27                                 Poss XL echo near center

04:47-04:54     -20.2  -20.4  -20.8  -20.2  Poss XL echo near +4500

04:58           -19.8  -20.1  -20.7  -20.1  Begin slew back to Earth

04:59 rec 4 d                               End 100 kHz recording

MiniCal2 05:00     1     -19.9  -20.3  -20.6  -18.5  XR ND ON

05:03     2     -19.9  -20.0  -18.6  -20.0  XR ND OFF; SR ND ON

05:06     3     -19.8  -18.4  -20.6  -20.0  SR ND OFF; XL ND ON

05:09     4     -18.5  -19.9  -20.4  -19.8  XL ND OFF; SL ND ON

05:12     5     -19.7  -19.8  -20.4  -19.9  SL ND OFF

05:15   end     -19.6  -19.9  -20.3  -20.5  Begin moving to zenith

Post-Cal 05:20   FRO       0      0      0      0    All FRO=0

05:25           -18.7  -21.9  -21.7  -22.4  DSS14 at zenith

05:27     1     -10.0   -9.7  -10.0   -9.7  All to AMB

AMB physical temps

S1=19.31

S2=22.62

X1=18.44

05:30     2     -10.1   -9.5  -10.0   -9.4  XR ND ON

05:33     3     -10.0   -9.7   -9.8   -9.8  XR ND OFF; SR ND ON

05:36     4     -10.1   -9.5  -10.1   -9.7  SR ND OFF; XL ND ON

05:39    5,6    -18.2  -21.9  -21.8  -22.4  XL ND OFF; SL ND ON;

All to sky (incorrect)

05:44     5      -9.7   -9.6  -10.0   -9.8  All to AMB

05:46     6     -17.1  -21.9  -21.7  -22.4  All to sky

05:49     7     -18.5  -19.5  -21.7  -22.5  SL ND OFF; XL ND ON

05:52     8     -16.9  -21.9  -19.3  -22.4  XL ND OFF; SR ND ON

05:55     9     -19.1  -21.8  -21.9  -20.0  SR ND OFF; XR ND ON

05:58    10     -19.5  -21.9  -21.9  -22.4  XR ND OFF

AMB physical temps:

S1=18.94C

S2=22.38C

X1=18.25C

Weather conditions:

T=66F

H=12 percent

sky=clear

EOA      06:02 rec 3 d   -19.6  -21.9  -21.8  -22.5  Stop 25 kHz recording

AMB = ambient load

BOT = Beginning of Track

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Dick Simpson

Original: 2006-05-30

NMC problem noted: 2006-07-19