Mars Express Bistatic Radar Experiment

Operations Plan and Report

24 June 2006

Summary

=======

DSN Antenna:                                                     43

Pass:                                                          1120

Orbit:                                                         3152

Orbit Start Time:

HGA Pointing:                                              Specular

Start   Phoenix B      End

--------  ----------  --------

Specular Condition (ERT):            05:49:50   06:21:00   06:51:00

Target Latitude (deg N):                49.58      68.18      -8.44

Longitude (deg E):               82.75     131.12     183.13

Rp (km):                         3394.      3394.      3394.

Incidence/Reflection Angle (deg):       51.86      49.48      67.47

Slant Range (km):                       5143.      1995.       994.

Slew Angle (deg):                       76.28      81.04      45.07

Doppler (carrier, fd; Hz):              20558       5231     -44901

Doppler (echo, fr; Hz):                 45381      47068     -52044

Doppler Difference (fdd; Hz):          -24824     -41837       7143

Earth-Mars Distance (m):            3.461E+11  3.461E+11  3.461E+11

Experiment Set Up

=================

This experiment was conducted using Canberra's DSS 43.  Gene Goltz, Danny Kahan, and Dick Simpson were in the Radio Science Support Area at JPL; Jose Valencia was in the NOPE area.  For the most part, Kahan operated the RSR's and Goltz handled communications.

Performance Problems and Notes

==============================

S-LCP and S-RCP inputs to the RSR's were swapped.  This has been "standard" at DSS 43 for several months.  The problem will be investigated during regular maintenance next Tuesday.

The S-RCP noise diode was turned on very early in the pre-cal.  As a result, the only useful data are in the AMB+ND configuration.  This makes the Top value from the pre-cal worthless and compromises the pre-cal estimate of the S-RCP noise diode power.

At the end of the pre-cal (Step 13, executed at 03:21:05) the X-RCP noise diode was incorrectly set to MFQ=20 rather than MFQ=ON.  This cut its power roughly in half during MiniCal #1, leading to an incorrect estimation of the X-RCP system temperature immediately before the BSR.

There were convincing X-RCP and X-LCP echoes 3 minutes before the BSR interval officially began at 05:50 (>20 dB/Hz spread over 2 kHz).  The X-RCP echo faded and didn't return in any convincing fashion until about 06:30.  The X-LCP echo was broad (2-5 kHz), fading in and out but generally present throughout.  At 06:40 the first of half a dozen very strong echoes were observed in both X-RCP and X-LCP; these reached strengths >30 dB/Hz and lasted 30-60 seconds each.  They were still in progress when the spacecraft transmitters were turned off at 6:51.  Presumably there are some very smooth surfaces between (30N, 187E) and (8S, 183E).  There were no real-time signs of S-Band echoes at any time during the experiment.

Data Acquisition

================

RSRs were configured as in Table 1.  Note that the S-Band polarizations are swapped compared with the nominal configuration; but this has been the case for several months at DSS 43.

Table 1

----------------------------------------------------

RSR  Channel Mode  ATT FGAIN        Operator

dB

----- ------- ---- ---- ----- ----------------------

RSR1A  S-RCP   1-W auto   60    Kahan

RSR1B  X-LCP   1-W auto   60    Kahan

RSR2A  S-LCP   1-W auto   60    Kahan

RSR2B  X-RCP   1-W auto   60    Kahan

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   backup (not recorded)

2          8 ksps   backup (not recorded)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  "Steps" are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-RCP  X-LCP  S-LCP  X-RCP  Notes / Comments

RSR1A  RSR1B  RSR2A  RSR2B

-------- ----- --------- -----  -----  -----  -----  ------------------------

2006/175

--------

Pre-Cal  02:32     1     -10.1   -9.8   -9.8   -9.7  All to sky (dB)

2.0   12.0    9.0   12.5  ATT settings

02:34     2     -10.1   -0.0   -9.8    0.1  X-Band to AMB

02:35     3     -10.2   -0.0   -0.4    0.0  S-LCP to AMB

02:36     4      -0.4   -0.0   -0.3    0.0  S-RCP to AMB

02:37            -9.8  -10.0   -9.8   -9.8  After ATT AUTO reset

13.5   25.5   20.5   25.0  ATT settings

02:38                                       Begin 25 kHz recording

AMB load physical temps:

S1=20.56C

S2=20.56C

X1=20.0C

Weather conditions:

T=9C

H=65.7 percent

sky=clear

02:39     5      -9.7   -9.9   -9.8   -9.8  Configure DTT01, DTT02

02:45     6      -9.6  -10.0   -9.8   -9.0  XR ND ON

02:50     7      -9.8  -22.2   -9.8  -15.7  X-Band to sky

02:55     8      -9.7  -22.2  -10.0  -22.5  XR ND OFF

03:00     9      -9.7  -17.0   -9.9  -22.3  XL ND ON

Confirmed using 12.5K ND

03:05    10      -9.8   -9.4   -9.9   -9.8  X-Band to AMB

AMB load physical temps:

S1=20.75

S2=20.62

X1=19.69

03:10    11      -9.7  -10.0   -9.9   -9.9  XL ND OFF

03:15    12      -9.8  -22.2   -9.8  -22.2  X-Band to sky

03:20    13      -9.7  -22.2   -9.8  -22.2  S-RCP ND ON

03:21                                       X-RCP ND set to MFQ=20

03:25    14     -19.5  -22.2   -9.9  -22.2  S-RCP to sky

03:30    15     -21.8  -22.2   -9.8  -22.2  SR ND OFF

Confirmed using 12.5K ND

03:35    16     -21.9  -22.3   -9.6  -22.1  SL ND ON

03:40    17     -21.9  -22.2  -18.6  -22.2  S-LCP to sky

03:45    18     -21.9  -22.2  -21.3  -22.2  SL ND OFF

03:50   end                                 Stop 25 kHz recording

AMB load physical temps:

S1=21.00

S2=20.81

X1=19.44

BOT/AOS  03:57                                 56.2  Carrier to noise (dB/Hz)

-200  3-W carrier offset (Hz)

04:20                                       DSS43 X-RCP in lock

57.9  Carrier to noise (dB/Hz)

1881  3-W carrier offset (Hz)

04:36                                       DSS43 S-RCP in lock

43.2   22.9    --    58.0  Carrier to noise (dB/Hz)

275   3024    --    3040  3-W carrier offset (Hz)

04:45                                       Carrier now 1-way

42.9   23.4    --    58.1  Carrier to noise (dB/Hz)

-1236  -2534    --   -2542  Carrier offset (Hz)

04:50                                       Begin 25 kHz recording

04:51           -21.6  -21.8  -20.8  -20.7  ADC amplitude

42.9   30.5    --    65.3  CNR (dB/Hz) (TLM OFF)

-1272  -2676    --   -2680  Carrier offset (Hz)

05:07           -21.6  -21.7  -20.9  -20.7  ADC amplitude (dB)

42.9   34.2    --    65.4  Carrier to noise (dB/Hz)

-1352  -2957    --   -2955  Carrier offset (Hz)

SLEW1    05:20                                       Begin Slew #1

-21.6  -21.7  -20.7  -20.8  ADC amplitude (dB)

42.7   23.4    --    58.2  Carrier to noise (dB/Hz)

-1387  -3086    --   -3088  Carrier offset (Hz)

05:25   FRO      3600  25000   3600  25000  SCHAN 3 FRO entered (Hz)

FRO         0  18000      0  18000  SCHAN 4 FRO entered (Hz)

MINICAL1 05:30     1     -21.5  -21.8  -20.9  -17.2  XR ND ON

05:33     2     -19.1  -21.7  -20.7  -20.8  XR ND OFF; SR ND ON

05:36     3     -21.5  -17.0  -20.7  -20.9  SR ND OFF; XL ND ON

05:39     4     -21.5  -21.7  -18.4  -20.9  XL ND OFF; SL ND ON

05:42     5     -21.5  -21.7  -20.6  -20.8  SL ND OFF

05:45   end

BSR      05:47                                       XL, XR echo at -5000 Hz

05:50                                       Begin 100 kHz recordings

06:00   FRO            31000         31000  SCHAN 3 FRO change (Hz)

21.7          19.0  Echo to noise (dB/Hz)

-3918                Echo center offset (Hz)

06:10   FRO            37000         37000  SCHAN 3 FRO change (Hz)

20.0          14.0  Echo to noise (dB/Hz)

-5500                Echo center offset (Hz)

06:33   FRO            25000         25000  SCHAN 3 FRO change (Hz)

06:37   FRO            14000         14000  SCHAN 3 FRO change (Hz)

06:40                                       1ST of several HUGE X-BD

ECHOES (>30 dB/Hz)

06:41   FRO             3000          3000  SCHAN 3 FRO change (Hz)

06:42:45                                    Another strong echo

06:45   FRO            -7000         -7000  SCHAN 3 FRO change (Hz)

06:51   end                                 End BSR; S-Tx, X-Tx OFF

Stop 100 kHz recordings

MINICAL2 06:52     1     -21.3  -21.5  -20.7  -15.3  XR ND ON

06:55     2     -19.2  -21.5  -20.8  -20.5  XR ND OFF; SR ND ON

06:58     3     -21.2  -16.9  -20.7  -20.5  SR ND OFF; XL ND ON

07:01     4     -21.2  -21.4  -18.2  -20.5  XL ND OFF; SL ND ON

07:04     5     -21.3  -21.6  -20.6  -20.8  SL ND OFF

FRO        0      0      0      0   All FRO = 0

EOT      07:07   end                                 End track

DSS43 to zenith

POSTCAL  07:13     1                                 At zenith; all to AMB

AMB load physical temps:

S1=20.12

S2=20.25

X1=19.69

07:16     2     -10.0  -10.0   -9.8   -9.4  XR ND ON

07:19     3      -9.8  -10.0   -9.8   -9.7  XR ND OFF; SR ND ON

07:22     4     -10.2   -9.4   -9.9   -9.8  SR ND OFF; XL ND ON

07:25     5     -10.1  -10.0   -9.7   -9.6  XL ND OFF; SL ND ON

07:28     6     -22.1  -22.3  -18.5  -22.4  All to sky

07:31     7     -22.0  -17.1  -21.3  -22.3  SL ND OFF; XL ND ON

07:34     8     -19.7  -22.3  -21.3  -22.2  XL ND OFF; SR ND ON

07:37     9     -22.2  -22.2  -21.3  -15.7  SR ND OFF; XR ND ON

07:40    10     -22.0  -22.3  -21.4  -22.2  XR ND OFF

AMB load physical temps:

S1=20.06

S2=20.12

X1=19.69

Weather conditions:

T=8.1C

H=47.2 percent

sky=clear

EOA      07:45                                       Stop 25 kHz recordings

AMB = ambient load

BOT = Beginning of Track

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Dick Simpson

Original: 2006-06-24

Added 05:50 entry to Table 3: 2006-07-12

Added AMB load phys temps before post-cal: 2006-07-17

X-RCP and S-RCP ND errors during pre-cal added: 2006-07-18