From jesse.velasco@dsn.nasa.gov Thu Oct  8 10:47:21 2009

Return-Path: <jesse.velasco@dsn.nasa.gov>

Received: from DSNOAM-MM.jpl.nasa.gov (dsnoam-mm.jpl.nasa.gov [128.149.207.83])

by magellan.stanford.edu (8.11.7p3+Sun/8.11.7) with ESMTP id n98HlGT26679

for <rsimpson@magellan.stanford.edu>; Thu, 8 Oct 2009 10:47:16 -0700 (PDT)

Received: from dsnoamex1.jpl.nasa.gov (Not Verified[128.149.207.88]) by DSNOAM-MM.jpl.nasa.gov with MailMarshal (v6,4,6,5922)

id <B4ace25a20002>; Thu, 08 Oct 2009 10:47:14 -0700

X-MimeOLE: Produced By Microsoft Exchange V6.5

Content-class: urn:content-classes:message

MIME-Version: 1.0

Content-Type: multipart/alternative;

boundary="----_=_NextPart_001_01CA483F.5E7C2016"

Subject: BRIEFING MESSAGE FOR MEX BI STATIC R/S DOY 284 DSS-14

Date: Thu, 8 Oct 2009 10:47:13 -0700

Message-ID: <E0C1F6A50A6ED64287BBCD54F0D371ED02666C19@dsnoamex1.jpl.nasa.gov>

X-MS-Has-Attach:

X-MS-TNEF-Correlator:

Thread-Topic: BRIEFING MESSAGE FOR MEX BI STATIC R/S DOY 284 DSS-14

Thread-Index: AcpIP16LS/BFtWhaRsicy9kOOFA62w=

From: "Velasco, Jesse" <jesse.velasco@dsn.nasa.gov>

To: "DSN-Official" <DSN-Official@jjpl.jpl.nasa.gov>,

"!DL-DSN-NOCC" <DL-DSN-NOCC@dsn.nasa.gov>,

"!DL-DSN-DSOT" <DL-DSN-DSOT@dsn.nasa.gov>,

"!DL-DSN-SPSSPA" <DL-DSN-SPSSPA@dsn.nasa.gov>,

<gene.goltz@jpl.nasa.gov>, <Daniel.S.Kahan@jpl.nasa.gov>,

<rs@list.jpl.nasa.gov>,

"GDSCC Operations," <GDSCCOperations@gdscc.nasa.gov>

Cc: "Thompson, Thomas W" <twthomps@mail.jpl.nasa.gov>,

"Angold, Nigel G" <nangold@mail.jpl.nasa.gov>,

"Landon, Arthur J" <arthur.landon@dsn.nasa.gov>,

"Hodder, James A" <jahodder@mail.jpl.nasa.gov>,

"Beyer, Patrick E" <pbeyer@mail.jpl.nasa.gov>,

"Williams, Raymond C" <rcw@mail.jpl.nasa.gov>,

"Magallanes, Margaret R" <margaret.magallanes@dsn.nasa.gov>,

"Berner, Jeff B" <jbberner@mail.jpl.nasa.gov>,

"Guerrero, Anamaria P" <ana@mail.jpl.nasa.gov>,

"Marina, Miguel" <mmarina@mail.jpl.nasa.gov>,

"Hodgin, Wendy K" <whodgin@mail.jpl.nasa.gov>,

"Hodder, James A" <jahodder@mail.jpl.nasa.gov>,

"Eaton, Curtis A" <ceaton@mail.jpl.nasa.gov>,

"Davis, Esker B" <eskerb@mail.jpl.nasa.gov>,

"Kurtik, Susan C" <skurtik@mail.jpl.nasa.gov>, <Michel.Denis@esa.int>,

<Peter.Schmitz@esa.int>, <Olivier.Reboud@esa.int>,

"!DL-DSN-MPSETD" <DL-DSN-MPSETD@dsn.nasa.gov>,

"Dick Simpson 650-723-3525" <rsimpson@magellan.stanford.edu>,

=?iso-8859-1?Q?Martin_P=E4tzold?= <mpaetzol@uni-koeln.de>

Content-Length: 81193

Status: RO

This is a multi-part message in MIME format.

------_=_NextPart_001_01CA483F.5E7C2016

Content-Type: text/plain;

charset="iso-8859-1"

Content-Transfer-Encoding: quoted-printable

Mars Express (MEX)

Briefing Message

Level 4

Bi-Static Radar Experiment Support

Prepared by: J Velasco / MEX  NOPE / MPSETD

Origination Date: DOY 281 /  1700 UTC

Revision: Original

DSS 14 DOY 284 / 1310 UTC

ROUTING: JFTL / JJPL / JGTS

FROM: MPSETD / J Velasco

SUBJECT:  Mars Express Bi-Static Radar Support

NOP: 871-049-041, REV. L

SCHEDULE: Refer to DSN 7-Day Schedule for actual support times.

DOY   Start   BOT   EOT   End   Facility   User   Activity

284   1310   1510   1725   1825   DSS-14   MEX   T/P BISTATIC R/S

LEVEL / TYPE: Level 4 / Bi-Static Radar support

1.   OVERVIEW:

Bi Static Radar (BSR) experiment employs the MEX spacecraft's

transmitter and a DSN 70-m antenna to receive weak S-band and X-band

dual polarized RF signals and Radio Science Receivers (RSRs) to

simultaneously receive and record these four signals. At a predetermined

time during the pass, the spacecraft slews toward Mars so that its

transmitted S-band and X-band RCP signals illuminate the planet's

surface. As these RCP signals bounce off the surface, part of the

signals change polarization to Left Circular Polarization (LCP)

effectively creating four signals; 1) S-band RCP, 2) S-band LCP, 3)

X-band RCP and 4) X-band LCP.

DSN Mars Express Bistatic Radar (BSR) calibration procedures are

performed in three parts: 1) Pre-calibration, 2) Mini- calibration and

3) Post-calibration. Section-8 details the pre-calibration procedures,

section-9 details mini-calibration procedures, and section-10 details

post calibration procedures.

2.   SUPPORT DOCUMENTATION:

a.   This briefing message

b.   Bi-Static Radar SOE. Radio Science shall provide start/stop times of

BSR mini-pre-calibrations near real-time.

3.   SUPPORT REQUIREMENTS:

NOTE:  Do not use Time Stacked Directives.  We have experienced

problems with certain time stacked directives slow to execute causing

the next directive in the queue to be rejected.  Consequently, this

leads to configuration errors and the need to repeat steps.

a.   DOWNLINK SUPPORT ONLY

b.   DTTS (DOWNLINK TRACKING AND TELEMETRY) RECEIVERS:

1.   One DTT shall be configured with table 7041HRX to support X-band, and

to control the 12.5k noise diode on/off at predetermined times during

pre-pass calibrations, real-time BSR activities and post calibrations

activities.

2.   A second DTT shall be configured with table 7041HRXS to support

S-band carrier only and to control the 12.5 k noise diode on/off at

predetermined times during pre-pass calibrations, real-time BSR

activities and post calibrations activities.

c.   UPLINK:

There are NO uplink requirements

d.   COMMAND:

There are NO command requirements

e.   RADIO SCIENCE RECEIVERS (RSR):

NOTE: For remote operations the FSPR must not be assigned to the DSS

link. The RSRs are controlled and configured remotely by the Radio

Science group located at JPL. The RSR operator will configure four radio

science receivers to simultaneously receive and record S-band and X-band

RCP and LCP polarized signals. The RSR equipment requires both S-band

and X-band 1-way and 2-way downlink predicts. The actual RSR resources

configured for support will depend on availability.

4.   SUPPORT PRODUCTS ANALYST:

(1)   Ensure the Support Data Package (SDP) is created and contains the

required support products. The SDP is created five days in advance of

the schedule support.

a.  SOE

b.  S and X-band DLF predicts

c.  PX6 predicts

(2)   Ensure S and X-band DLF predicts are posted to the SPS portal four

days before the schedule support to meet Radio Science support

requirement.

(3)   Ensure the SDP is transmitted to the station 24 hours before the

scheduled support.

5.   NOCC:

OPS-CHIEF/TSS:

Participate in the pre and post-pass briefing and help in trouble

shooting.

COMM-Chief:

Configure a voice line for MEX MOC, R/S group, and supporting station.

DSOT:

There are no SLE telemetry return link services required.

6.   SPACECRAFT CONFIGURATION:

The spacecraft shall be reconfigured for X-band and S-band downlink

carrier only in accordance with the SOE.

7.   PRE-CALIBRATION PROCEDURES AND CONFIGURATION

The times shown below in step-1 through step-18 are to illustrate event

chronology and event duration:

a.   Pre-calibration requires configuring the 70m-antenna microwave

subsystem so that each receiving downlink channel (S-RCP, S-LCP, X-RCP,

X-LCP) can be cycled in sequence through the four configurations listed

below.  The antenna must be pointed to zenith for pre-calibration.

1.   Receiving channel into ambient load with noise diode off

2.   Receiving channel into ambient load with noise diode on

3.   Receiving channel into sky (zenith) with noise diode on

4.   Receiving channel into sky (zenith) with noise diode off

NOTE 1: In this briefing message DTT01 is used for X-band and DTT02 is

used for S-band, but any available DTT resource can be used.

NOTE 2: Do not time stack Operator Directives (ODs). Pass experience

has shown that time stacking may result in rejection of ODs or delayed

OD execution.

b.   Link controller perform the procedures in step 1 and advise radio

science when completed; wait at this point until directed by radio

science to proceed to step 2.

Step 1   00:00:00   Confirm dichoric reflector is in place

Configure X-RCP (LNA-1) to sky and output 1

Configure X-LCP (LNA-2) to sky and output 2

Configure S-LCP (LNA-2) low noise to sky and output 2

Configure S-RCP (LNA-1) via Diplexer to sky and output 1

Turn off CONSCAN

Track Sub-reflector

c.   Radio science operator set each RSR attenuator using the AUTO

feature. After checking for proper signal levels (about -10.0 dB ADC

amplitude on each RSR), direct the link controller to proceed to step 2.

Step 2   00:04:00   Configure X-LCP (LNA-2) to ambient load-1

Configure X-RCP (LNA-1) to ambient load-1

Step 3   00:06:00   Configure S-LCP (LNA-2) to ambient load-2

Step 4   00:08:00   Configure S-RCP (LNA-1) to ambient load-1

d.   Link controller and radio science operator after completing steps 2

through 4, perform the following procedures, (1) through (5):

1.   Link Controller report ambient load temperatures (S1, S2, and X1)

from the PRFREA display and report current weather conditions,

(temperature, humidity, and sky conditions) to the Radio Science

operator.

2.   Radio Science operator set each RSR attenuator using AUTO feature

3.   RSR operator run radio science recorders

4.   RSR operator report to Link Controller when radio science recorders

are recording

5.   Link controller execute the following procedures at 5 min intervals

and report the completion of each step to the RSR operator:

Step 5   00:10:00   Disconnect DC01 IF

Connect DC01 IF to X-RCP

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Disconnect DC02 IF

Connect DC02 IF to S-RCP

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

Step 6   00:15:00   Enable X-RCP (DC01) noise diode (SNT)

Step 7   00:20:00   Configure X-RCP to sky and output 1

Configure X-LCP to sky and output 2

Step 8   00:25:00   Disable X-RCP (DC01) noise diode

Disconnect DC01 IF

Connect DC01 IF to X-LCP

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Step 9   00:30:00   Enable X-LCP (DC01)  noise diode

Confirm noise diode selected is 12.5

Step 10  00:35:00   Configure X-RCP (LNA-1) to ambient load and output 1

Configure X-LCP (LNA-2) to ambient load and output 2

00:36:00   Link controller report ambient load temp (S1, S2, X1)

from the PRFREA display to the RS operator.

Step 11  00:40:00   Disable X-LCP (DC01) noise diode

Step 12  00:45:00   Configure X-RCP (LNA-1) to sky and output 1

Configure X-LCP (LNA-2) to sky and output 2

Step 13  00:50:00   Enable S-RCP (DC02) noise diode

Disconnect DC01 IF

Connect DC01 IF to X-RCP

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Step 14  00:55:00   Configure S-RCP (LNA-1) to sky via the diplexer and

output 1

Step 15  01:00:00   Disable S-RCP (DC02) noise diode

Disconnect DC02 IF

Connect DC02 IF to S-LCP

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

Confirm noise diode is 12.5

Step 16  01:05:00   Enable S-LCP (DC02) noise diode

Step 17  01:10:00   Configure S-LCP (LNA-2) to sky with output 2

Step 18  01:15:00   Disable S-LCP (DC02) noise diode

Disconnect DC02 IF

Connect DC02 IF to S-RCP

Turn DC02 SNT MFQ on

Confirm noise diode is 12.5

Link controller report ambient load physical

temperatures (S1, S2, and X1) from PRFREA display

to the RS operator

01:20:00   End of BSR noise measurement pre-cal procedure

8.   MINI CALIBRATION PROCEDURES AND TIMELINE

NOTE: Carrier lock of X and S-band closed loop receiver (DTT) not

required.

a.   Link controller, shortly after MEX begins its slew and before the BSR

surface observations begin, confirm DTT 01 and DTT 02 configurations.

b.   Link controller confirm DTT 01 is configured for X-RCP with noise

diode 12.5 and MFQ on.

c.   Link controller confirm DTT 02 is configured for S-RCP with noise

diode 12.5 and MFQ on.

d.   RSR operator ensure all radio science Recorders are recording.

e.   Link controller, at direction from RSR operator, begin the BSR

mini-noise calibration procedures. The times shown are to illustrate

event chronology and event duration:

Step 1   00:00:00   Enable X-RCP (DC01) noise diode

Confirm noise diode value is 12.5

Step 2   00:03:00   Disable X-RCP (DC01) noise diode

Enable S-RCP (DC02) noise diode

Disconnect DC01 IF

Reconnect DC01 IF to X-LCP

Verify X-band microwave configuration

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Step 3   00:06:00   Disable S-RCP (DC02) noise diode

Enable X-LCP (DC01) noise diode

Disconnect DC02 IF

Reconnect DC02 IF to S-LCP

Verify S-band microwave configuration

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

Step 4   00:09:00   Disable X-LCP (DC01) noise diode

Enable S-LCP (DC02) noise diode

Disconnect DC01 IF

Reconnect DC01 IF to X-RCP

Verify X-band microwave configuration

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Step 5   00:12:00   Disable S-LCP (DC02) noise diode

Disconnect DC02 IF

Reconnect DC02 IF to S-RCP

Verify S-band microwave configuration

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

00:15:00   End of BSR mini-noise cal

Step 6   Link controller repeat the BSR mini-noise calibration procedures

steps 1-5 after MEX has completed its surface observations and

before it returns to Earth point. The start time will be provided

by radio science.

9.   POST CALIBRATION PROCEDURES AND TIMELINE:

Step 1   00:00:00   Link controller move antenna to zenith (do not stow)

Configure S-RCP (LNA-1) to ambient load-1

Configure S-LCP (LNA-2) to ambient load-2

Configure X-RCP (LNA-1) to ambient load-1

Configure X-LCP (LNA-2) to ambient load-1

Disconnect DC01 IF

Connect DC01 IF to X-RCP

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Disconnect DC02 IF

Reconnect DC02 IF to S-RCP

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

a.   Link controller advise the RSR operator when the antenna is at zenith

and the configurations listed above have been completed.

b.   Link controller report physical temperatures of each ambient load

(S1, S2, and X1) from the downlink PRFREA display.

c.   RSR operator run all radio science Recorders and record ambient loads

for 3 min. At completion, advise the link controller to proceed with the

following steps:

Step 2   00:03:00   Enable X-RCP (DC01) noise diode

Step 3   00:06:00   Disable X-RCP (DC01) noise diode

Enable S-RCP (DC02) noise diode

Disconnect DC01 IF

Reconnect DC01 IF to X-LCP

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Step 4   00:09:00   Disable S-RCP (DC02) noise diode

Enable X-LCP (DC01) noise diode

Disconnect DC02 IF

Reconnect DC02 IF to S-LCP

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

Step 5   00:12:00   Disable X-LCP (DC01) noise diode

Enable S-LCP (DC02) noise diode

Step 6   00:15:00   Configure S-RCP (LNA-1) to sky

Configure S-LCP (LNA-2) to sky

Configure X-RCP (LNA-1) to sky

Configure X-LCP (LNA-2) to sky

Step 7   00:18:00   Disable S-LCP (DC02) noise diode

Enable X-LCP (DC01) noise diode

Disconnect DC02 IF

Reconnect DC02 IF to S-RCP

Select the 12.5 noise diode on DC02

Turn DC02 SNT MFQ on

Step 8   00:21:00   Disable X-LCP (DC01) noise diode

Enable S-RCP (DC02) noise diode

Disconnect DC01 IF

Reconnect DC01 IF to X-RCP

Select the 12.5 noise diode on DC01

Turn DC01 SNT MFQ on

Step 9   00:24:00   Disable S-RCP (DC02) noise diode

Enable X-RCP (DC01) noise diode

Step 10   00:27:00   Disable X-RCP (DC01) noise diode

00:30:00   End

d.   Link Controller report physical temperatures of each ambient load

(S1, S2, and X1) from the downlink PRFREA display and report the current

weather (temperature, humidity, and sky conditions) to radio science.

e.   Radio Science operator stop RSRs.

f.   End of BSR noise post-calibration procedures.

g.   Link Controller proceed with normal tear-down procedures.

h.   Re-initialization of the DTTs is recommended.

MPSETD POINTS OF CONTACT:   !DL-DSN-MPSETD@dsn.nasa.gov

MPSETD NOPE's   OFFICE   CELL

Scott riley (Lead)   (626) 305-6284   (626) 372-0862

Jesse Velasco    (626) 305-6315

Romy Paredes    (626) 305-6309

Greg Hewitt    (626) 305-6292

Anthony Knight   (626) 305-6305

Jesse Velasco

NOPE

MEX/SELE/VEX/ROSE/CLUS

(626) 305-6315

THE TECHNICAL DATA IN THIS DOCUMENT (OR FILE) IS CONTROLLED UNDER THE

U.S. EXPORT REGULATIONS, AND MAY NOT BE RELEASED TO FOREIGN PERSONS

WITHOUT A LICENSE AUTHORITY.

This document has been reviewed for export control and it does NOT

contain export-controlled technical data.