Mars Express Bistatic Radar Experiment

Operations Plan and Report

01 May 2010

Summary

=======

DSN Antenna:                                                     63

Orbit:                                                         8107

Orbit Start Time:                              2010-05-01T17:32:25

HGA Pointing:                                              Specular

Start    Mid Point      End

--------  ----------  --------

Specular Condition (ERT):               19:21      19:42      20:03

Target Latitude (deg N):               -20.55     -26.52     -34.44

Longitude (deg E):              140.94     137.40     135.53

Rp (km):                         3394.      3394.      3394.

Incidence/Reflection Angle (deg):       40.03      45.47      52.85

Slant Range (km):                       8838.      7841      6633.

Slew Angle (deg):                       99.39     89.06      74.29

Doppler (carrier, fd; Hz):            -39844.    -43359.    -45278.

Doppler (echo, fr; Hz):                15736.     18740.     19812.

Doppler Difference (fdd; Hz):         -55581.    -62100.    -65090.

Earth-Mars Distance (m):            1.935E+11  1.935E+11  1.935E+11

Experiment Set Up

=================

This experiment was conducted using the Madrid DSS 63.  Danny Kahan and Gene Goltz were in the Radio Science Support Area (RSSA) at JPL.  This report is largely based on notes provided by Kahan and Goltz.

Performance Problems and Notes

==============================

There no problems worthy of note.

Data Acquisition

================

RSRs were configured as in Table 1.

Table 1

----------------------------------------------------

RSR  Channel Mode  ATT FGAIN        Operator

dB

----- ------- ---- ---- ----- ----------------------

RSR1A  S-LCP   1-W auto   60    UNK

RSR1B  X-LCP   1-W auto   60    UNK

RSR2A  S-RCP   1-W auto   60    UNK

RSR2B  X-RCP   1-W auto   60    UNK

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   Occultation bandwidth (not recorded for BSR)

2          8 ksps   Occultation backup (not recorded for BSR)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  "Steps" are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-LCP  X-LCP  S-RCP  X-RCP  Notes / Comments

2010/121                 RSR1A  RSR1B  RSR2A  RSR2B

-------- ----- --------- -----  -----  -----  -----  ------------------------

FGAIN    15:44             60     60     60     65   Set FGAIN

Pre-Cal  16:54      1    -11.0  -15.7  -14.5   -9.9

16:55 att auto  -10.0   -9.6  -10.1   -9.9  Reset attenuators

17.5   17.5   15.5   26.5  Attenuator settings (dB)

16:56      2    -10.0   -0.3  -10.2   -0.0

16:57      3     -0.7   -0.3  -10.1   -0.1

16:58    "4,5"   -0.8   -0.4   -0.6   -0.2

17:01 att auto  -10.0  -10.1  -10.1   -3.2  Ambient load phys temps

S1=18.94

S2=23.69

X1=15.62

28.5   28.5   27.0   31.5  Attenuator settings (dB)

Local weather:

T=19.2C

H=45.7 percent

sky=partly cloudy

17:02  rec 3 e                              Begin 25 kHz recording

17:02      6     -9.9  -10.2  -10.1   -3.1

17:07      7    -10.0  -10.2  -10.1   -3.0

17:12      8    -10.0  -21.8  -10.1  -12.7

17:17      9    -10.1  -21.8  -10.1  -15.0

17:22     10    -10.0  -19.8  -10.1  -15.0   Confirmed 12.5 K ND

17:27   "11,12" -10.0   -9.9  -10.2   -3.2   Ambient load phys temp:

S1=18.94

S2=23.69

X1=15.62"

17:32     13    -10.1  -10.1  -10.1   -3.2

17:37     14    -10.0  -21.8  -10.1  -14.9

17:42     15    -10.1  -21.8   -9.9  -15.0

17:47     16     -9.9  -21.8  -19.5  -14.9

17:52     17     -9.9  -21.8  -21.5  -15.0   Confirmed 12.5 K ND

17:57     18     -9.8  -21.9  -21.5  -15.0

18:02     19    -19.2  -21.8  -21.4  -15.1

18:07     20    -21.0  -21.8  -21.4  -15.2   Ambient load phys temp:

S1=18.69

S2=23.62

X1=15.44

18:12  21/end   -21.0  -21.9  -21.3  -15.3   Stop 25 kHz recording

BOT      18:35           -21.0  -21.7  -21.5  -14.3   TLM on until 18:51

18:50 rec 3 e   -21.0  -21.6  -21.5  -12.7   Resume 25 kHz recording

19:00           -21.0  -21.7  -21.6  -13.0   DSS 63 switch to Mars

pointing predicts

19:02 sfro 3/SX  +10k   +49k   +10k   +49k   Rcvr tuning offset (Hz)

sfro 4/X          +45k          +45k

MiniCal1 19:04      1    -20.9  -21.7  -21.5  -11.3   Confirmed 12.5 K ND

19:07      2    -20.8  -21.7  -19.6  -13.0

19:10      3    -20.9  -19.7  -21.9  -13.0

19:13      4    -19.2  -21.7  -21.8  -12.9

19:16      5    -20.9  -21.7  -21.7  -12.9

19:19     end   -20.9  -21.7  -21.6  -12.8

BSR      19:21  rec 4 e  -20.8  -21.7  -21.6  -12.9   Begin 100 kHz recording

19:33 sfro 3/X          +53k          +53k   Rcvr tuning offset (Hz)

19:48 sfro 3/X          +57k          +57k   Rcvr tuning offset (Hz)

end      20:03  rec 4 d  -21.1  -21.6  -21.6  -12.6   end 100 kHz recording

MiniCal2 20:06      1    -21.1  -21.6  -21.4  -10.8   Confirmed 12.5K ND

20:09      2    -21.1  -21.6  -19.5  -12.5

20:12      3    -21.4  -19.7  -21.3  -12.5

20:15      4    -19.6  -21.6  -21.3  -12.5

20:18      5    -21.3  -21.7  -21.3  -12.5

20:21    end    -21.3  -21.7  -21.4  -13.6

20:22 sfro 3/SX     0      0      0      0  Rcvr tuning offset (Hz)

Return to s/c pointing

predicts

EOT      20:37    stow   -21.1  -21.6  -21.4  -12.6

PostCal  20:43      1     -9.8  -10.2   -9.8   -2.9  AMB load phys temps:

S1=16.88

S2=21.25

X1=14.50

20:46      2     -9.8  -10.1   -9.8   -2.7

20:49      3     -9.7  -10.4   -9.7   -2.9

20:52      4     -9.7  -10.0   -9.9   -3.0

20:55      5     -9.6          -9.8   -3.0

20:58      6    -19.2  -21.0  -21.3  -14.6

21:01      7    -21.0  -19.8  -21.2  -14.5

21:04      8    -21.2  -21.8  -19.4  -14.6

21:07      9    -21.0  -21.9  -21.4  -12.2

21:10     10    -21.0  -21.9  -21.3  -14.6  AMB load phys temps:

S1=16.75

S2=20.81

X1=14.94

Local weather:

T=14.5C

H=60.0 percent

sky=partly cloudy

21:13  11/end   -21.1  -21.9  -21.3  -14.6  End 25 kHz recording

AMB = ambient load

BOT = Beginning of Track

BW = bandwidth

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOA = End of activity

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

NOP = Network Operations Plan

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

s/c = spacecraft

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Post Analysis Summary

X-Band Spur:  There is a spur of unknown origin that drifts with the X-Band surface echo in both polarizations.  It starts about 1 kHz below the echo (19:21) and ends about 5 kHz below (20:03).  It never infringes on the echo bandwidth, so careful choices of noise and echo windows keeps it from being a problem.  There was an X-Band spur in data collected at DSS 63 on day 106; it started about 20 kHz above the echo and ended 6 kHz above, also not causing problems during analysis.

S-LCP Amplitude Calibration: S-LCP noise power varies about 5 percent between 19:36 and 19:45 -- starting high, dropping to its final value, returning to its original value, and ending low.  There is no comparable variation in S-RCP noise power.  The S-LCP amplitude scaling was modified to correct for these changes by using a linear correction.  The GNC file has the following entries:

Gain (G)      dG/dt           t_start (s)  t_stop (s)

---------  -----------         -----------  ----------

2761.278   0.00000000         69600.000    70560.000

2761.278   0.32181221         70560.000    70773.000

2829.824  -0.29932750         70773.000    71002.000

2761.278   0.39852326         71002.000    71174.000

2829.824   0.00000000         71174.000    72300.000

Dick Simpson

Original: 2010-05-18

Added Post-Analysis Summary: 2010-05-25

Removed PDS unfriendly characters: 2011-05-17