Mars Express Bistatic Radar Experiment

Operations Plan and Report

06 August 2010

Summary

=======

DSN Antenna:                                                     43

Orbit:                                                         8438

Orbit Start Time:                               2010-08-06T04:33:12

HGA Pointing:                                              Specular

Start    Mid Point      End

--------  ----------  --------

Specular Condition (ERT):               06:50      07:33      08:16

Target Latitude (deg N):                14.43     -10.94     -44.59

Longitude (deg E):              141.25     133.25     230.22

Rp (km):                         3394.      3394.      3394.

Incidence/Reflection Angle (deg):       51.29      61.84      87.08

Slant Range (km):                       8017.      5008.      1468.

Slew Angle (deg):                       77.41      56.32       5.83

Doppler (carrier, fd; Hz):            -17341.    -14766.     25451.

Doppler (echo, fr; Hz):                23528.     28833.     25729.

Doppler Difference (fdd; Hz):         -40868     -43599.      -277.

Earth-Mars Distance (m):            3.027E+11  3.027E+11  3.027E+11

Experiment Set Up

=================

This experiment was conducted using the Canberra DSS 43.  Danny Kahan and Gene Goltz were in the Radio Science Support Area (RSSA) at JPL.  This report is largely based on notes provided by Goltz.

Performance Problems and Notes

==============================

It appears from the system temperatures that the S-Band configuration was optimized for telemetry rather than bistatic radar.  At zenith S-RCP Tsys was 19-20K while the S-LCP value was 25-26K.

Data Acquisition

================

RSRs were configured as in Table 1.

Table 1

-----------------------------------------------------

RSR   Channel Mode  ATT FGAIN        Operator

dB

------ ------- ---- ---- ----- ----------------------

WVSR1A  S-LCP   1-W auto   60    UNK

WVSR1B  X-LCP   1-W auto   60    UNK

RSR2A   S-RCP   1-W auto   60    UNK

RSR2B   X-RCP   1-W auto   65    UNK

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   Occultation bandwidth (not recorded for BSR)

2          8 ksps   Occultation backup (not recorded for BSR)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  Steps are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-LCP  X-LCP  S-RCP  X-RCP  Notes / Comments

2010/218                 RSR1A  RSR1B  RSR2A  RSR2B

-------- ----- --------- -----  -----  -----  -----  ------------------------

Set-Up   03:35   FGAIN      60     60     60     65  FGAIN settings (dB)

Pre-Cal  04:16     1      -3.5   -9.7  -14.4  -10.6  Confirm ND disabled

04:17  att auto  -9.8   -9.9   -9.8   -9.6  ADC magnitudes (dB)

19.5   16.0    8.5   12.5  Attenuator settings (dB)

04:18     2      -9.8   -0.1   -9.9    0.1

04:20     3      -1.5   -0.0   -9.8    0.0

04:21    4,5     -1.4   -0.0   -0.4    0.1

04:23  att auto -10.2   -9.6   -9.8   -9.5  Attenuator auto reset

29.5   28.0   20.0   25.0  Attenuator settings (dB)

Ambient load phys temps:

S1=20.81

S2=21.56

X1=21.12

Local weather:

T=10.4C

H=49.0 percent

sky=scattered clouds

04:25  rec 3 e                              Begin 25 kHz recording

04:25     6     -10.2   -9.5   -9.7   -9.6

04:30     7     -10.2   -9.5   -9.7   -8.9

04:35     8     -10.4  -22.0   -9.6  -15.6

04:40     9     -10.4  -22.0   -9.7  -22.2

04:45    10     -10.2  -16.8   -9.8  -22.1  Confirm 12.5K ND

04:50   11,12   -10.2   -9.0   -9.7   -9.6  Ambient load phys temps:

S1=21.12

S2=21.62

X1=21.06

04:55    13     -10.3   -9.5   -9.8   -9.7

05:00    14     -10.3  -21.9   -9.7  -22.2

05:05    15     -10.3  -22.0   -9.6  -22.3

05:10    16     -10.4  -22.0  -19.3  -22.3

05:15    17     -10.3  -22.0  -21.5  -22.2  Confirm 12.5K ND

05:20    18     -10.2  -21.9  -21.5  -22.2

05:25    19     -18.4  -22.1  -21.6  -22.2

05:30    20     -19.8  -22.1  -21.5  -22.1  Ambient load phys temps:

S1=21.31

S2=21.69

X1=21.06

05:35  21/end   -19.8  -22.0  -21.5  -22.2  Stop 25 kHz recording

BOT      05:50           -19.9  -21.7  -21.7  -21.9  collect TLM until 06:09

06:10  rec 3 e  -19.9  -21.7  -21.4  -21.9  resume 25 kHz recording

06:25           -19.9  -21.8  -21.4  -22.1  DSS 43 switch to Mars

planetary predicts

06:28 sfro 3/SX   +5K   +37K    +5K   +37K  Rcvr tuning offset (Hz)

sfro 4/X          +20K          +20K

MiniCal1 06:31     1     -19.9  -21.9  -21.4  -15.7  Confirm 12,.5K ND

06:34     2     -19.7  -21.8  -19.3  -22.1

06:37     3     -19.9  -16.8  -21.5  -22.0

06:41     4     -18.5  -21.7  -21.5  -21.9

06:44     5     -19.7  -21.7  -21.5  -21.9

06:47    end    -19.6  -21.6  -21.4  -21.0

BSR      06:50 rec 4 e   -19.7  -21.7  -21.4  -21.1  Begin 100 kHz recording

07:48 sfro 3/X          +27K          +27K  Rcvr tuning offset (Hz)

07:56 sfro 3/X          +17K          +17K

08:02 sfro 3/X           +7K           +7K

08:09 sfro 3/X             0             0  Remove rcvr offsets

end      08:16 rec 4 d   -19.8  -21.5  -21.4  -20.8  End 100 kHz recording

sfro 3/SX  +37K   +37K   +37K   +37K  Rcvr tuning offset (Hz)

MiniCal2 08:20     1     -19.5  -21.5  -21.4  -15.5  Confirm 12.5K ND

08:22     2     -19.5  -21.4  -19.2  -20.7

08:24     3     -19.6  -16.6  -21.4  -20.8

08:26     4     -18.3  -21.5  -21.2  -20.8

08:28     5     -19.6  -21.5  -21.2  -20.7

08:30    end    -19.5  -21.4  -21.1  -20.7

08:31 sfro 3/SX     0      0      0      0  Remove rcvr offsets

Collect TLM to EOT

EOT      08:45    stow   -19.5  -21.4  -21.2  -20.0  ADC amplitudes (dB)

Post-Cal 08:51     1     -10.0   -9.4   -9.9   -9.6  Ambient load phys temps:

S1=19.25

S2=20.38

X1=20.25

08:54     2     -10.2   -9.4  -10.0   -8.8

08:57     3     -10.2   -9.6   -9.8   -9.7

09:00     4     -10.2   -9.0   -9.9   -9.7

09:03     5      -9.9   -9.4   -9.9   -9.7

09:06     6     -18.4  -22.0  -21.5  -22.3

09:09     7     -19.7  -16.8  -21.5  -22.0

09:12     8     -19.7  -22.0  -19.2  -22.1

09:15     9     -19.7  -22.1  -21.5  -15.5

09:18    10     -19.6  -22.1  -21.5  -22.2  Ambient load phys temps:

S1=19.25

S2=20.12

X1=20.12

Local weather:

T=3.8C

H=87.0 percent

sky=clear

EOA      09:22  11/end   -19.8  -22.0  -21.6  -22.3  End 25 kHz recording

AMB = ambient load

BOT = Beginning of Track

BW = bandwidth

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOA = End of activity

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

NOP = Network Operations Plan

occn = occukltation

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

s/c = spacecraft

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Post Analysis Summary

X-Band Power: X-Band data were processed to power spectra with 60 second averaging (sums of 1464 individually calculated 1024-point spectra).  The 86 minutes of 25 kHz data were divided into 10 time intervals -- four with split echoes (caused by receiver tuning offset changes, FRO) and eight during which the echo drifted within the passband at fixed FRO.

The directly propagating carrier did not appear in the 25 kHz passband until the last 14 spectra; except for these 14 spectra, the carrier tracking window was used to find the frequency bin with maximum echo power.  Carrier suppression was used to process spectra 80-86 since the returning carrier was between the two components of the surface echo in the first and was within the echo power computation window of the others.

Int       Times       Spectra   Noise  Bins     Echo      Echo Bins    Notes

Peak

--- ----------------- ------- --------------- ------- ---------------- ------

A     06:50-07:38     01-48  104:455,785:916 460:780      460:780

B     07:38-07:48     49-58  104:160,785:916 460:780 460:660->164:410

BC    07:48-07:49       59   104:160,765-916 165:760      165:760       [1]

C     07:49-07:56     60-66  104:160,720:916 165:715 460:710->164:420

CD    07:56-07:57       67   104:160,765:916 165:760      165:760       [1]

D     07:57-08:02     68-72  104:160,720:916 165:715 410:710->164:450

Int       Times       Spectra   Noise  Bins   Carrier     Echo Bins    Notes

Peak

--- ----------------- ------- --------------- ------- ---------------- ------

DE    08:02-08:03       73   104:160,785:916 079:083      164:780      [1,2]

E     08:03-08:09     74-79  104:160,740:916 079:083 460:730->164:450   [2]

EF    08:09-08:10       80   104:160,700:916 365:369      165:695      [1-3]

F     08:10-08:16     81-86  104:250,640:916 365:369 400:630->275:510   [3]

Notes: [1] Split echo resulting from change in X-Band receiver tuning offset

[2] Carrier at bin 81

[3] Carrier at bin 367

S-Band Power: S-Band data were processed in the same way.  The echo signals were weak so two different integrations were used (60 s and 360 s -- first three rows and second three rows, respectively, in the table below).  The directly propagating carrier was in frequency bin 246 for the entire observation.

Int       Times       Spectra   Noise  Bins   Carrier     Echo Bins    Notes

Peak

--- ----------------- ------- --------------- ------- ---------------- ------

A     06:50-07:38     01-48  250:630,830:916 244:248      635:825

B     07:38-08:08     49-78  104:245,815:916 244:248 640:880->250:400

C     08:08-08:16     79-86  104:240,380:916 244:248 260:360->220:300   [1]

A     06:50-07:38     01-08  250:630,830:916 244:248      635:825

B     07:38-08:08     09-13  104:240,780:916 244:248 610:840->250:380

C     08:08-08:14       14   104:240,380:916 244:248      250:350

Notes: [1] Carrier suppression was used to calculate echo power.  The carrier

Was located.  The power in that frequency bin and its two

neighbors on either side were set to values interpolated from the

neighbors beyond.

Dick Simpson

Original: 2010-08-12

Added Post-Analysis Summary: 2010-08-13