Mars Express Bistatic Radar Experiment

Operations Plan and Report

14-15 February 2012

Summary

=======

DSN Antenna:                                                      63

Orbit:                                                         10352

Orbit Start Time:                                2012-02-14T23:49:05

HGA Pointing:                                               Specular

Start  Descend EQX      End

--------  ----------   --------

Specular Condition (ERT):               00:54       01:25      02:23

Target Latitude (deg N):                 9.75       -0.03     -27.91

Longitude (deg E):              242.68      236.85     234.97

Rp (km):                         3394.       3394.      3394.

Incidence/Reflection Angle (deg):       61.10       63.34      68.92

Slant Range (km):                      11141.      10111.      6671.

Slew Angle (deg):                       57/80       53.33      42.15

Doppler (carrier, fd; Hz):             -5668.       -704.     15778.

Doppler (echo, fr; Hz):                10195.      17458.     34125.

Doppler Difference (fdd; Hz):         -15863      -18162.    -18347.

Earth-Mars Distance (m):            1.072E+11   1.072E+11  1.072E+11

Experiment Set Up

=================

This experiment was conducted using the Madrid DSS 63.  Danny Kahan and Gene Goltz were in the Radio Science Support Area (RSSA) at JPL.  Jesse Velasco was in the JPL NOPE area.  Dick Simpson monitored by telephone from Stanford.

Performance Problems and Notes

==============================

There were some problems with signal levels at the beginning of track.  Expected ADC levels were not obtained with the nominal FGAIN and automatic attenuator settings on two channels.  It appeared that the X-RCP levels were clipping intermittently.  After some experimentation it was decided to change X-RCP FGAIN to 70 dB and not to make changes on other channels.

Echoes were visible in all four channels; they became stronger as the experiment progressed.

Data Acquisition

================

RSRs were configured as in Table 1.

Table 1

-----------------------------------------------------

RSR   Channel Mode  ATT FGAIN        Operator

dB

------ ------- ---- ---- ----- ----------------------

RSR1A   S-LCP   1-W auto   60      UNK

RSR1B   X-LCP   1-W auto   60      UNK

RSR2A   S-RCP   1-W auto   60      UNK

RSR2B   X-RCP   1-W auto 65-70     UNK

RSR subchannels (SCHAN) were defined as follows:

Table 2

----------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          2 ksps   Occultation bandwidth (not recorded for BSR)

2          8 ksps   Occultation backup (not recorded for BSR)

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Times are in UTC and should be considered approximate.  Steps are as defined in the briefing message.  RSR ATT settings are in units proportional to dB.  Acronyms and abbreviations are explained after Table 3.

Table 3

-----------------------------------------------------------------------------

Activity  Time   Step #  S-LCP  X-LCP  S-RCP  X-RCP  Notes / Comments

2012/045                 RSR1A  RSR1B  RSR2A  RSR2B

-------- ----- --------- -----  -----  -----  -----  ------------------------

Set-Up   21:30   FGAIN      60     60     60     65  FGAIN settings (dB)

0      0      0      0  RSR tuning offset (Hz)

Pre-Cal  22:14     1      -7.8  -18.4  -15.8  -11.9  All rcvrs to SKY

22:15  att auto -10.0   -9.9   -9.7   -9.9  Autoset attenuators

23.0   17.5   13.5   24.5  Attenuator settings (dB)

22:16     2     -10.0   -0.4   -9.6   -0.1

22:18     3      -0.8   -0.3   -9.6   -0.1

22:19     4      -0.7   -0.3   -0.4   -0.1

22:23  att auto  -7.8   -9.8   -9.8   -4.8  Ambient load phys temps:

S1=14.75

S2=14.56

X1=14.56

31.5   29.0   25.0   31.5  Attenuator settings (dB)

Local weather:

T=3.4C

H=55.4 percent

sky=clear

22:25  rec 3 e                              Begin 25 kHz recording

22:30     5      -7.6   -9.6   -9.7   -4.7

22:35     6      -7.6   -9.7   -9.8   -4.5

22:40     7      -7.5  -21.5   -9.7  -14.6

22:45     8      -7.7  -21.4   -9.7  -17.1

22:50     9      -7.6  -19.5   -9.9  -16.9  Confirm 12.5 K ND

22:55    10      -7.7   -9.6   -9.7   -4.7  Ambient load phys temps:

S1=14.38

S2=14.25

X1=14.12

23:00    11      -7.7   -9.8   -9.8   -4.8

23:05    12      -7.7  -21.4   -9.8  -17.0

23:10    13      -7.7  -21.5   -9.8  -17.0

23:15    14      -7.7  -21.4  -19.3  -17.0

23:20    15      -7.7  -21.4  -21.3  -17.0  Confirm 12.5 K ND

23:25    16      -7.4  -21.4  -21.3  -17.1

23:30    17     -16.3  -21.4  -21.2  -17.0

23:35    18     -18.6  -21.5  -21.3  -17.1  Confirm 12.5 K ND

Ambient load phys temps:

S1=14.25

S2=13.88

X1=13.31

23:40   end     -18.6  -21.5  -21.3  -17.1  Stop 25 kHz recording;

antenna to point

2012/046

--------

BOT      00:10           -18.6  -21.2  -21.1  -13.0  X-Band AOS, TLM on

00:16                                       S-Band AOS

00:31 rec 3 e                               Resume 25 kHz recording

70  Revised FGAIN

X-Band TLM OFF

00:33           -18.6  -21.2  -21.1  -12.2  Switch to planetary

pointing predicts

00:34  fro 3/X          +10k          +10k  RSR tuning offset (Hz)

MiniCal1 00:37     1     -18.3  -21.1  -21.2  -10.8  Confirm 12.5 K ND

00:40     2     -18.4  -21.2  -19.2  -11.8

00:43     3     -18.5  -19.3  -21.1  -11.6

00:46     4     -16.3  -21.2  -21.1  -12.3

00:49     5     -18.4  -21.3  -21.1  -12.2

00:52    end    -18.4  -21.1  -21.1  -12.1

BSR      00:54 rec 4 e   -18.4  -21.2  -21.2  -12.5  Begin 100 kHz recording

end BSR  02:15 rec 4 d   -18.5  -21.3  -21.3  -16.3  End 100 kHz recording

MiniCal2 02:24     1     -18.4  -21.3  -21.2  -14.0  Confirm 12.5 K ND

02:27     2     -18.4  -21.3  -19.4  -16.3

02:30     3     -18.4  -19.4  -21.1  -15.6

02:33     4     -16.2  -21.3  -21.2  -14.7

02:36     5     -18.3  -21.2  -21.2  -14.6

02:39    end    -18.4  -21.2  -21.2  -14.7

02:40 sfro 3/X             0             0  RSR tuning offset (Hz)

Return to spacecraft

pointing predicts

EOT      02:48           -18.4  -21.6  -21.1  -14.6  Move antenna to zenith

(do not stow)

Post-Cal 02:51     1      -7.6   -9.8   -9.7   -4.6  AMB load phys temps:

S1=14.00

S2=12.81

X1=13.25

02:54     2      -7.7   -9.8   -9.7   -4.3

02:57     3      -7.6   -9.9   -9.5   -4.6

03:00     4      -7.6   -9.6   -9.8   -4.6

03:03     5      -7.4   -9.8   -9.7   -4.7

03:06     6     -16.1  -21.4  -21.0  -16.8

03:09     7     -18.4  -19.4  -21.1  -16.8

03:12     8     -18.5  -21.5  -19.2  -16.8

03:15     9     -18.5  -21.5  -21.0  -14.2

03:18    10     -18.5  -21.4  -21.1  -16.8  AMB load phys temps:

S1=14.06

S2=12.81

X1=13.56

Local weather:

T=1.2C

H=54.7 percent

sky=clear

EOA      03:22  rec 3 d  -18.4  -21.5  -21.1  -16.9  End 25 kHz recording

AMB = ambient load

BOT = Beginning of Track

BW = bandwidth

C = Celsius

CNR = Carrier to noise ratio

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOA = End of activity

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

k = kilo, thousand

K = Kelvin

LOS = loss of signal

ND = noise diode

No = noise power

NOP = Network Operations Plan

occn = occultation

Pc = carrier power

rcvr = receiver

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

s/c = spacecraft

SKY = receiver looking at sky

SL = S-LCP

SNR = Signal to noise ratio

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Post Analysis Summary

Strong echoes at end, modest at the beginning, and weak in the middle (but very visible at X-Band).  Only over the final 20 minutes is the S-LCP echo strength above 20 zW, which means earlier is probably not good for estimating S-Band dielectric constant.  Over the final 20 minutes (south of 15 deg S latitude), X-Band dielectric constant is 3-4 while S-Band dielectric constant is 2-2.5 (wavelength inversion).

Dick Simpson

Original: 2012-02-19

Post Analysis Summary added: 2013-05-08