Notes for 21 Jan 04 MEX BSR Test

Files and sources

DKF:

mger1:/domops/data/sle/41/seq/misc/dkf/xd002a.00.dkf	19974	Jan 16 14:42

TSOE:

mger1:/domops/data/sle/41/seq/misc/tsoe/xd002a.00.rsoe	48035	Jan 16 14:32

mger1:/domops/data/sle/41/seq/misc/tsoe/xd002a.00.rsoe.hdr	459	Jan 16 14:32

mger1:/domops/data/sle/41/seq/misc/tsoe/xd002a.00.rsoe.ps	62756	Jan 16 14:32

mger1:/domops/data/sle/41/seq/misc/tsoe/xd002a.00.rsoe.ps.hdr	465	Jan 16 14:32

mger1:/domops/data/sle/41/seq/misc/tsoe/xd002a.00.tsoe	20040	Jan 16 14:32

mger1:/domops/data/sle/41/seq/misc/tsoe/xd002a.00.tsoe.hdr	459	Jan 16 14:32

NOPE

Jesse Velasco will be on duty

Contact Info:

Martin Pätzold FAX:	(49) 221-470-5198

Martin Pätzold TEL:	(49) 221-470-3385

TCXO Frequency:

S-band	2296.482 MHz

X-band	8420.432 MHz

| ERT | Activity | Quant | XRCP=RSR1A | SRCP=RSR1B | SLCP=RSR2A | XLCP=RSR2B | RSR |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | rms | SNR | other | rms | SNR | other | rms | SNR | other | rms | SNR | other |  |
| 01:20:00 | Sami setting up voice net; MEX MOC and DSS 43 ready. MEX NOPE joined later. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 01:35:00 | DSS 43 reports: antenna=cold sky, CLR's=LCP; ready to begin noise cals when RSR's are recording |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 01:42 | RSRs recording; bandwidths/sample rate (kHz); bits per sample; freq offset (kHz) | fgain srate nbits FRO | 24 |  | 60 25 16 0 | 28 |  | 63 25 16 0 | 29 |  | 63 25 16 0 | 29 |  | 60 25 16 0 | R |
| 01:48 | LCP ND's on |  | 24 |  |  | 33 |  |  | 34 |  |  | 39 |  |  | R |
| 01:58 | Antenna=amb load |  | 77 |  |  | 84 |  |  | 85 |  |  | 85 |  |  | R |
| 02:13 | DSS 43 notes briefing message did not specify whether SNT should be on during ambient load, so it did both. |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 02:16 | CLRs=RCP, ND's off, cold sky |  | 25 |  |  | 29 |  |  | 30 |  |  | 39 |  |  | R |
| 02:18 | DSS 43 confirms XLCP diode off |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 02:20 | RCP ND's on |  | 25 |  |  | 33 |  |  | 34 |  |  | 39 |  |  | R |
| 02:25 | Amb load;ND's off |  | 77 |  |  | 84 |  |  | 85 |  |  | 84 |  |  | R |
| 02:33 | Ambient load physical temps (K) from downlink CALREDC display | S1 S2 X1 X2 |  |  | 293.0 |  |  | 293.4 |  |  | 295.1 |  |  | 291.6 | R |
| 02:37 |  |  | 25 |  |  | 84 |  |  | 85 |  |  | 39 |  |  | R |
| 02:38 |  |  | 25 |  |  | 84 |  |  | 85 |  |  | 28 |  |  | R |
| 02:46 | End RSR recording |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 03:20 | X-band carrier in RCP, LCP; no S-band signal. Station unable to lock S-band |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 03:33 | DSS 43 explains S-band: dichroic reflector prohibits S-band reception while X-band is being transmitted |  | 27 |  |  | 28 |  |  | 30 |  |  | 26 |  |  |  |
| 03:42 | DSS 43 X-band transmitter off |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 03:44 | s/c now 2-W; S-band signal appears; seems the same in both channels. X-band out of passband; lots of splatter in passband |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 03:59 | X-band carrier now at -10 kHz |  |  | 56 |  |  |  |  |  |  |  |  | 39 |  |  |
|  | S-band carrier now at -3 kHz |  |  |  |  |  | 47 |  |  | 47 |  |  |  |  |  |
| 04:06 | Start RSR recording | fgain |  |  | 70 |  |  | 63 |  |  | 60 |  |  | 60 | R |
| 04:08 | Reset offset freqs (kHz): X carrier to +6000; S carrier to +2500. Echoes should appear at -6000, -2500, respectively | FRO | 29 |  | -10 | 28 |  | -4 | 28 |  | -4 | 32 |  | -10 | R |
| 04:10 | RCP ND's ON |  | 39 |  |  | 34 |  |  | 32 |  |  | 35 |  |  | R |
| 04:16 | CLR's=LCP; S-band carrier gone |  | 27 |  |  | 33 |  |  | 32 |  |  | 29 |  |  | R |
| 04:18 | LCP ND's on |  | 27 |  |  | 32 |  |  | 32 |  |  | 37 |  |  | R |
| 04:24 | CLR's=RCP; S-band carrier reappears |  | 27 | 64 |  | 28 | 47 |  | 27 | 47 |  | 36 | 45 |  | R |
| 04:38 | Asmar questions whether S-LCP feeds RSR2A |  | 22 | 65 |  | 28 | 47 |  | 27 | 47 |  | 36 | 44 |  | R |
| 04:51 | DSS 43 confirms SLCP feeds RSR2A |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 05:05 | X carrier down; S carrier gone. Slew start early? X carrier remains very close to +6 kHz, since FRO entered. |  |  | 34 |  |  | N/A |  |  | N/A |  |  | 27 |  | R |
| 05:08 |  |  | 25 | 33 |  | 27 | 19 |  | 27 | 19 |  | 35 | 27 |  | R |
| 05:10 | DSS confirms RCP ND's on. No carrier visible in any channnel |  | 26 |  |  | 32 |  |  | 31 |  |  | 35 |  |  | R |
|  | rsops2 not connected to local printer; Aseel working on script to capture screen dumps |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 05:16 | CLR's=LCP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 05:17 |  |  | 26 |  |  | 27 |  |  | 27 |  |  | 36 |  |  | R |
| 05:20 |  |  | 26 |  |  | 32 |  |  | 31 |  |  | 36 |  |  | R |
| 05:23 | CLR's=RCP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 05:24 |  |  | 26 |  |  | 322 |  |  | 31 |  |  | 29 |  |  | R |
| 05:35 |  |  | 25 |  |  | 31 |  |  | 31 |  |  | 27 |  |  | R |
| 05:40 |  |  | 26 |  |  | 32 |  |  | 31 |  |  | 26 |  |  | R |
| 05:45 |  |  | 25 |  |  | 32 |  |  | 31 |  |  | 27 |  |  | R |
| 05:46 | X surface echoes appear; stronger in LCP than RCP. Hints of S-band echo. |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 05:50 | XLCP peak echo near -7500 Hz at ~8 dB above noise. XRCP echo relatively weaker, centered closer to -5000 Hz. S echo very transient |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
|  | Aseel's script is capturing screen dumps every ~10 s |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 05:56 | Echoes gone |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 05:59 |  |  | 25 |  |  | 32 |  |  | 31 |  |  | 26 |  |  | R |
| 06:20 | RCP ND's on |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 06:21 |  |  | 25 |  |  | ? |  |  | 31 |  |  | 26 |  |  | R |
|  | Somewhere around here the XRCP and SRCP windows containing ADC rms values were swapped. Problem wasn't discovered until 07:31. Should be possible to resolve by looking at RSR data. |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 06:25:10 | s/c TX off (not observed on Earth) |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 06:26 | CLR's to LCP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 06:27 | LCP ND's on |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 06:28 |  |  |  |  |  |  |  |  | 31 |  |  | 35 |  |  | R |
| 06:33 | CLR's to RCP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Asmar sends pair of Aseel's digital X-band plots to Pätzold |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 06:36 | Weak XRCP carrier visible at +7574 Hz; intermittent XLCP carrier at +5786 Hz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 06:39 |  |  | 27 |  |  | 17 |  |  | 26 |  |  | 35 |  |  | R |
| 06:46 | X-band telemetry in lock |  | 27 |  |  | 18 | N/A |  | 26 | N/A |  | 35 | 33 |  | R |
| 06:48 | End RSR recording |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | DSS 43 reports X-band lock throughout bistatic period, but unable to lock at S-band |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 07:00 | Pätzold returns plots embedded in Powerpoint file for review before taking to press conference |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 07:01 |  |  | 26 | 61 |  | 18 | N/A |  | 26 | N/A |  | 35 | 33 |  |  |
| 07:16 |  |  | 27 |  |  | 18 |  |  | 26 |  |  | 35 |  |  |  |
| 07:17 | Begin 3-W with New Norcia; X-band carrier moves rapidly across the passband (several times) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 07:19 |  |  | 27 | 60 |  | 19 | N/A |  | 26 | N/A |  | 36 | 32 |  |  |
| 07:20 | End of track |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 07:21 | Begin RSR recording |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:23 |  |  | 28 | 59 |  | 27 | N/A |  | 29 | N/A |  | 30 | 35 |  | R |
| 07:29 | DSS 43 on cold sky |  | 27 |  |  | 26 |  |  | 28 |  |  | 29 |  |  | R |
| 07:31:10 | XRCP (only) ND on |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
|  | Discovered windows swapped (see 06:21). rms values after this should be correct |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:32 |  |  | 42 |  |  | 28 |  |  | 29 |  |  | 30 |  |  | R |
| 07:34 | XRCP ND off, SRCP ND on |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:35 |  |  | 29 |  |  | 33 |  |  | 34 |  |  | 32 |  |  | R |
| 07:36 | CLR's to LCP |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:37 | Antenna=cold sky |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:38 |  |  | 25 |  |  | 27 |  |  | 28 |  |  | 29 |  |  | R |
| 07:39 | XLCP (only) ND on |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:40 |  |  | 25 |  |  | 27 |  |  | 28 |  |  | 28 |  |  | R |
| 07:42 | XLCP ND off; SLCP ND on |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:43 |  |  | 25 |  |  | 33 |  |  | 33 |  |  | 21 |  |  | R |
| 07:45 | All diodes off; configuring for ambient loads |  |  |  |  |  |  |  |  |  |  |  |  |  | R |
| 07:46 |  |  | 78 |  |  | 82 |  |  | 85 |  |  | 69 |  |  | R |
| 07:47 | Temperatures of ambient loads (K) reported as | S1 S2 X1 X2 |  |  | 293.0 |  |  | 293.4 |  |  | 295.1 |  |  | 291.6 | R |
| 07:48 | End RSR recording |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 07:50 | DSS 43 (Delta) Crew recommends 2-1/2 hours for setup because of complexity of radio science pre-cals |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Review on 21 Jan

Station recommended 2-1/2 hour set up

Uplink at 70-m at X precludes reception at S.

Jose - Goldstone and Freily say X up and S/X down should be possible; maybe the crew did not understand the process.  Jesse will open a DR if it turns out to be a procedural problem; he will ask the crew to phone us on the meet me line.

Freily - 'retratced' means X only.  'Extended' means S/X down possible with either S or X up.  If 'retracted, would have X up and down, but the S is not reflected into the horn.  Noise Temp in 'extended is 1.0-1.5K higher.

Normal configuration is to 'retract' the dichroic plate for X-band up.  So need to put dichroic plate into 'extended.'  Jose says this should already be in the X-up, S/X-down configuration procedure; but it may not have been followed.

S band went away during LCP noise diode measurements.