Mars Express Bistatic Radar Experiment

Operations Plan and Report

25-26 February 2005

Summary

=======

DSN Antenna:                 43

Pass:                        637

Orbit:                       1430

Orbit Start Time:            2005-02-27T00:36:19 (SCET)

HGA Pointing:                Inertial

Specular Condition:          2005-02-27T02:00:00 (ERT)

Target:                      (57.33S, 38.61W, 3382 km) (see note at end)

(Argyre, SE rim)

Incidence/Reflection Angle:  61.64 deg

Slant Range:                 10373 km

Slew Angle:                  56.72 deg

Doppler (carrier, fd):       -18276 Hz

Doppler (echo, fr):            9731 Hz

Doppler Difference (fdd):    -28007 Hz

Earth-Mars Distance:         2.75685E11 m

Data Acquisition

================

The experiment was supported by DSS 43 staff at the Canberra DSN complex.  Also on site in Canberra were Dwight Holmes, Jose Valencia, and Tommy Thompson of JPL.  The support team at JPL included Gene Goltz, Danny Kahan, Art Freiley, and Dick Simpson; Essam Marouf (Cassini Radio Science Team) was present as an observer.

The experiment began with pre-calibration activities starting on 26 February at 21:45; the pre-cal was completed 45 minutes ahead of schedule.  The bistatic surface observations were collected in the interval 01:45-02:15.  There were conflicting schedules regarding DSS 43 support for MEX after bistatic radar; the post-calibration was completed and the RSR's stopped recording at 03:43 on 27 February.

Valencia, working with Holmes and the DSS 43 staff, had refined the calibration procedure tested on 21-22 February.  He distributed the new procedure at the beginning of the pre-cal period.  It included an explicit confirmation of channel assignment through staged connection of ambient loads at the beginning of the pre-cal and improvements to the DTT control of noise diodes.  There were no anomalies during the calibration or experiment periods, for which we can credit Valencia and the DSS 43 staff.

RSRs were configured as follows.

Table 1

--------------------------------------

RSR  Channel Mode  ATT FGAIN Operator

dB

----- ------- ---- ---- ----- --------

RSR1A  S-LCP   1-W auto   60    Kahan

RSR1B  X-LCP   1-W auto   60    Kahan

RSR2A  S-RCP   1-W auto   60    Goltz

RSR2B  X-RCP   1-W auto   60    Goltz

Subchannels were defined as follows:

Table 2

---------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          1 ksps   Used for seeking weak carrier signals

2          8 ksps

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording (able to capture both X-band

residual carrier and surface echo)

Predicts were provided by NSS and were for one-way operation.

Table 3 lists ADC RMS levels read from RSR displays during the experiment.  Times in hh:mm are in UTC from the RSSG wall clock, which appeared to be about 2 minutes fast; times in hh:mm:ss are from RSR displays.  For more accurate times, see the next section of this report on Amplitude Calibration.  Acronyms/abbreviations are explained below Table 3; "steps" are explained in more detail in the accompanying "procedures" document.

Table 3

------------------------------------------------------------------------------

TIME (ERT) RSR1A RSR1B RSR2A RSR2B                COMMENTS

2005-02-26 S-LCP X-LCP S-RCP X-RCP

RMS   RMS   RMS   RMS

---------- ----- ----- ----- -----  ------------------------------------------

22:30       28    28    29    28   Step 1: All RSRs to sky; ATT set by AUTO

22:35       28    89    29    89   Step 2: X to AMB

22:36       84    89    28    89   Step 3: SL(LNA2) to AMB

22:38       84    88    87    89   Step 4: SR(LNA1) to AMB

22:39                              Step 5d: Reset all RSR ATT using AUTO

22:40       29    29    29    30   Step 5e: All RSRs recording

22:45                              Step 5c: Ambient load temperatures:

S1=21.94C  S2=22.69C  X1=20.75C

22:46                              DSS 43 wx: overcast, 17C, 67% humidity

22:47                              Step 6: XR ND on

22:48       29    29    29    31

22:51                              Step 7: XR, XL to sky

22:52       30     7    29    12

22:57       29     7    29     7   Step 8: XR ND off

23:01       29    10    29     7   Step 9: XL ND on

23:07       29    30    29    30   Step 10: XR, XL to AMB

23:12                              Step 10c: Ambient load temperatures:

S1=22:06C  S2=22.81C  X1=20.62C

23:12       29    29    30    30   Step 11: XL ND off

23:16       29     7    30     7   Step 12: XR, XL to sky; SR ND on

23:18                              Simpson requests 10 min w/SL ND on

23:21                              DSS 43 makes "B" connection to RSR's so

they can monitor (but not control) the

open loop channels

23:27       29     7     9     7   Step 13: SR to sky

23:32       29     7     7     7   Step 14: SR ND off

23:37       30     7     8     7   Step 15: SL ND on

DSS 43 offers to stay here 10 min; accept

23:47        9     7     7     7   Step 16: SL to sky

23:49                              Step 17b: Ambient load temperatures:

S1=22.12C  S2=22.88C  X1=20.56C

23:52        8     7     7     7   Step 17: All RSRs to sky, all NDs off

23:53                              DSS 43 explains that it needs control of

SR LNA at beginning of track; otherwise

no configuration changes

23:59                              End of pre-cal; RSRs continue to record

2005-02-27

----------

00:10        8           8     8   XR subchannel 4 carrier at -28 kHz with

Pc/No=60 dB/Hz; XL at 30 dB/Hz

00:31        8     7     8     7

00:37:28                           XR FGAIN reset to 70

00:38:15                           XL FGAIN reset to 70

00:40:28                           XL FGAIN returned to 60

00:40:29                           XR FGAIN returned to 60

00:52:20                           X TLM off; S-band carrier appears

SR Pc/No=45 dB, SL Pc/No=12 dB

XR Pc/No=67 dB, XL Pc/No=42 dB,

XR histogram approximately 50% full scale

01:00                              XR, XL FRO set to +25400 Hz; carrier moves

to -28 kHz (subchannel 4)

SR, SL FRO set to +2750 Hz; carrier moves

to -4 kHz

01:02                              All FROs reset to 0

01:14                              DSS 43 confirms CONSCAN off

01:23        8     7     8     7   XR carrier dropping

01:24                              XR Pc/No=61, XL Pc/No=38, SR Pc/No=44

01:25                              Mini-cal Step 1: XR ND on

01:27        8     7     8    12

01:30        8     7     9     7   Mini-cal Step 2: SR ND on

01:33        8    10     8     7   Mini-cal Step 3: XL ND on

01:36       10     7     8     7   Mini-cal Step 4: SL ND on

01:39        8     7     8     7   Mini-cal Step 5: all NDs off (end)

01:41:10                           XL FRO set to +25400 Hz; no carrier seen

01:41:13                           SL FRO set to +2750 Hz; no carrier seen

01:41:15                           XR FRO set to +25400 Hz; no carrier seen

01:41:17                           SR FRO set to +2750 Hz; no carrier seen

01:45:00                           Start XR, XL subchannel; 4 RSR recording

01:49                              Visually confirmed FRO=0 from each display

01:55                              Possible X echo; near f=0, width = 1 kHz

01:58                              Faint XL echo near -200 Hz

02:00:27                           Fairly convincing XR echo centered on f=0

02:02:40                           Possible SR carrier and echo at f=+/-4 kHz

02:05                              No consistent echoes

02:15        8     7     8     7   Stop XR, XL subchannel 4 recording

02:16        8     7     8    12   Mini-cal Step 1: XR ND on

02:19        8     7     9     7   Mini-cal Step 2: SR ND on

02:23        8    10     8     8   Mini-cal Step 3: XL ND on

02:26       10     7     8     7   Mini-cal Step 4: SL ND on

02:29        8     7     8     8   Mini-cal Step 5: all NDs off

02:30                              All FROs set to 0

XR Pc/No=30 at f=-2900 Hz

SR Pc/No=17 at f=-1300 Hz

02:32:12                           XR Pc/No=33, SR Pc/No=25

02:37:32     8     7     8     8   HGA returned to Earth point

XR Pc/No=66.9, XL Pc/No=41.9

SR Pc/No=44.4, SL Pc/No=19.8

02:45                              DSS 43 agrees to begin post-cal at 03:00

02:58                               XR Pc/No=66.9, XL Pc/No=41.8

SR Pc/No=44.3, SL Pc/No=17.2

02:58:01                           LOS on all channels

03:11                              Going to zenith, after some confusion with

MEX ops over end of track

03:16       30    29    30    30   Post-cal Step 1: Ambient load temperatures

S1=21.44C  S2=22.62C  X1=18.18C

03:17       30    29    30    31   Post-cal Step 2: XR ND on

03:20       30    29    30    29   Post-cal Step 3: SR ND on

03:22                              DSS 43 confirms SR ND on

03:23       29    30    30    29   Post-cal Step 4: XL ND on

03:25       30    30    29    29

03:26       30    29    29    30   Post-cal Step 5: SL ND on

03:31        9     7     8     7   Post-cal Step 6: all RSRs to sky, SL ND on

03:32        8    10     8     7   Post-cal Step 7: XL ND on

03:35        8     7     9     7   Post-cal Step 8: SR ND on

03:38        8     7     7    12   Post-cal Step 9: XR ND on

03:41        8     7     7     7   Post-cal step 10: all NDs off

Ambient load temperatures:

S1=21.38C  S2=22.38C  X1=18.22C

03:43:00     8     7     8     7   Stop RSR recordings

AMB = ambient load

CONSCAN = conical scan tracking

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

NB = noise diode

No = noise power

Pc = carrier power

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

SL = S-LCP

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP

Amplitude Calibration

=====================

Data from the Pre-Calibration and Post-Calibration were used to determine the operating system temperature (Top) for each receiver channel at zenith.  The value of each noise diode was obtained by calibration against Top and the ambient load temperature Tamb, either directly or indirectly.  During the bistatic experiment, the (time varying) system temperature in each channel was obtained by comparison of the background radiothermal noise with the energy injected by the now-calibrated noise diode.

"Intervals" in Table 4 refer to the center times associated with 10 second average power spectra.  The data were processed in three segments.  Interval 1 was the center time (22:41:04) of the first spectrum in the pre-calibration segment.  Interval 475 was the time (01:15:04) of the first spectrum in the second segment -- a mini-calibration, the bistatic radar experiment itself, and a second mini-calibration.  Interval 913 was the time (03:10:04) of the first spectrum in the post-calibration segment.  Not all intervals are shown in Table 4; transition times and times when the system state was ambiguous were omitted.

Table 4XR

-------------------------------------------

Center Times    Intervals  Configuration

-----------------  ---------  -------------

Pre-Calibration (zenith)

------------------------

22:41:04-22:45:34     1-  28  AMB      X1=20.75 at 22:45

22:45:54-22:49:54    30-  54  AMB+ND

22:50:24-22:54:54    57-  84  SKY+ND

22:55:14-23:04:54    86- 144  SKY

23:05:14-23:14:54   146- 204  AMB      X1=20.62 at 23:12

23:15:23-23:29:54   207- 294  SKY

23:30:04-23:44:54   295- 384  SKY (power drifting up slightly)

23:45:04-23:59:54   385- 474  SKY      X1=20.56 at 23:49

Bistatic Radar (tracking)

-------------------------

01:15:04-01:22:54   475- 522  SKY + carrier

01:23:04-01:24:54   524- 534  SKY + sidelobes (slew)

01:25:04-01:27:54   536- 552  SKY+ND

01:28:14-01:30:54   554- 570  SKY

01:31:04-01:44:53   571- 654  SKY

01:45:04-02:11:54   655- 816  SKY (echoes)

02:12:03-02:14:53   817- 834  SKY

02:15:13-02:17:53   836- 852  SKY+ND

02:18:13-02:20:53   854- 870  SKY

02:21:03-02:27:53   871- 912  SKY

Post-Calibration (zenith)

-------------------------

03:13:54-03:15:14   936- 944  AMB

03:15:34-03:18:24   946- 963  AMB+ND   X1=18.19 at 03:16

03:18:44-03:28:54   965-1026  AMB

03:29:14-03:36:24  1028-1071  SKY

03:36:44-03:39:23  1073-1089  SKY+ND

03:39:43-03:42:53  1091-1110  SKY      X1=18.12 at 03:41

Table 4SR

-------------------------------------------

Center Times    Intervals  Configuration

-----------------  ---------  -------------

Pre-Calibration (zenith)

------------------------

22:41:04-23:14:53     1- 204  AMB      S1=????? at 22:45

23:15:23-23:24:54   207- 264  AMB+ND

23:25:14-23:29:54   266- 294  SKY+ND

23:30:14-23:59:53   296- 474  SKY

Bistatic Radar (tracking)

-------------------------

01:15:04-01:22:54   475- 522  SKY + carrier

01:23:04-01:27:54   523- 552  SKY + sidelobes (slew)

01:28:14-01:30:54   554- 570  SKY

01:31:14-01:33:54   572- 588  SKY+ND

01:34:04-01:44:53   589- 654  SKY

01:45:04-02:14:53   655- 834  SKY (echoes?)

02:15:03-02:17:53   835- 852  SKY

02:18:13-02:20:53   854- 870  SKY+ND

02:21:13-02:27:53   872- 912  SKY

Post-Calibration (zenith)

-------------------------

03:12:24-03:18:34   927- 964  AMB

03:18:44-03:21:24   965- 981  AMB+ND

03:21:54-03:27:24   984-1017  AMB

03:27:44-03:33:24  1019-1053  SKY

03:33:44-03:36:24  1055-1071  SKY+ND

03:36:44-03:42:53  1073-1110  SKY

Table 4XL

-------------------------------------------

Center Times    Intervals  Configuration

-----------------  ---------  -------------

Pre-Calibration (zenith)

------------------------

22:41:04-22:49:54     1-  54  AMB      X1=????? at 22:45

22:50:24-22:59:54    57- 114  SKY

23:00:04-23:04:54   116- 144  SKY+ND

23:05:24-23:09:54   147- 174  AMB+ND

23:10:13-23:14:53   176- 204  AMB

23:15:23-23:29:54   207- 294  SKY

23:30:04-23:44:54   295- 384  SKY (power drifting slightly higher)

23:45:04-23:59:54   385- 474  SKY

Bistatic Radar (tracking)

-------------------------

01:15:04-01:22:54   475- 522  SKY + carrier

01:23:04-01:27:54   523- 552  SKY + sidelobes (slew)

01:28:04-01:30:54   553- 570  SKY

01:31:14-01:33:54   572- 588  SKY+ND

01:34:14-01:36:54   590- 606  SKY

01:37:04-01:44:53   607- 654  SKY

01:45:04-02:14:53   655- 834  SKY (echoes)

02:15:03-02:17:53   835- 852  SKY

02:18:03-02:20:53   853- 870  SKY

02:21:03-02:23:53   872- 888  SKY+ND

02:24:13-02:27:53   890- 912  SKY

Post-Calibration (zenith)

-------------------------

03:14:04-03:21:24   937- 981  AMB

03:21:44-03:24:24   983- 999  AMB+ND

03:24:34-03:28:54  1001-1026  AMB

03:29:14-03:30:24  1028-1035  SKY

03:30:44-03:33:24  1037-1053  SKY+ND

03:33:44-03:42:53  1055-1110  SKY

Table 4SL

-------------------------------------------

Center Times    Intervals  Configuration

-----------------  ---------  -------------

Pre-Calibration (zenith)

------------------------

22:41:04-23:34:54     1- 324  AMB      S2=????? at ?????

23:35:04-23:44:54   325- 384  AMB+ND

23:45:14-23:49:54   386- 414  SKY+ND

23:50:13-23:59:53   416- 474  SKY

Bistatic Radar (tracking)

-------------------------

01:15:05-01:30:54   475- 570  SKY

01:31:04-01:33:54   571- 588  SKY

01:34:14-01:36:54   590- 606  SKY+ND

01:37:14-01:39:54   608- 624  SKY

01:40:04-01:44:53   625- 654  SKY

01:45:04-02:14:53   655- 834  SKY (echoes?)

02:15:13-02:20:53   836- 870  SKY

02:21:03-02:23:53   871- 888  SKY

02:24:13-02:26:53   890- 906  SKY+ND

02:27:13-02:27:53   908- 912  SKY

Post-Calibration (zenith)

-------------------------

03:13:24-03:24:24   933- 999  AMB

03:24:44-03:27:24  1001-1017  AMB+ND

03:27:44-03:30:24  1019-1035  SKY+ND

03:30:44-03:42:53  1037-1110  SKY

Error in HGA Targeting

======================

There was an apparent error in the targeting of the bistatic radar experiment.  A specular point target, originally chosen for the geometry which would apply at 2005-02-27T01:45:00 Earth received time (ERT), was shifted to 02:00:00.  In the experiment request sent to ESOC, the time was updated, but the target coordinates were not changed.  When the high-gain antenna (HGA) pointing maneuver was designed, the HGA was told to go to the old target at the new time.

To determine the high-gain antenna (HGA) pointing error, the geometry is calculated here.  Distances/vectors are in meters; angles are in degrees.

Constants:

Rp = 3.3897E+06       Radius of assumed spherical Mars

pi = 3.1416E+00

For reference, these are J2000 (Earth mean equator and equinox) vectors as derived by the Stanford program BSRGEOM.  They are valid for the geometry at 02:00:00 ERT; light time corrections have been included.  Only DOS is used in this calculation.  "Mars" here is the planet's center of mass.

DOD = [-6.8399E+10  2.4392E+11  1.0875E+11]     Mars to DSS 43

|DOD| = 2.7569E+11

DOS = [-8.2208E+06 -3.0494E+06 -8.6878E+06]     Mars to spacecraft

|DOS| = 1.2343E+07

DOP = [-2.7645E+06  1.5686E+06 -1.1777E+06]     Mars to specular point

|DOP| = 3.3897E+06

Target coordinates in Mars planetocentric fixed-body coordinates:

Correct specular point target at 02:00:00:

LAT1 = -55.989 deg

LON1 = -35.997 deg

DOP1A = [1.5339E+06 -1.1144E+06 -2.8098E+06]    Mars to correct target

|DOP1A| = 3.3897E+06

Incorrect target:

LAT2 = -57.330 deg

LON2 = -38.610 deg

DOP2A = [1.4298E+06 -1.1418E+06 -2.8534E+06]    Mars to wrong target

|DOP2A| = 3.3897E+06

Angular separation between these vectors (seen from center of Mars):

vsep(DOP1A,DOP2A) = 1.9642 deg

Difference between these vectors and its magnitude.  The separation is equivalent to about 2 degrees of longitude at Mars' equator.

DOP2A-DOP1A = [-1.0417E+05 -2.7420E+04 -4.3589E+04]

|DOP2A-DOP1A| =  1.1620E+05

Fixed Body to J2000 rotation matrix (valid for t0 = 2005-02-27T02:00:00 ERT):

| -8.8413E-01 -3.3830E-01  3.2229E-01 |

M = |  1.3881E-01 -8.4880E-01 -5.1017E-01 |

|  4.4615E-01 -4.0600E-01  7.9740E-01 |

Fixed body target vectors converted to J2000 at t0:

DOP1B = M'*DOP1A = [-2.7645E+06 1.5686E+06 -1.1777E+06]

|DOP1B| = 3.3897E+06

DOP2B = M'*DOP2A = [-2.6957E+06 1.6439E+06 -1.2320E+06]

|DOP2B| = 3.3892E+06

where  M' = transpose(M) = inverse(M)

Spacecraft to Target Vectors in J2000 coordinates:

DSP1B = DOP1B - DOS = [ 5.4563E+06  4.6180E+06  7.5101E+06]

|DSP1B| = 1.0368E+07

DSP2B = DOP2B - DOS = [ 5.5252E+06  4.6933E+06  7.4558E+06]

|DSP2B| = 1.0399E+07

Spacecraft to target unit vectors in J2000:

USP1B = norm(DSP1B) = [ 0.5263  0.4454  0.7243]

USP2B = norm(DSP2B) = [ 0.5313  0.4513  0.7170]

Angle between the unit vectors (error in HGA pointing):

vsep(USP1B,USP2B) = 0.6145 deg