Mars Express Bistatic Radar Experiment

Operations Plan and Report

06 July 2005

Summary

=======

DSN Antenna:                 43

Pass:                        767

Orbit:                       1894

Orbit Start Time:            2005-07-06T22:46:47 (ERT)

HGA Pointing:                Inertial

Specular Condition:          2005-07-06T23:18:00 (ERT)

Target:                      60.85S, 74.92E (S of Hellas)

Incidence/Reflection Angle:  64.92 deg

Slant Range:                 11550 km

Slew Angle:                  50.7 deg

Doppler (carrier, fd):       27755 Hz

Doppler (echo, fr):          11744

Doppler Difference (fdd):    16011

Earth-Mars Distance:         1.451E11 m

Data Acquisition

================

This experiment was supported by DSS 43 staff at the Canberra DSN complex.  The support team at JPL included Gene Goltz, Danny Kahan, and Dick Simpson.  In the NOPE area were Jose Valencia and Jesse Velasco.

There were some early problems establishing the voice network; Gene Goltz had these resolved by 18:55, only 10 minutes after the beginning of the setup period.

The DSS 43 receiver configuration seemed somewhat unstable throughout the experiment.  According to operators at DSS 43, the X-band microwave configuration, which is usually automatic, was not correctly set initially; when commands were issued to the X-band noise diode controller, they were not executed.  By using "lower level" UWV commands the operators  were able to force the proper configuration; but these UWV commands had to be issued repeatedly throughout the activity.  In fact, the pre-cal was restarted after the first hour so that a more continuous set of measurements could be obtained.  The problems were documented in DR C104458.

The set up period began at 18:45.  DSS 43 announced that it was ready to begin the pre-calibrations at 19:25.  Because of the UWV configuration problems, the pre-calibrations were restarted at about 20:15; they then moved more-or-less smoothly to completion at 21:35.  The antenna was tracking the spacecraft by 21:45 and operators reported both S- and X-band closed loop receivers in lock at 21:52.  The spacecraft transmitted an unmodulated carrier toward Earth at both S- and X-band until about 22:37 (ERT), when it slewed to the BSR inertial pointing attitude.

For the BSR observation an X-band frequency offset of -13 kHz moved the carrier to about +10 kHz in the ±12.5 kHz RSR bandwidth; an S-band offset of -3.5 kHz moved that carrier to about +2.5 kHz.  Good X-RCP and X-LCP echoes were seen in real time displays for about 15 minutes centered on 23:18.  The X-band echoes were at about -6.5 kHz and reached a maximum 30 dB/Hz in RCP and 27 dB/Hz in LCP.  Convincing S-RCP echoes were seen at about -2.5 kHz, but no reliable estimates of strength were obtained in real time.  No S-LCP echoes were observed in real time, but they have been identified in quick-look output at Stanford.  Mini-calibrations were performed during the HGA slew periods using the noise diode sources; both mini-calibrations appear to have been successful.

There was no spacecraft bistatic radar calibration (BCAL) after the experiment because of time constraints.  The ground system post-calibration began at about 00:10 and was completed at 00:42.  Except that the X-band noise level appeared to be significantly higher (both polarizations) than during the pre-cal, these measurements appeared to be nominal.  Light rain had been reported during the pre-cal; although the sky was described only as "overcast" for the post-cal, the humidity had increased and the difference is consistent with a weather change.  A better picture of the X-band noise question may emerge from the more detailed data processing which will be carried out at Stanford.

Jose Valencia adapted the calibration procedure and briefing message from the version that was used at DSS 43 in April.  He is planning to include more specific UWV configuration instructions in future messages.  He will also change "US" commands to "UG" commands; the former do not work at DSS 43.  DSS 43 also reported that the operator directive to turn CONSCAN off does not work as written in the procedure.

RSRs were configured as in Table 1:

Table 1

---------------------------------------------

RSR  Channel Mode  ATT FGAIN    Operator

dB

----- ------- ---- ---- ----- ---------------

RSR1A  S-LCP   1-W auto   60    Kahan

RSR1B  X-LCP   1-W auto   60    Kahan

RSR2A  S-RCP   1-W auto   60    Goltz

RSR2B  X-RCP   1-W auto   65    Goltz

RSR subchannels (SCHAN) were defined as follows:

Table 2

---------------------------------------------------------------------

Subchannel  Sample Rate  Comments

----------  -----------  ---------------------------------------------

1          1 ksps

2          8 ksps

3         25 ksps   Primary recording bandwidth

4        100 ksps   Backup recording

Table 3 lists ADC amplitude levels read from RSR displays during the experiment.  Where available, signal-to-noise ratios, frequency offsets, and other measurements are also listed. Times are in UTC read from a wall clock and may not reflect actual times when configurations changed.  "Steps" are as defined in the briefing message.  Acronyms and abbreviations are explained after Table 3.

Table 3

------------------------------------------------------------------------------

TIME (ERT)  RSR1A  RSR1B  RSR2A  RSR2B                COMMENTS

2005-07-06  S-LCP  X-LCP  S-RCP  X-RCP

ADC    ADC    ADC    ADC

(dB)   (dB)   (dB)   (dB)

---------- ------ ------ ------ ------ ---------------------------------------

18:30                                 Goltz seeking to establish voice net

18:55                                 Voice net operational

Pre-Calibration

19:25      -10.0  -10.2  -10.4  -10.0 Step 1: all receivers to sky

19:27       -9.9   -0.3  -10.3   -0.2 Step 2: X-band to AMB

19:28       -0.5   -0.3  -10.4   -0.2 Step 3: S-LCP to AMB

19:29       -0.4   -0.4   -1.5   -0.2 Step 4: S-RCP to AMB

19:30                                 Ambient Load physical temperatures:

DC01  S1=19.22C  S2=20.00C  X1=19.75C

DC02  S1=19.19C  S2=20.00C  X1=19.75C

19:31                                 Begin RSR SCHAN=3 (25 kHz) recording

-10.0   -9.6  -10.0   -9.7 Use RSR auto feature to set attenuators

19:32                                 Meteorological conditions:

T = 8.3C  H = 70.9%

Sky: overcast; light rain in area

19:35       -9.9   -9.6  -10.0   -9.7 Step 5: Reconfigure closed loop receivers

19:40                                 DSS 43 unable to link 12.5K noise diode

to X-band closed loop receiver

19:45                                 DSS 43 will reboot X-band receiver

19:52                                 DSS 43 working through some options in

attempt to clear controller problem.

19:53                                 Problem resolved by issuing "low level"

UWV command to assign ND controller to

receiver; usually this happens

automatically during initialization.

Will resume with Pre-Cal Step 5.

19:54      -10.0   -9.6  -10.1   -9.0 Step 5: Configure closed loop receivers

19:55       -9.8   -9.7   -9.9   -8.9 Step 6: X-RCP ND on

20:01                                 DSS 43 reports continuing problems; X-RCP

did not go back to the ambient load

20:05                                 DSS 43 will enter a "more permanent"

correction for the low level command

problem, then return to Pre-Cal Step 1

20:12                                 Valencia requests that operators use full

commands (per briefing message) rather

than short forms.  DSS 43 reports that

"US" commands in message must be

replaced by "UG" commands in Canberra

and that the CONSCAN OFF command in the

briefing message does not work at all.

20:17                                 DSS 43 reports it is ready at Step 1.

RSR operators reset attenuators using RSR

"auto" feature.

20:18       -9.8  -10.2  -10.4  -10.0 Step 1: All receivers to sky

20:19       -9.9   -0.3  -10.4   -0.2 Step 2: X-band to AMB

20:20       -0.5   -0.4  -10.4   -0.2 Step 3: S-LCP to AMB

20:21       -0.4   -0.3   -0.5   -0.3 Step 4: S-RCP to AMB

20:22                                 DSS 43 ambient load physical temperatures

DC01: S1=18.56C  S2=19.56C  X1=18.56C

DC02: S1=18.56C  S2=19.56C  X1=18.56C

Weather:

T=8.1C  H=71.7%

Sky: overcast, light rain in area

20:23                                 RSR operators reset attenuators using

"auto" feature

20:23      -10.0   -9.6  -10.2   -9.8

20:28      -10.0   -9.6  -10.2   -9.8 Step 5 successfully completed

20:30      -10.1   -9.6  -10.0   -9.0 Step 6: X-RCP ND on

20:35      -10.0  -21.2  -10.0  -15.5 Step 7: X-band to sky

20:40      -10.0  -21.1   -9.9  -21.4 Step 8: X-RCP ND off

20:41                                 DSS 43 unable to reset ND; attempting low

level command again

20:48      -10.0  -16.4   -9.9  -21.5 Step 9: X-LCP ND on

20:50      -10.0   -9.1  -10.0   -9.9 Step 10: X-band to AMB

DSS ambient load physical temperatures

DC01: S1=18.25  S2=19.31  X1=18.19

DC02: S1=18.31  S2=19.31  X1=18.12

20:55       -9.9   -9.7   -9.9   -9.7 DSS 43 reports that the ND controller has

been lost again; there is a crew change,

and the new crew will have to re-enter

the low level UWV command from time to

time.

21:01       -9.9  -19.2  -10.0  -20.7 Step 12: X-band to sky

21:06      -10.1  -19.1   -9.8  -20.8 Step 13: S-RCP ND on

21:10       -9.9  -19.0  -19.3  -20.7 Step 14: S-RCP to sky

21:16       -9.9  -19.0  -21.7  -20.8 Step 15: S-RCP ND off

21:21       -9.7  -19.0  -21.5  -20.8 Step 16: S-LCP ND on

21:25      -18.5  -19.1  -21.6  -20.7 Step 17: S-LCP to sky

21:30      -21.1  -19.2  -21.7  -20.8 Step 18: S-LCP ND off

DSS 43 ambient load physical temperatures

s1=17.94C  S2=18.81C  X1=17.75C

21:35                                 End of Pre-Calibration

Begin Tracking

21:42       -21.1  -18.8  -21.6  -19.9 ADC Amplitudes (dB)

50.24  64.28 Carrier to Noise ratio (dB/Hz)

-1130  -2147 Carrier offset from spectrum center (Hz)

21:52                                  FRO_x = -12300 puts carrier at ~10 kHz

DSS 43 reports both receivers in lock

21:53                     -1190  -2364 Carrier offset from spectrum center (Hz)

after resetting FRO_x=0

22:21                     -1325  -2862 Carrier offset from spectrum center (Hz)

22:29       24.38  36.37  49.88  68.45 Carrier to Noise ratio (dB/Hz)

-1355  -2971  -1350  -2950 Carrier offset from spectrum center (Hz)

22:30                                  Entered FRO_x = -12300, FRO_s = -3500

22:31                                  Reset FRO_x = -13000

22:32       26.18  37.22  50.13  67.75 Carrier to Noise ratio (dB/Hz)

+2319 +10007  +2137  +9998 Carrier offset from spectrum center (Hz)

-20.9  -16.9  -21.5  -17.2 ADC Amplitude (dB)

22:38       22.41  36.23  50.02  66.03 Carrier to Noise ratio (dB/Hz)

-5164   9960   2127   9964 Carrier offset from spectrum center (Hz)

-20.9  -16.6  -21.2  -17.0 ADC Amplitudes (dB)

Begin Mini-Cal #1 (simultaneous with HGA SLEW #1)

22:40       -20.9  -16.5  -21.2  -14.0 Step 1: X-RCP ND on

22:43       -20.7  -16.6  -19.0  -17.3 Step 2: X-RCP ND off, S-RCP ND on

22:46                            18.48 Carrier to Noise ratio (dB/Hz)

+9920 Carrier offset from spectrum center (Hz)

-20.7  -14.3  -21.1  -17.2 Step 3: S-RCP ND off, X-LCP ND on

22:48                                  Begin RSR SCHAN=4 (100 kHz) recording

22:49                            21.52 Carrier to Noise ratio (dB)

+9911 Carrier offset from spectrum center (Hz)

-18.3  -16.5  -21.2  -17.3 Step 4: X-LCP ND off, S-LCP ND on

22:52              16.05         21.45 Carrier to Noise ratio (dB/Hz)

+9902         +9900 Carrier offset from spectrum center (Hz)

-20.9  -16.5  -21.1  -17.2 Step 5: S-LCP ND off

22:53                                  DSS 43 confirms use of 12.5K ND, MFQ=ON

23:13                                  Hint of X-RCP echo at offset -6 kHz

23:16                25            20  Surface echo peak SNR (dB/Hz)

-6000         -6000 Surface echo frequency offset (Hz)

23:18                28     20     30  Surface echo peak SNR (dB/Hz)

-6000  -2200  -6000 Surface echo frequency offset (Hz)

23:20                27     19     30  Surface echo peak SNR (dB/Hz)

-5900  -2225  -5920 Surface echo frequency offset (Hz)

23:22                25             29 Surface echo peak SNR (dB/Hz)

-5705         -5776 Surface echo frequency offset (Hz)

23:26                                  Echo no longer visible

23:47       -20.5  -16.3  -20.7  -16.6 ADC Amplitudes (dB)

23:48                                  End RSR SCHAN=4 (100 kHz) recording

Begin Mini-Cal #2 (simultaneous with HGA SLEW #2)

23:48       -20.5  -16.4  -20.7  -13.8 Step 1: X-RCP ND on

23:51                             17.0 Carrier to Noise ratio (dB/Hz)

+9912 Carrier offset from spectrum center (Hz)

-20.5  -16.4  -18.5  -16.8 Step 2: X-RCP ND off, S-RCP NS on

23:54       -20.4  -14.2  -20.6  -16.8 Step 3: S-RCP ND off, X-LCP ND on

23:57       -18.3  -16.2  -20.8  -16.6 Step 4: X-LCP ND off, S-LCP ND on

00:01       -20.4  -16.3  -20.6  -16.3 Step 5: S-LCP ND off

Begin Post-Calibration

00:07                                  DSS 43 confirms EOT; will advise when

ready to begin post-cal measurements

00:08                                  Set FRO_x = 0, FRO_s = 0.

00:12                                  DSS 43 ambient load physical

temperatures; antenna to zenith

S1=16.69C  S2=17.19C  X1=16.94C

-10.3   -9.8  -10.1   -9.8 Step 1: All receivers to AMB

00:15       -10.2   -9.8   -9.9   -9.0 Step 2: X-RCP ND on

00:18       -10.2   -9.8   -9.8   -9.8 Step 3: X-RCP ND off, S-RCP ND on

00:21       -10.3   -9.1  -10.0   -9.8 Step 4: S-RCP ND off, X-LCP ND on

00:24       -10.0   -9.7  -10.0   -9.7 Step 5: X-LCP ND off, S-LCP ND on

00:27       -18.8  -15.5  -21.4  -15.6 Step 6: All receivers to sky

00:30       -21.3  -13.8  -21.4  -15.7 Step 7: S-LCP ND off, X-LCP ND on

00:33       -21.3  -15.6  -19.1  -15.7 Step 8: X-LCP ND off, S-RCP ND on

00:36       -21.4  -15.7  -21.5  -13.3 Step 9: S-RCP ND off, X-RCP ND on

00:39       -21.4  -15.5  -21.5  -15.9 Step 10: X-RCP ND off

DSS 43 ambient load physical temps

S1=16.62C  S2=17.19C  X1=16.88C

Weather conditions:

T = 9C   H = 80%

Sky: overcast

00:42                                  End RSR SCHAN=3 (25 kHz) recording

AMB = ambient load

BOT = Beginning of Track

CONSCAN = conical scan tracking

CW = continuous wave (carrier only)

EOT = End of Track

FRO = frequency offset

HGA = high-gain antenna

LOS = loss of signal

ND = noise diode

No = noise power

Pc = carrier power

S1 = ambient load for S-RCP

S2 = ambient load for S-LCP

SL = S-LCP

SR = S-RCP

TLM = telemetry

X1 = Ambient load for both X-band channels

XL = X-LCP

XR = X-RCP