DISR Data Software Companion Document

Version 1.0

28 September 2012

Contents

Introduction...	1

DISRSOFT...	2

Hardware Platform...	2

Contents of the IDL_PROGRAMS directory...	3

Flat Fields...	3

NEW_GSE...	3

Frequently used commands, routine or functions...	4

Some commonly used IDL utilities:	8

PTEST...	8

IR spectrometer g structure...	9

Example Program #1: DISR Image Display	13

Example program #2: Summary Listing of IR spectrometer data...	19

Details of IDL_PROGRAMS directory...	22

### Introduction...

The Descent Image & Spectral Radiometer (DISR) data from the Huygens probe is generally analyzed using 3 tools:

1)	Research Systems Incorporated (RSI)'s  Interactive Data Language (IDL),

2)	Microsoft Excel Spreadsheets, and

3)	Fortran

A collection of data manipulation routines has been developed in IDL for the DISR instrument, named DISRSOFT.  It allows easy access to the data.  In DISRSOFT there are commands to read the header and pixel data into IDL arrays, which can then be printed into tables or displayed as 2D plots, 3D surfaces, contours, or images by investigators using other, ad hoc, IDL routines.  Once extracted from the datasets analysis is often performed using Excel spreadsheets.  Examples of these spreadsheets exist in many of the IDL_PROGRAMS subdirectories.  Fortran was also occasionally used to reduce the DISR data, most notably for the radiative transfer models and descent simulations.

The DISR flight data volume is discussed in the document: "DISR XDR Data Archive Document.doc", which is in the Planetary Data System (PDS) archive.  In summary, the data is collected and organized by the instrument's Ground Support Equipment (GSE) into  External Data Representation (XDR) format datasets (generally one dataset per observation) which are stored in a particular directory structure.  This document discusses the software used to access and analyze that data.

### DISRSOFT...

DISRSOFT is a collection of IDL routines, developed by the project, to allow easy extraction, manipulation, and display of the DISR's XDR datasets.  A text document titled "DISRSOFT_DOC.rtf" exists in the IDL_PROGRAMS\OTHER\CAL_SOFT directory which describes the DISRSOFT concept and many of the associated IDL routines.  The document was initially very optimistic, purporting to "..describe everything necessary for the calibration of DISR...", however it does not.  Also, it was expanded to incorporate similar software for the Imager for Mars Pathfinder (IMP).  References to the IMP software can be ignored by the DISR user.  DISRSOFT_DOC does have a good description of the DISR header information, and the primary routines necessary to access the data.  It also describes how to 'install' the DISRSOFT routines into the IDL directory structure.

In general 'installing' DISRSOFT involves placing the routines in a known directory, and then directing IDL to that directory.  Here are the basic steps...

1) Copy the CAL_SOFT directory from \IDL_PROGRAMS\OTHER to the root directory of your machine (typically C:\).

2) Using a text editor, modify the idl_start.pro routine, found in the CAL_SOFT directory to add the location of your IDL routine depository to the path thustly:

!path = !path + {your idl repository directory}

As an example I typically use:  !path=!path+'C:\idl_programs\csee'

Note the added path must be in quotes.

3) In UNIX it is typically necessary to run the start program from the IDL prompt with the batch command @C:/CAL_SOFT/idl_start.pro.

In Windows, one can have the start program to automatically execute by adding it to the IDL preferences:

File -> Preferences -> Startup:

IDL Main directory = C:\RSI\IDL

Working Directory = C:\

Satrtup file = C:\CAL_SOFT\idl_start.pro

### Hardware Platform...

The software developed during the DISR program on three different platforms: HP Unix, Apple Macintosh and Windows PC.  Although many IDL routines transfer well from one platform to the other, no serious effort was made to keep these programs platform independent.  It may be necessary to change some lines of code to accommodate a platform other than the one the routine was developed on.

### Contents of the IDL_PROGRAMS directory...

The IDL_PROGRAMS directory is generally a collection of the IDL programs used for the analysis of the DISR data, organized by author.  There is no further sub-organization.   The IDL_PROGRAMS\OTHER subdirectory contains the DISRSOFT code (CAL_SOFT), the flat field values used in the DISR's on-board software, and the IDL code for the Windows based GSE program.

### Flat Fields...

The \IDL_PROGRAMS\OTHER\FLAT_FIELD directory contains the flat field information for each DISR imager.  The flight unit, which landed on Titan is DISR #3.  The files present the 'correction_factor', which is to be divided into the image, as described in 5.8 of the DISR Users' Guide.  This information is presented in 4 formats:

1)  The files with no extension are the raw correction_factor values in tabular form (corresponding to row and column of the specific imager).

2) The files with the ".txt" extension contain the same data plus imager identification information, and row & column headings.

3) The ".csv" files contain the same information in Comma Separated Variable format.

4) The ".disrsoft" files contain the same data plus the header information contained in the "...Header..." files in XDR format.

### NEW_GSE...

The 'new' gse program is the Windows based Ground Support Equipment data stream decoding software, which runs under IDL.  It takes the European Space Operations Center (ESOC) supplied data stream (i.e. file o500sd_.1h_), and produces the XDR formatted DISR datasets.  In order for the batch program (gse) to work correctly the files from the \IDL_PROGRAMS\OTHER\NEW_GSE directory must be copied to 'C:\idl_programs\new_gse (or modify the batch program).  Once this is done, one can follow the directions in "\IDL_PROGRAMS\OTHER\NEW_GSE\Instructions for new3.doc" to run the program.

### Frequently used commands, routine or functions...

Here are some of the most commonly used DISRSOFT commands:

d_read,dataset_name,h,p  ;reads the header and pixel information from the XDR formatted dataset (dataset_name) into arrays h & p respectively.

d_irread,dataset_name,h,p,g  ;reads the header, pixel & bin information from the XDR formatted IR spectrometer dataset (dataset_name) into arrays h, p & g respectively.

d_whelp	; help GUI

d_look		; image display GUI

Exposure=d_value(h,36)	; reads the value for the exposure time from the header structure, and places it in variable 'Exposure'.  d_value is also applicable to all other header entries:

| d_value |  | Name | Description |
| --- | --- | --- | --- |
| 0 |  | H_TYPE | Header type (D=DISR, I=IMP) |
| 1 |  | H_DIRECTORY | Directory file last stored in |
| 2 |  | H_FILENAME | Filename file was stored as |
| 3 |  | H_FILETIME | Time file was last written by D_WRITE |
| 4 |  | H_LENGTH | Length of header string array |
| 5 |  | H_DIMENSION | Number of dimensions in data |
| 6 |  | H_XSIZE | Number of columns |
| 7 |  | H_YSIZE | Number of rows |
| 8 |  | H_ZSIZE | Number of images |
| 9 |  | H_DATATYPE | Type of data |
| 13 |  | H_PURPOSE | Purpose of observation |
| 14 |  | H_SUBJECT | Subject of observation |
| 15 |  | H_DATE | Date observation made |
| 16 |  | H_ENGINEER | Engineer responsible |
| 17 |  | H_SITE | Site of observation |
| 18 |  | H_SET_NAME | Text description of data set |
| 22 |  | H_CCDTEMP | On chip CCD temperature in [K] |
| 23 |  | H_REF_TEMP | CCD electronics reference temperature (MPAE) |
| 30 |  | H_DETECTOR | detector type (CCD, IR, PHOTOMETER) |
| 31 |  | H_SENSOR_ID | sensor id number |
| 36 |  | H_EXPTIME | integration time [ms] for CCD measurement |
| 37 |  | H_IMAGE_TIME | start time of exposure |
| 50 |  | H_COORD_XL | image coordinates (lower x) |
| 51 |  | H_COORD_YL | image coordinates (lower y) |
| 54 |  | H_FILTER | filter in use |
| 62 |  | H_VACUUM | vacuum or not (yes or no) |
| 63 |  | H_OPTICS | additional optics on bench (MPAE) |
| 64 |  | H_TESTLAMP | external test lamp (MPAE) |
| 80 |  | H_GSE_REV | GSE revision creating data set |
| 81 |  | H_CONFIG_FILE | configuration file associated with data set |
| 82 |  | H_TEST_LOG | test log filename generating data |
| 83 |  | H_REC_BEG | first record of this data set in test log |
| 84 |  | H_REC_END | last record of this data set in test log |
| 85 |  | H_PIXEL_UNITS | units of pixels |
| 86 |  | H_SET_ID | data set id |
| 87 |  | H_SET_NUMBER | sequential number of this data set |
| 88 |  | H_MISSION_TIME | mission time in seconds |
| 89 |  | H_CYCLE_NUMBER | sequential numbering of cycles |
| 90 |  | H_CYCLE_TYPE | cycle type |
| 91 |  | H_SCEN_STEP | cycle criteria table entry number |
| 92 |  | H_SPM_FLAG | spectrophotometric flag |
| 93 |  | H_CCD_MEAS | number of CCD sets performed during cycle |
| 94 |  | H_IR_MEAS | number of IR sets performed during cycle |
| 95 |  | H_VIOLET_MEAS | number of violet sets performed during cycle |
| 96 |  | H_MEAS_TYPE | measurement type |
| 97 |  | H_AZIMUTH | azimuth at start of cycle |
| 98 |  | H_ALTITUDE | altitude at start of cycle |
| 99 |  | H_SPIN | spin rate at start of cycle |
| 100 |  | H_TARGET_AZ | target azimuth for measurement |
| 101 |  | H_ACTUAL_AZ | actual azimuth for measurement |
| 102 |  | H_LAMP_STATE | cal and surf lamp status |
| 103 |  | H_IR_STATUS | IR hardware status word |
| 104 |  | H_IR_FLAGS | IR sampling and compression flags |
| 105 |  | H_IR_CHP_TMPB | IR chip temperature (start) |
| 106 |  | H_IR_CHP_TMPE | IR chip temperature (end) |
| 107 |  | H_PRECHARGE | Average precharge voltage |
| 108 |  | H_IR_COL_TIME | IR collection time [ms] |
| 109 |  | H_NUM_ROT | number of region/rotations (IR) |
| 110 |  | H_NUM_REGIONS | number of regions (IR) |
| 111 |  | H_DC_OFFSET_U | DC Offset voltage for ULIS |
| 112 |  | H_DC_OFFSET_D | DC Offset voltage for DLIS |
| 113 |  | H_UIR_TGT_PRC | target %age for ULIS |
| 114 |  | H_DIR_TGT_PRC | target %age for DLIS |
| 115 |  | H_UIR_PRCTILE | %ile point used for ULIS |
| 116 |  | H_DIR_PRCTILE | %ile point used for DLIS |
| 117 |  | H_CCD_STATUS | CCD hardware status |
| 118 |  | H_DCS_STATUS | DCS hardware status |
| 119 |  | H_CCD_FLAGS | CCD flags |
| 120 |  | H_PROC_FLAGS | CCD processing flags |
| 121 |  | H_NUM_COL | number of columns transmitted |
| 122 |  | H_NULL_PIXEL2 | sum of null pixels (col 2) |
| 123 |  | H_NULL_PIXEL3 | sum of null pixels (col 3) |
| 124 |  | H_CCD_TGT_PRC | target %age for CCD |
| 125 |  | H_CCD_PRCTILE | %ile point for CCD |
| 126 |  | H_STP_CNT_COL | strip centre column |
| 127 |  | H_STP_FST_COL | 1st column of strip |
| 128 |  | H_CAL_TMP_SORS | cal. source voltage |
| 129 |  | H_CCDLUG_TEMP | CCD thermal lug temperature [K} |
| 130 |  | H_STRAP_TEMP | thermal strap temperature |
| 131 |  | H_OPTICS_TEMP | conduit housing temperature |
| 132 |  | H_VIOLET_TEMP | violet detector temperature |
| 133 |  | H_SH_AUX_TEMP | sensor header aux board temperature |
| 134 |  | H_SH_BOX_TEMP | sensor header box temperature |
| 135 |  | H_EA_BOX_TEMP | EA box temperature |
| 136 |  | H_AUX_BRD_VOLT | divided 12V in volts |
| 137 |  | H_CPU_BRD_VOLT | divided 5V in volts |
| 138 |  | H_ADC_OFFSET | 0V input; ADC offset |
| 139 |  | H_ADC_GAIN | 2.5 input; gain of ADC |
| 140 |  | H_DISPQ_SIZE | max. dispatcher queue size |
| 141 |  | H_ALRMQ_SIZE | max. alarm queue size |
| 142 |  | H_TLMQ_SIZE | max. TM queue size |
| 143 |  | H_SCIPRQ_SIZE | max science processing size |
| 144 |  | H_STACK_SIZE | max stack size |
| 145 |  | H_CAL_SCENARIO | cal. scenario number |
| 146 |  | H_CCD_REP | CCD cal. repetition number |
| 147 |  | H_IR_REP | IR cal. repetition number |
| 148 |  | H_VIOLET_REP | violet cal. repetition number |
| 149 |  | H_SHUTTER_REP | shutter test rep. number |
| 150 |  | H_SHUTTER_CYC | number of shutter cycles |
| 151 |  | H_DCS_REP | DCS cal. repetition number |
| 152 |  | H_COMP_RATIO | compression ratio |
| 153 |  | H_HEATER_REP | heater test rep. number |
| 154 |  | H_HEATERS | which heaters |
| 155 |  | H_CAL_LAMP_REP | cal. lamp repetition number |
| 156 |  | H_NUM_BINS | number of IR bins for data collection |
| 157 |  | H_SURF_LAMP_REP | surface lamp rep. number |
| 158 |  | H_SUN_LAMP_REP | sun sensor LED rep. number |
| 159 |  | H_CAL1_VOLT1 | voltage on cal. lamp 1 |
| 160 |  | H_CAL1_CURR | current on cal. lamp 1 |
| 161 |  | H_CAL2_VOLT1 | voltage on cal. lamp 2 |
| 162 |  | H_CAL2_CURR | current on cal. lamp 2 |
| 163 |  | H_CAL3_VOLT1 | voltage on cal. lamp 3 |
| 164 |  | H_CAL3_CURR | current on cal. lamp 3 |
| 165 |  | H_SURF_VOLT1 | voltage on surface lamp |
| 166 |  | H_SURF_CURR | current on surface lamp |
| 167 |  | H_DCS_TST_STAT | overall DCS test status |
| 168 |  | H_DCS_SLF_STAT | DCS self test status |
| 169 |  | H_DCS_SW_STAT | DCS s/w test status |
| 170 |  | H_SUN_LED_VLT1 | voltage on Sun sensor LED |
| 171 |  | H_SUN_LED_CURR | current on Sun sensor LED |
| 172 |  | H_SUN_RESP | Sun sensor reading with LED on |
| 173 |  | H_NUM_HEAT | number of heaters tested |
| 174 |  | H_NUM_TRIPLET | number of sun triplets in data set |
| 175 |  | H_NUM_TIME_PAIRS | number of time data pairs |
| 176 |  | H_DUMP_START | address of first word in dump |
| 177 |  | H_DUMP_LEN | number of words in dump set |
| 178 |  | H_DUMP_FLAG | packing flag |
| 179 |  | H_MESSAGE | message type code |
| 180 |  | H_MESSAGE_ID | additional information code |
| 181 |  | H_NUM_BAD | number of bad ranges in RAM or EEPROM |
| 182 |  | H_LOTS_BAD | flag - lots bad RAM or EEPROM areas |
| 217 |  | H_OBJECTIVE | Objective of test |
| 218 |  | H_DUMMY | Flag for dummy detector |
| 219 |  | H_MODEL | DISR model for MMC |
| 222 |  | H_SQRT_MIN | Minimum value for sqrt table |
| 223 |  | H_SQRT_MAX | Maximum value for sqrt table |
| 225 |  | H_SUN_SOURCE | source of spin data |
| 226 |  | H_OGSE_STATUS | status of OGSE |
| 227 |  | H_OGSE_MSG | last msg from EGSE displayed on OGSE |
| 228 |  | H_OGSE_LAMP | lamp current |
| 229 |  | H_OGSE_SUNFILE1 | path of sun pulse file |
| 230 |  | H_OGSE_SUNFILE2 | path of sun pulse file |
| 231 |  | H_OGSE_SAMP | sun amplitude current |
| 232 |  | H_OGSE_SUNTABLE | sun table |
| 233 |  | H_OGSE_RPM | sun pulse RPM |
| 234 |  | H_OGSE_SPAN | sun pulse span value |
| 235 |  | H_OGSE_SIDEC | Si detector reference |
| 236 |  | H_OGSE_GEDEC | Ge detector reference |
| 237 |  | H_OGSE_EXTDEC | external detector reference |
| 238 |  | H_OGSE_5V | 5V reference |
| 239 |  | H_OGSE_TEMP | internal temperature |
| 240 |  | H_OGSE_SSS_TEMP | sun sensor stimulator temp. |
| 241 |  | H_OGSE_GN | analog ground noise |
| 255 |  | H_MONO_WAVL | Monochromator wavelength [nm] |
| 256 |  | H_MONO_SI | Monochromator Si detector reading |
| 257 |  | H_MONO_GE | Monochromator Ge detector reading |
| 258 |  | H_MONO_FLTR | Monochromator filter |
| 259 |  | H_MONO_G | Monochromator gain |
| 260 |  | H_MONO_RT | Monochromator response time [s] |
| 261 |  | H_MONO_GRAT | Monochromator grating |
| 262 |  | H_MONO_TUR | Monochromator turret number |
| 263 |  | H_SPSI | Sphere Si detector reading |
| 264 |  | H_SPFLSI | Sphere filtered Si reading |
| 265 |  | H_SPINGAS | Sphere InGaAs detector reading |
| 266 |  | H_SP_DETTMP | Sphere detector temperature |
| 267 |  | H_COSI | Collimator silicon detector reading |
| 268 |  | H_COFLSI | Collimator filtered Si reading |
| 269 |  | H_COINGAS | Collimator InGaAs detector reading |
| 270 |  | H_COTMP | Collimator detector temperature |
| 271 |  | H_PLMINGAS | Palmer InGaAs detector reading |
| 272 |  | H_PLMTMP | Palmer detector temperature |
| 278 |  | H_CPGASTEMP | Temperature of SH internal purge gas |
| 279 |  | H_AMBTEMP | Ambient temperature of clean room |
| 280 |  | H_SPTEMP | Temp[erature of gas in sphere |
| 281 |  | H_BOXTEMP | Temperature of gas in dry box |
| 282 |  | H_CHMBTEMP | Temperature in environment chamber |
| 286 |  | H_CAL_EL | Sensor head elevation |
| 287 |  | H_CAL_AZ | Sensor head azimuth |
| 288 |  | H_CAL_POL | Collimated beam polarizing angle |
| 289 |  | H_CAL_SHUT | Calibrator high intensity shutter state |
| 290 |  | H_LAST_CALTIME | Time of last cal. log entry |

A more complete listing of the DISR header entries exists in the archive under:

\IDL_PROGRAMS\OTHER\CAL_SOFT\Headers2.xls

### Some commonly used IDL utilities:

average = mean(array)	; returns the average value of an array

short_string = sstr(long_string)	; strips leading and trailing spaces from a string

time=hmsplus3(seconds)	; converts seconds to string of Hours:Min:Sec.XXXX

nsecs=seconds(hms)	; converts string in the form Hrs:Min:Sec to decimal seconds

path	: prints out the directories in the current path

dir	; prints the current directory contents

up	; moves the current directory up one level

array_sort,array	; rearranges array into ascending order.

filtzero,a,b,n	; removes the common 0 elements of a & b and returns resulting size, n.

thumbnails2,log	;  creates postscript thumbnails of the images in log (from DB2).

SingleImages3,log	; creates jpg, png & hist. equalized files of images in log.

@reset		; closes all files and resets parameters, echoing current directory.

### PTEST...

PTEST is short for Probe Testing.   The ptest, ptestUNIX and ptestPC batch routines were designed to get rapid instrument status and health during the cruise phase testing.  These routines are hardware platform specific, with ptest and ptestUNIX being designed for HPUX machines and ptestPC (most recent) modified to work on Windows platforms.  The ptest programs are interactive and call the following other IDL routines:

Routine	Output

thumbnails.pro	Prints thumbnail pictures of all the images. (.\PS\thumbnails.ps)

tripletfiles.pro	Creates jpeg, png and histogram equ. files of the triplets (.\triplets)

SingleImages.pro	Creates jpeg, png and histogram equ. files of the images (.\Images)

plot_temps.pro	Creates the time-ordered lists (voltages, temps, etc) & plots temperatures (plot_temps.out)

sun_sensor.pro	Tabularizes the pulse time, amplitude & spin rate for each rotation. (.post\anal_results\sun_pulses)

idx_check.pro	Time of first & last packets, Test duration, # of packets. (idx_check.out)

telem_packet_checker.pro	Reports time & # of  lost packets. (telem_packet_ck.out)

plot_rate.pro	Plots the telemetry rate, altitude & spin vs. mission time. (telem_alt_spin_rate.out)

check_times.pro	Checks for missing or erratic DDB times. (.\time_checker.out)

cycles.pro	Summarizes the # of each type of cycle & lists spin and altitude. (cycles.out)

cycle_type_vs_alt_plot.pro	Plots & tabularizes the cycle progression vs. altitude. (cycle_types.out)

plot_spin.pro	Plots & tabularizes the spin rate vs. mission time. (spin_profile.out)

plot_alt.out	Plots & tabularizes the altitude vs. mission time. (alt_profile.out)

ds_summary3.pro	Creates a summary of the contents of the datasets. (DS_Summary)

time_checker.pro	Creates a report of time discrepancies. (time_checker.out)

count_DB_files.pro	Lists the number of each type of Data Base files. (DB_file_count.out)

resource.pro	Tallies the usage of the limited life items. (lamps & shutter) (resource.dat)

ccdstat.pro	Examines the CCD error flags for every CCD measurement.

lamplist.pro 	Summarized the time and duration of lamp activations. (lamplist3.out)

lampdetail.pro	Lists the voltage and current  for every lamp activation. (lamp_detail.out)

plot_drift.pro	Plots the clock drift vs. mission time. (clock_drift.out)

plot_time.pro	Plots the progression of the DISR and DDB time. (clock_time.out)

plot_tolist.pro	Plots all the parameters (voltages, temperatures, etc) from the TOL's.

sun_sensor_history	Plots the progression of the Sun Sensor amplitude vs time.

sun_lamp_history	Plots the Sun Sensor Stimulator LED power & associated counts (sun_lamp_history.out)

PTEST is run from the test log level (i.e. in the directory containing DB and/or DB2).  The output from these routines are typically deposited into the test log under examination, and subsequently copied into the .\post\anal_results directory (in new directory: 'ptest').  One particularly valuable output file is DS_Summary, which is a chronological ASCII text listing of all the datasets collected.

Below are presented two example programs used to manipulate DISR data. The first interactively displays the DISR images in the data log, and the second prints out an ASCII list summarizing the IR spectrometer datasets.

### IR spectrometer g structure...

The following is a rudimentary explanation of the IR spectrometer's 'g' data structure:

Besides having a header, the IR spectrometer data also contains a data structure with information on the azimuth at which the data was taken.   There are 3 fundamental members to the IR g structure:

1) "Regions" or Regions Table (in the archive) defines the shape of the data collection bins (regions) in azimuth space and  which bin (region) has ULVS or DLVS data. (member g.regions)

2) "Reading" or Reading Table chronologically lists the IR data accretion by rotation number and region (bin); giving mission time, Collection Time, Shutter Time & Sample Time for each accumulation. (member g.reading)

3) "Bins" or Bins Table relates the datasets pixel information (in the data table) to the bins (regions). For each column (in the archive data table), Bins tell whether the data is ULIS, DLIS, shutter open or shutter closed, plus the total number of samples & collection time for each bin.  (member g.bins)

"Regions" is a 5 by N array where N is the number of regions each rotation is divided into (typically 1 or 8).  Each line contains the following 5 elements:

(0,x) = Region number.  Usually equal to x+1 (where x goes from 0 to N-1)

(1,x) = Start azimuth in 100th's of degrees.* Az_begin = g.regions(1,x)/100.0

(2,x) = Ending azimuth in 100th's of degrees.* Az_end = g.regions(2,x)/100.0

(3,x) = Up bin index.  Identifies bin that ULIS data will be summed into

(4,x) = Down bin index.  Identifies bin that DLIS data will be summed into

In the archive data the Regions table is arrange in 5 columns by N rows.  Typically the DLVS is collected in 8 regions and the ULVS is collected in 4 regions.

"Reading" is a 6 by N array, where N is the product of the number of rotations completed and the number of regions (bins) used per rotation (i.e. 8 bins & 2 rotations yields 16 elements).

Each line contains the following:

(0,x) = Rotation number (1-N)

(1,x) = Region of rotation used. This often does NOT start with 1.

(2,x) = Mission time at start of the rotation/region read in 10,000th's of a second.

Mission time (sec) = g.reading(1,x)/10000.0

(3,x) = IR duration (collection time) in this rotation/region.

Duration (msec) = g.reading(3,x)*8.064

(4,x) = IR shutter period for this rotation/region. This is composed of period/2 closed, followed by period open, followed by period/2 closed in each shutter cycle.  There is also a 16.128 msec shutter transition wait in between each open/close and close/open change.

(5,x) = IR sample time.  This is the time to use to normalize all IR data into counts per second (equivalent to exposure time). Sample time (msec) = g.reading(5,x)*8.064

The shutter period should be an integer multiple of the sample time to assure proper IR operation.

In reading, the transform between duration (collection time), period (shutter time), and cycles is: :

Cycles = (duration(raw) - 2)/(2 * period(raw) + 4) = (g.reading(3,x) - 2) / (2 * g.reading(4,x) + 4)

Duration (msecs) = ((period(raw)*2*cycles + 4*cycles + 2)*8.064 msec

where (raw) is the number of 8.064 ms steps from the g.reading table, and cycles is the number or repetitions of the basic collection cycle (closed, open, closed).

The number of shutter cycles in a collection is not stored in the reading array, and must be deduced from the above equation.

"Bins", is a 6 by N array, where N in the number of columns of data in the pixel (data) array.  It is not unusual for there to be a gap between the highest down bin number and the lowest up bin number (g.bins(0,*)).

Each line contains the follow entries:

(0,x) = Bin number. This is NOT a continuous sequence.

(1,x) = DLIS or ULIS bin. 0 = DLIS (down bin), 1 = ULIS (up bin)

(2,x) = IR shutter open or closed. 1 = closed, 0 = open

(3,x) = Total shutter open integration time over all rotations for that bin (region) in 10,000ths of a second. Total time (sec) = Bins (3,i)/10000.0. Since the datacontained in Bins (5,i) are four times the average counts in all the reads producedby the French digital output, not the total counts divided by the total integrationtime, do NOT divide the data numbers by Bins (3,i) to determine counts persecond. Counts/sec is obtained by dividing the data by the average sample timedefined below.

(4,x) = Total number of samples taken with shutter open for that bin (region)

g.bins(4,x) = summ(all rotations) of period*cycles/sample

(5,x) = Column number of the pixel array that corresponds to this bin.

p(*,g.bins(5,x) contains the averaged data for bin g.bins(0,x)

* Azimuths are defined as CCW, viewed from above,  relative to the sun.

Note that the data recorded for each pixel in each region with the shutter closed or open is the average data number. The average sample time is the total collection time divided by the total number of samples taken on all rotations for that region, or Bins (3,i)/Bins (4,i). Thus the net count rate, DN/sec is:

DN/sec = (data value closed – data value open)/ [Bins (3,i)/Bins (4,i)]

### Example Program #1: DISR Image Display

pro images_ex,log

; CSee, 2012.07.16

; This program displays the images in data directory: log.

; It is to be run from the Log level (i.e. the directory containing DB).

db='DB2'	;DB for UNIX data or DB2 for Windows data

print,''

print,'This program prints images frames from the specified log to the screen.'

print,'The default is the current test log.'

cd,'',current=cdir & cd,cdir        ;the current directory is the default log

if n_params() eq 0 then log = cdir+'\'  ;test for # of input parameters

if strmid(log,0,/reverse_offset) ne '\' then log=log+'\'	;add final '\' if missing

print,''

print,'The operant Test Log is: ',log

;____________________________________________________________________________

;List Files...

cd,log+db+'\Image\',current=cdir

files=file_search()

cd,cdir

s=size(files)

nfiles=fix(s(1))

numfiles=sstr(nfiles)          ;numfiles=short string (nfiles)

if files(0) eq '' then begin & print,'No files found' & goto,exit & endif

print,'The number of Images in this log is: ',sstr(nfiles)

;____________________________________________________________________________

;Initialize...

auto=1    ;for auto=1 tvscl

min=0     ;the tvscl min setting

max=4095  ;the tvscl max setting

ilast=0   ;ilast is the previous value of i

ff=-1     ;flag for flat fields, 1=>enabled, -1=>disabled

menu:

print,''

print,'Enter  to...              Enter  to...

print,'  0    Get this menu       -4    Autoscale, min to max

print,' -1    Quit the program    -5    Scale from min to 2 x average

print,' -2    Change minimum      -6    Print current image

print,' -3    Change maximum      -7    Toggle flat field	-8  Jpeg image.

;____________________________________________________________________________

;Loop that reads the desires...

again:

i=0    ;make i an integer

print,'Pick a file (from 1 to ',sstr(nfiles),') or choose menu (0): '

read,i               ;i=file index

if i eq 0 then goto,menu    ;display menu

if i eq -1 then goto, exit  ;end of program

if i eq -2 then begin      ;set minimum of stretch

auto=0

print,'Min = ', sstr(min)

read,'Enter new min: ',min

i=ilast

endif

if i eq -3 then begin      ;set maximum of stretch

auto=0

print,'Max = ',sstr(max)

read,'Enter new max: ',max

i=ilast

endif

if i eq -4 then begin       ;autoscale to max and min

auto=1

i=ilast

endif

if i eq -5 then begin        ;autoscale, range = minimum to 2 x average

auto=2

i=ilast

endif

if i eq -6 then begin   ;prints current image

set_plot,'ps'

device,filename = 'c:\idl.ps',/times,/portrait,xsize=7.5,ysize=9,yoffset=1.0,/inches,bits_per_pixel=8

if auto eq 1 then tvscl,bytscl(p,min=min(p),max=max(p),top=255) else $

tvscl,bytscl(p,min=min,max=max,top=255)  ;p>min<max

xyouts,0,-.02,typ+sstr(ilast)+'  Min= '+sstr(min(p))+', Ave= '+sstr(mean(p))+', Max= '+sstr(max(p)),/norm

xyouts,0,-.04,'Exposure (ms) = '+sstr(d_value(h,36))+'   lamps = '+sstr(d_value(h,102)),/norm

xyouts,0,1.02,'From Log: '+cdir,/norm

device,/close_file

spawn,'gsview32 c:\idl.ps'	;requires ghostscript viewer to print.

;set_plot,'x'   ;returns to X windows environment

set_plot,'WIN'   ;returns to X windows environment

print,string(10b),'*** Postscript file created as C:\idl.ps ***'

i=ilast

endif

if i eq -7 then begin   ;use flat fields

ff=-ff

i=ilast

endif

if i eq -8 then begin   ;create jpeg image

pout=bytscl(p,min=min,max=max,top=255)

outfile='C:/Image'+sstr(ilast)+'.jpg'

check_file=file_search(outfile,count=nfiles)

ans=''

if nfiles ne 0 then begin

read,outfile+' Exists ***, Replace?? ', ans

if ans ne 'y' then goto,skip_write

endif

write_jpeg,outfile,pout,quality=100

print,'*** Made jpeg image under C: ***'

skip_write:

i=ilast

endif

; if i eq -8 then begin   ;create png image

;   pout=p*21845.0/mean(p)  ;scale average up to 1/3 of 16 bits

;   sigma=stdev(pout,avep)

;   index=where(pout gt avep+4.0*sigma)

;   ;;print,min(pout),avep,max(pout),sigma

;   if index(0) eq -1 then goto,skip2

;   pout(index)=max(pout(where(pout le avep+4.0*sigma))) ;chops off histogram above 4 sigma

;   skip2:

;   minpt=min*21845.0/mean(p)>0

;   maxpt=max*21845.0/mean(p)

;   p_png=uint(65535d0*(double(pout)-double(minpt))/(double(maxpt)-double(minpt)))

;   outfile='C:/Image'+sstr(ilast)+'.png'

;   write_png,outfile,p_png

;   print,'*** Made png image under C: ***'

;  i=ilast

; endif

if i eq -10 then stop	;for debugging

if i le 0 or i gt nfiles then begin    ;for i input not in range

print,'Invalid value'

goto,menu

endif

;____________________________________________________________________________

;Read & present file...

d_read,log+db+'\Image\'+files(i-1),h,p

;determine image type and apply flat field if required...

type=d_value(h,96)

typ='Unknown'

model=d_value(h,219)   ;the model is needed to get the right flat field...

case model of

'DISR1': model='DISR#1'

'DISR2': model='DISR#2'

'DISR3': model='DISR#3'

else: model='Unknown'

endcase

if model eq 'Unknown' then begin

print,'There is no flat field for model: ',d_value(h,219)

ff=-1

endif

if type eq 21 then begin

typ='MRI '

if ff eq 1 then begin

;d_read,'\local\Imagers\Flat_Field\'+model+'\dli2_flat_field.disrsoft',hff,pff

d_read,'C:\idl_programs\Flat_Field\'+model+'\dli2_flat_field.disrsoft',hff,pff

if model eq 'DISR#1' then pff=pff/256.  ;DISR1 Flat field is wrong

p=p*pff		;removes flat field

endif

endif

if type eq 22 then begin

typ='SLI '

if ff eq 1 then begin

;d_read,'\local\Imagers\Flat_Field\'+model+'\sli_flat_field.disrsoft',hff,pff

d_read,'C:\idl_programs\Flat_Field\'+model+'\sli_flat_field.disrsoft',hff,pff

if model eq 'DISR#1' then pff=pff/256.   ;DISR1 Flat field is wrong

p=p*pff		;removes flat field

endif

endif

if type eq 23 then begin

typ='HRI '

if ff eq 1 then begin

;d_read,'\local\Imagers\Flat_Field\'+model+'\dli1_flat_field.disrsoft',hff,pff

d_read,'C:\idl_programs\Flat_Field\'+model+'\dli1_flat_field.disrsoft',hff,pff

if model eq 'DISR#1' then pff=pff/256.   ;DISR1 Flat field is wrong

p=p(*,2:255)*pff		;removes flat field

endif

endif

ilast=i

p2=rotate(p,2)		;rotate image 180 degrees so that up is up (p2).

s=size(p2)

;p3=rebin(p2,2*s(1),2*s(2))   ;,/sample)       ;doubles image size

x=2*s(1) & y=2*s(2)

p3=congrid(p2,x,y,/center,cubic=-0.5,/interp)       ;doubles image size (p3)

erase

if auto eq 2 then begin & min=min(p) & max=min([2*mean(p),4095]) & endif

if auto eq 1 then begin & min=min(p) & max=max(p) & endif

;tv,bytscl(p2,min=min,max=max,top=255)	;to make actual size jpegs

tv,bytscl(p3,min=min,max=max,top=255)

print,string(10b),cdir,'\Log\',db,'\',files(ilast-1)

print,typ,sstr(i),'  Min= ',sstr(min(p)),', Ave= ',sstr(mean(p)),', Max= ',sstr(max(p))

print,'Exposure (ms) = ',sstr(d_value(h,36)),'   lamps = ',sstr(d_value(h,102))

if ff eq -1 then print,'Model= ',model,'  Flat Field is included' $

else print,'Model= ',model,'  Flat Field is removed'

print,'Streach Settings = ',min,max

goto, again

;____________________________________________________________________________

;Done...

exit:

wdelete,0

print,'Done'

cd,cdir

end

### Example program #2: Summary Listing of IR spectrometer data...

pro ir_list_files,first

; This program prints out a summary list of the ir spectrometer measurements

; in the current directory.  It is to be run from the test log (i.e. the directory containing "DB").

; 'first' is the number of the first IR to read (default = 0)

; The output is place in the log as IR_list.out

if n_params() eq 0 then first = 0  ;i.e. begin with first IR in Log

cd,'', current=cdir & cd,cdir	     ;make cdir the test log directory

cd,cdir+'/DB2/Ir'

files=findfile('*_Ir',count=nfiles)

; Output data to root directory as IR_list.out

close,1

openw,1,'C:\IR_list.out'

printf,1,cdir

printf,1,string(10b),'There are ',sstr(nfiles),' IR files in this Log.'

printf,1,' * = Possibly Saturated Data, min(measurement) < 15000 dn'

printf,1,''

printf,1,'   N   IR    Time  altitude  Cycle  Rows  Type           Ave.     Max.   Lamp     Exp.   Collect   Rots Regns Min(p)   Temp.    Resol.   1 Rot.

printf,1,'        #     min     Km       #                          dn       dn              ms       s                  dn        K        Km       Km

printf,1,''

nn=0	; files counter

for i=first,nfiles-1 do begin

d_irread,files(i),h,p,g

siz=size(p)

seq=d_value(h,87)		;measurement sequence number

time=d_value(h,88)		;mission time in seconds

temp=(d_value(h,105)+d_value(h,106))/2.		;average IR temperature during measurement

collect=d_value(h,108)		;collection time in seconds

rows=d_value(h,7)		;number of data rows (spectra)

cycle=d_value(h,89)		;cycle number

alt=d_value(h,98)/1000.	;altitude in Km

lamps=''

lamps=d_value(h,102)		;lamp state (i.e. 0000)

g1=g.(1)				;Sample-time from structure g

rots=d_value(h,109)		;number of rotations

regions=d_value(h,110)		;number of IR regions

exp=g1(5)*8.064

pi=3.141592654

tt=tan(24.5*pi/180)-tan(15.5*pi/180)	;ratio of altitude to anulis thickness 9 deg at 20 deg

cir=pi*tan(20*pi/180)

sat=''

type=mtype(files(i))

typ='Unknown'

if type eq 8 then typ='DLIS'

if type eq 9 then typ='ULIS'

if type eq 10 then typ='Comb'

if type eq 11 then typ='Long   '

;for descent ir's...

if siz(2) eq 24 then begin

r=p(*,8:15)-p(*,0:7)   ;DLIS Closed-Open

aved=intarr(8)

for j=0,7 do aved(j)=mean(r(9:140,j))

if min(p(9:140,*)) le 15000 then sat=' * ' else  sat='   '

for j=0,7 do printf,1,nn,seq,time/60.,alt,cycle,rows,typ,j,aved(j),max(r(9:140,j)),lamps,exp,collect,rots,regions,min(p(9:140,0:7)),sat,temp,alt*tt,alt*cir, $

format='(i4,i5,f9.2,f9.2,i5,i7,3x,a," D-",i2,T54,f10.2,i8,2x,a4,f9.1, f10.2,2x,i4,2x,i3,i7,a3,f7.1,f11.2,f11.2)'

r=p(*,20:23)-p(*,16:19)        ;ULIS Closed-Open

aveu=intarr(4)

for j=0,3 do aveu(j)=mean(r(9:140,j))

if min(p(9:140,*)) le 15000 then sat=' * ' else  sat='   '

for j=0,3 do printf,1,nn,seq,time/60.,alt,cycle,rows,typ,j,aved(j),max(r(9:140,j)),lamps,exp,collect,rots,regions,min(p(9:140,0:7)),sat,temp,alt*tt,alt*cir, $

format='(i4,i5,f9.2,f9.2,i5,i7,3x,a," U-",i2,T54,f10.2,i8,2x,a4,f9.1, f10.2,2x,i4,2x,i3,i7,a3,f7.1,f11.2,f11.2)'

goto,next_file

endif

;for simple ulis or dlis files

r=p(*,1)-p(*,0)             ;Shutter Closed-Open.

if min(p(9:140,0)) le 15000 then sat=' * ' else  sat='   '

if type eq 10 then typ2=typ+' dn' else typ2=typ+'   '

printf,1,nn,seq,time/60.,alt,cycle,rows,typ,mean(r(9:140,*)),max(r(9:140,*)),lamps,exp,collect,rots,regions,min(p(9:140,0)),sat,temp,alt*tt,alt*cir, $

format='(i4,i5,f9.2,f9.2,i5,i7,3x,a,T54,f10.2,i8,2x,a4,f9.1, f10.2,2x,i4,2x,i3,i7,a3,f7.1,f11.2,f11.2)'

;for ircomb files...

if siz(2) eq 4 then begin

if min(p(9:140,2)) le 15000  then sat=' * ' else  sat='   '

r=p(*,3)-p(*,2)              ;Upward looking data for Combined reads

if type eq 10 then typ2=typ+' up'

printf,1,nn,seq,time/60.,alt,cycle,rows,typ,mean(r(9:140,*)),max(r(9:140,*)),lamps,exp,collect,rots,regions,min(p(9:140,2)),sat,temp,alt*tt,alt*cir, $

format='(i4,i5,f9.2,f9.2,i5,i7,3x,a,T54,f10.2,i8,2x,a4,f9.1, f10.2,2x,i4,2x,i3,i7,a3,f7.1,f11.2,f11.2)'

endif

next_file:

nn=nn+1

endfor

exit:

cd,cdir

print,cdir

print,'Done!'

end

### Details of IDL_PROGRAMS directory...

The following is a listing of the subdirectories contained in the IDL_PROGRAMS directory in the DISR archive.  The first number after the directory name is the number of subdirectories contained in that directory, and the second number is the quantity of files at that level.

IDL_PROGRAMS  (8 - 0)

-> BASHAR_RIZK   (15 - 0)

--|| Bashar   (0 - 2110)

--|| Prep Changes 1-14-05   (0 - 3)

--|| br   (0 - 3)

--|| cpe1   (0 - 21)

--|| gtsl1   (0 - 22)

--|| hp   (0 - 14)

--|| m4   (0 - 44)

--|| merge   (0 - 1)

--|| oc   (0 - 68)

--|| other   (0 - 13)

--|| prep   (0 - 41)

--|| specmap   (0 - 52)

--|| st2   (0 - 80)

--|| supersim   (0 - 12)

--|| table   (0 - 11)

-> CHUCK_SEE   (22 - 0)

--|| 2ndary   (0 - 1)

--|| Backups   (0 - 3)

--|| Erich's Kabs 2005   (1 - 0)

---||| Software   (1 - 0)

----|||| Spectra   (0 - 41)

--|| PDS   (8 - 29)

---||| BROWSE   (2 - 1200)

----|||| IMG   (0 - 0)

----|||| PNG   (0 - 1200)

---||| DATA   (13 - 0)

----|||| DARK   (2 - 0)

----|||| DESCENT   (2 - 0)

----|||| HKEEPING   (1 - 0)

----|||| IMAGE   (13 - 0)

----|||| IR   (3 - 0)

----|||| LAMP   (10 - 0)

----|||| SOLAR   (2 - 0)

----|||| STRIP   (2 - 0)

----|||| SUN   (1 - 0)

----|||| TIME   (4 - 0)

----|||| VIOLET   (7 - 0)

----|||| VISIBLE   (11 - 0)

----|||| VISIBLE_EXT   (11 - 0)

---||| DDP   (7 - 1)

----|||| DLIS   (0 - 6)

----|||| DLV   (0 - 5)

----|||| DLVS   (0 - 2)

----|||| Old   (0 - 8)

----|||| ULIS   (0 - 6)

----|||| ULV   (0 - 6)

----|||| ULVS   (0 - 2)

---||| DERIVED_DATA_PRODUCTS   (6 - 0)

----|||| DLIS   (0 - 6)

----|||| DLV   (0 - 4)

----|||| DLVS   (0 - 2)

----|||| ULIS   (0 - 6)

----|||| ULV   (0 - 4)

----|||| ULVS   (0 - 2)

---||| Junk   (0 - 2)

---||| Old_programs   (1 - 6)

----|||| PDS_23Apr06   (0 - 20)

---||| Out   (0 - 43)

---||| idl_programs   (0 - 17)

--|| SA_simulator   (4 - 66)

---||| Results   (0 - 4)

---||| Source and Unused Files   (2 - 29)

----|||| from lyn   (0 - 17)

----|||| to lyn   (0 - 2)

---||| picture of board equations approach   (0 - 12)

---||| test cases   (1 - 9)

----|||| disr3_cal.24Jul96.absresp_cold_24Jul96.4   (0 - 5)

--|| Surf_Images   (0 - 6)

--|| UNIX   (10 - 0)

---||| 2ndary   (0 - 1)

---||| PB_160   (1 - 1)

----||||  Programs   (6 - 94)

---||| cmdndata   (0 - 17)

---||| data   (0 - 59)

---||| des_cal_cycles   (0 - 13)

---||| hc_comp   (0 - 20)

---||| hkeeping   (0 - 34)

---||| ptest   (0 - 79)

---||| trash   (0 - 2)

---||| util   (0 - 68)

--|| VIMS   (1 - 1)

---||| idl   (5 - 3)

----|||| HST   (6 - 34)

----|||| VIMS data   (0 - 17)

----|||| VIMS_ir_Aug2007   (1 - 0)

----|||| VIMS_vis_Aug2007   (1 - 0)

----|||| namlists   (1 - 8)

--|| cmdndata   (0 - 17)

--|| data   (0 - 138)

--|| des_cal_cycles   (0 - 13)

--|| hc_comp   (0 - 20)

--|| hkeeping   (0 - 35)

--|| ir   (0 - 0)

--|| movie_complete   (1 - 222)

---||| jpegs   (0 - 103)

--|| other   (0 - 75)

--|| ptest   (0 - 78)

--|| radxfer   (0 - 2)

--|| temp   (0 - 0)

--|| thn   (0 - 7)

--|| trash   (0 - 2)

--|| util   (0 - 81)

-> LISA_MCFARLANE   (4 - 0)

--|| Archive_junk   (0 - 12)

--|| Lisa Programs   (1 - 1)

---||| PDS_prog_20Mar04   (1 - 14)

----|||| other   (0 - 1)

--|| Lyn programs   (0 - 6)

--|| PDS_prog_Feb04   (0 - 19)

-> LYN_DOOSE   (3 - 1)

--|| IR Simulator   (0 - 94)

--|| Lyns   (0 - 1)

--|| keycode   (0 - 3)

-> MICHAEL_BUSHROE   (2 - 1)

--|| Mike   (0 - 3)

--|| old   (2 - 0)

---||| batch   (6 - 0)

----|||| gse   (0 - 8)

----|||| new   (3 - 0)

----|||| old   (0 - 169)

----|||| panoramas   (0 - 14)

----|||| sharpening   (0 - 4)

----|||| specmap   (0 - 4)

---||| telemetry   (0 - 8)

-> MICHAEL_KUEPPERS   (1 - 0)

--|| SOFTWARE   (0 - 6)

-> OTHER   (3 - 0)

--|| CAL_SOFT   (3 - 3)

---||| disrsoft   (14 - 4)

----|||| batch   (0 - 11)

----|||| common   (0 - 18)

----|||| doc   (0 - 14)

----|||| enhance   (0 - 2)

----|||| local   (0 - 62)

----|||| output   (0 - 16)

----|||| radio   (0 - 4)

----|||| readme   (0 - 8)

----|||| simulate   (0 - 6)

----|||| startup   (0 - 7)

----|||| system   (1 - 46)

----|||| tools   (0 - 76)

----|||| verify   (0 - 12)

----|||| xy   (0 - 1)

---||| journal   (0 - 275)

---||| win32   (14 - 0)

----|||| batch   (0 - 12)

----|||| common   (0 - 15)

----|||| data   (0 - 0)

----|||| doc   (0 - 11)

----|||| enhance   (0 - 3)

----|||| output   (0 - 16)

----|||| radio   (0 - 5)

----|||| readme   (0 - 9)

----|||| simulate   (0 - 7)

----|||| startup   (0 - 6)

----|||| system   (0 - 46)

----|||| tools   (0 - 78)

----|||| verify   (0 - 13)

----|||| xy   (0 - 2)

--|| FLAT_FIELD   (3 - 1)

---||| DISR#1   (0 - 3)

---||| DISR#2   (0 - 3)

---||| DISR#3   (0 - 16)

--|| NEW_GSE   (0 - 28)

-> STEFFI_ENGEL   (54 - 13)

--|| AZ comparison   (0 - 9)

--|| AZ ir   (0 - 19)

--|| Copy of DLVS-ULVS before combining corr+fluxes   (4 - 1)

---||| DN-Fluxes   (4 - 9)

----|||| input   (1 - 6)

----|||| new dark   (0 - 13)

----|||| old   (0 - 2)

----|||| output   (2 - 4)

---||| VIS_corr_factors   (3 - 30)

----|||| input   (1 - 39)

----|||| not needed   (0 - 14)

----|||| output   (0 - 10)

---||| input   (0 - 6)

---||| old   (3 - 0)

----|||| DLVS   (3 - 10)

----|||| ULVS   (2 - 11)

----|||| VIS_corr_factors_old   (2 - 43)

--|| DATA   (4 - 0)

---||| Descent_test_11Sep96.2   (3 - 26)

----|||| DB   (27 - 0)

----|||| Verification   (2 - 0)

----|||| post   (2 - 0)

---||| Descent_test_11Sep96.2_sim   (2 - 1)

----|||| DB   (5 - 0)

----|||| post   (1 - 0)

---||| Descent_test_11Sep96.3   (3 - 18)

----|||| DB   (26 - 0)

----|||| Verification   (2 - 0)

----|||| post   (2 - 0)

---||| Descent_test_11Sep96.3_sim   (3 - 4)

----|||| DB   (6 - 0)

----|||| Dark   (0 - 81)

----|||| post   (1 - 0)

--|| DLIS-ULIS   (10 - 17)

---||| DN-fluxes   (2 - 11)

----|||| corr_factors   (2 - 0)

----|||| input   (0 - 34)

---||| DN-fluxes_jan18   (6 - 17)

----|||| corr_factors   (8 - 6)

----|||| good copy   (0 - 0)

----|||| input   (0 - 34)

----|||| last changes   (0 - 17)

----|||| old   (0 - 4)

----|||| output   (11 - 11)

---||| DN-fluxes_old   (2 - 4)

----|||| input   (0 - 12)

----|||| output   (0 - 6)

---||| IR_corr_factors   (3 - 13)

----|||| input   (0 - 31)

----|||| output   (1 - 0)

----|||| probably don't need   (0 - 2)

---||| analysis   (3 - 11)

----|||| jan 11   (0 - 6)

----|||| jan12   (0 - 2)

----|||| old   (0 - 5)

---||| input   (1 - 1)

----|||| old   (0 - 2)

---||| output   (2 - 10)

----|||| old   (0 - 18)

----|||| old1   (0 - 9)

---||| plots   (2 - 8)

----|||| old   (0 - 4)

----|||| old1   (0 - 4)

---||| titan14   (1 - 16)

----|||| jan14 data   (0 - 10)

---||| titan14_jan19   (0 - 21)

--|| DLIS_descent   (2 - 4)

---||| input   (0 - 19)

---||| output   (0 - 21)

--|| DLIS_descent_Apr25   (3 - 10)

---||| April 2005   (0 - 19)

---||| input   (0 - 9)

---||| output   (0 - 11)

--|| DLIS_descent_Dec_2005   (3 - 6)

---||| input   (1 - 9)

----|||| old   (0 - 10)

---||| old   (0 - 1)

---||| output   (2 - 20)

----|||| old   (0 - 9)

----|||| old up to may 2006   (0 - 42)

--|| DLVS-ULVS   (10 - 4)

---||| DN-Fluxes   (5 - 28)

----|||| corr_factors   (2 - 8)

----|||| input   (1 - 32)

----|||| misc   (0 - 8)

----|||| old subroutines   (0 - 8)

----|||| output   (1 - 7)

---||| DN-Fluxes_jan19   (5 - 20)

----|||| corr_factors   (4 - 5)

----|||| input   (1 - 32)

----|||| misc   (0 - 8)

----|||| old subroutines   (0 - 8)

----|||| output   (12 - 14)

---||| DN-Fluxes_single_spectra   (0 - 13)

---||| VIS_corr_factors   (3 - 22)

----|||| input   (1 - 21)

----|||| not needed   (0 - 17)

----|||| output   (1 - 1)

---||| analysis   (3 - 18)

----|||| input   (1 - 6)

----|||| old   (0 - 7)

----|||| output   (0 - 2)

---||| input   (1 - 13)

----|||| old   (0 - 2)

---||| misc   (1 - 17)

----|||| plots for talks   (0 - 13)

---||| old   (3 - 0)

----|||| DLVS   (3 - 10)

----|||| ULVS   (2 - 11)

----|||| VIS_corr_factors_old   (2 - 43)

---||| output   (7 - 20)

----|||| old   (0 - 23)

----|||| old2   (0 - 6)

----|||| old3   (0 - 14)

----|||| old4   (0 - 12)

----|||| old5   (0 - 9)

----|||| old6   (0 - 24)

----|||| old7   (0 - 12)

---||| plot visible   (2 - 6)

----|||| namelist files   (0 - 4)

----|||| old   (0 - 9)

--|| DLVS_4avg_sc   (1 - 9)

---||| output   (2 - 27)

----|||| final output   (1 - 41)

----|||| some output   (0 - 26)

--|| DLVS_check_wavelength_cal   (0 - 6)

--|| DLVS_descent   (4 - 14)

---||| crosstalk   (1 - 23)

----|||| probably no use   (0 - 1)

---||| input   (0 - 10)

---||| output   (3 - 14)

----|||| Feb7   (0 - 6)

----|||| March8   (0 - 5)

----|||| extra   (1 - 7)

---||| responsitivities   (0 - 9)

--|| DLVS_descent_3_14_2005   (2 - 14)

---||| input   (0 - 8)

---||| output   (2 - 11)

----|||| Feb7   (0 - 6)

----|||| extra   (1 - 6)

--|| DN_sec   (0 - 4)

--|| Erich_absorption_coef   (9 - 34)

---||| Marty talks   (0 - 4)

---||| Radiative transfer for PC   (0 - 1)

---||| analysis   (2 - 23)

----|||| sept20,06   (0 - 17)

----|||| sept6,06   (0 - 29)

---||| dont need   (0 - 1)

---||| esfit1   (0 - 5)

---||| excel   (0 - 26)

---||| input   (3 - 18)

----|||| old   (0 - 3)

----|||| sept20,06   (0 - 11)

----|||| sept6,06   (0 - 28)

---||| ir_model   (1 - 56)

----|||| Fortran   (0 - 11)

---||| rotation_function   (2 - 11)

----|||| old programs   (0 - 1)

----|||| output   (0 - 116)

--|| Far_IR   (3 - 14)

---||| Rad_Transfer   (5 - 4)

----|||| analysis   (0 - 8)

----|||| input   (0 - 5)

----|||| model   (1 - 764)

----|||| output   (0 - 11)

----|||| read_intensi   (1 - 6)

---||| Rad_Transfer_VIMS   (6 - 9)

----|||| VIMS spectra   (0 - 6)

----|||| analysis   (0 - 3)

----|||| input   (0 - 12)

----|||| model   (0 - 342)

----|||| output   (0 - 11)

----|||| read_intensi   (0 - 6)

---||| methane_coeff   (0 - 12)

--|| Heating Rates   (3 - 18)

---||| Rad_Transfer   (4 - 3)

----|||| input   (0 - 5)

----|||| model   (1 - 196)

----|||| output_paper1   (1 - 68)

----|||| read_intensi   (0 - 4)

---||| graphs for heating paper   (0 - 34)

---||| heating   (1 - 23)

----|||| older programs   (0 - 1)

--|| Heating Rates2   (3 - 0)

---||| Rad Transfer   (4 - 6)

----|||| input   (1 - 6)

----|||| model   (0 - 114)

----|||| output   (6 - 0)

----|||| probably don't need   (0 - 1)

---||| Rad Transfer vis   (3 - 6)

----|||| input   (0 - 4)

----|||| model   (2 - 224)

----|||| output   (4 - 0)

---||| heating   (2 - 3)

----|||| output   (0 - 9)

----|||| plots   (0 - 8)

--|| IR   (10 - 1)

---||| IR alt cont models   (3 - 6)

----|||| analysis   (6 - 14)

----|||| ir_model   (1 - 5)

----|||| rotation_function   (2 - 9)

---||| IR_corr_factors   (4 - 12)

----|||| 2nd try   (0 - 16)

----|||| input   (2 - 10)

----|||| output   (6 - 0)

----|||| probably don't need   (0 - 3)

---||| IR_data   (2 - 0)

----|||| Descent_test_11Sep96.2   (3 - 26)

----|||| Descent_test_11Sep96.2_sim   (2 - 1)

---||| Radiative Transfer   (0 - 7)

---||| analysis   (5 - 10)

----|||| Lyn_fluxes   (0 - 5)

----|||| input   (0 - 5)

----|||| old   (0 - 12)

----|||| old2   (0 - 2)

----|||| tauwagg   (3 - 7)

---||| input   (0 - 0)

---||| old   (1 - 3)

----|||| IR_Simulator_old   (3 - 14)

---||| old stuff   (2 - 22)

----|||| old   (2 - 0)

----|||| old programs   (0 - 4)

---||| output   (0 - 0)

---||| read_ulis_dlis   (5 - 7)

----|||| data1   (0 - 10)

----|||| data2   (0 - 6)

----|||| input   (0 - 19)

----|||| old2   (0 - 5)

----|||| old3   (0 - 6)

--|| IR Simulator_Lyn   (1 - 208)

---||| output   (0 - 0)

--|| IR alt spec models   (3 - 1)

---||| analysis   (0 - 16)

---||| ir_model   (0 - 6)

---||| rotation_function   (2 - 9)

----|||| input   (0 - 6)

----|||| output   (0 - 12)

--|| IR alt spec models 2006   (11 - 13)

---||| Bruno methane coeff   (0 - 6)

---||| analysis   (4 - 42)

----|||| october06   (0 - 19)

----|||| summer06   (0 - 24)

----|||| summer06_b   (0 - 8)

----|||| wrong   (0 - 2)

---||| input_fall06   (1 - 26)

----|||| oct20006   (0 - 9)

---||| ir_model   (3 - 187)

----|||| october06   (0 - 143)

----|||| summer06   (0 - 13)

----|||| summer06_b   (0 - 3)

---||| kabsfront   (2 - 38)

----|||| Lyn's versions   (0 - 3)

----|||| zip   (0 - 1)

---||| model input   (0 - 25)

---||| phase_function   (0 - 2)

---||| rotation_function   (1 - 10)

----|||| output   (1 - 38)

---||| summer06   (0 - 32)

---||| summer07   (0 - 10)

---||| test_input   (1 - 37)

----|||| lyn files   (0 - 2)

--|| IR analysis Aug05   (6 - 15)

---||| calculate_weights   (2 - 2)

----|||| input   (0 - 2)

----|||| output   (0 - 3)

---||| calculate_weights_dlis   (1 - 4)

----|||| output   (0 - 3)

---||| comparison   (1 - 4)

----|||| input   (0 - 3)

---||| ir_models   (2 - 9)

----|||| extra   (0 - 9)

----|||| old   (0 - 4)

---||| rotation_function   (3 - 10)

----|||| input   (0 - 22)

----|||| old   (0 - 2)

----|||| output   (1 - 0)

---||| rotation_function_dlis   (2 - 10)

----|||| input   (2 - 19)

----|||| output   (2 - 38)

--|| IR analysis Nov05   (5 - 14)

---||| comparison   (1 - 3)

----|||| input   (0 - 6)

---||| ir_models2   (1 - 15)

----|||| old   (0 - 6)

---||| ir_models_old   (0 - 8)

---||| rotation_function   (4 - 9)

----|||| backup Jan 2006   (0 - 9)

----|||| input   (1 - 2)

----|||| input_files   (0 - 2)

----|||| output   (3 - 6)

---||| smooth_ir   (3 - 15)

----|||| input   (0 - 2)

----|||| input_files   (0 - 8)

----|||| output   (0 - 46)

--|| IR analysis Oct05   (5 - 5)

---||| calculate_weights_dlis   (1 - 3)

----|||| output   (0 - 7)

---||| calculate_weights_ulis   (1 - 2)

----|||| output   (0 - 10)

---||| comparison   (1 - 2)

----|||| input   (0 - 4)

---||| ir_models   (0 - 10)

---||| rotation_function   (4 - 9)

----|||| input   (5 - 25)

----|||| input_files   (0 - 2)

----|||| old programs   (0 - 1)

----|||| output   (5 - 50)

--|| IR combined   (5 - 23)

---||| Radiative transfer for PC   (0 - 1)

---||| analysis   (0 - 16)

---||| ir_model   (1 - 49)

----|||| Fortran   (0 - 12)

---||| rotation_function   (2 - 11)

----|||| old programs   (0 - 1)

----|||| output   (1 - 40)

---||| summer06   (0 - 4)

--|| IR combined with amoeba   (5 - 13)

---||| Radiative transfer for PC   (0 - 1)

---||| analysis   (0 - 16)

---||| ir_model   (1 - 28)

----|||| Fortran   (0 - 11)

---||| output   (1 - 10)

----|||| old 1   (0 - 15)

---||| rotation_function   (2 - 10)

----|||| old   (0 - 1)

----|||| output   (0 - 26)

--|| IR ground cont models   (3 - 1)

---||| analysis   (2 - 6)

----|||| feb06   (0 - 16)

----|||| jan30   (0 - 11)

---||| ir_model   (0 - 6)

---||| rotation_function   (2 - 9)

----|||| input   (2 - 3)

----|||| output   (2 - 7)

--|| IR models   (0 - 7)

--|| IR rot   (3 - 18)

---||| input   (0 - 18)

---||| output   (0 - 8)

---||| probably don't need   (0 - 27)

--|| Stefan   (3 - 21)

---||| IR   (0 - 40)

---||| don't need this   (0 - 3)

---||| input   (0 - 6)

--|| ULIS_descent   (2 - 4)

---||| input   (0 - 23)

---||| output   (0 - 12)

--|| ULIS_descent_Apr25   (2 - 20)

---||| input   (0 - 21)

---||| output   (0 - 15)

--|| ULIS_descent_Dec_2005   (2 - 4)

---||| input   (1 - 15)

----|||| old   (0 - 10)

---||| output   (1 - 24)

----|||| old   (0 - 2)

--|| ULVS   (4 - 10)

---||| 4avg   (2 - 8)

----|||| extra copy   (0 - 1)

----|||| output   (3 - 6)

---||| output   (1 - 3)

----|||| final output   (0 - 21)

---||| ulvs_single_col   (0 - 6)

---||| xls files   (0 - 1)

--|| ULVS_descent   (4 - 36)

---||| input   (1 - 22)

----|||| corr_files   (0 - 5)

---||| make crosstalk factors   (0 - 14)

---||| output   (5 - 23)

----|||| Feb18   (0 - 13)

----|||| Feb22   (0 - 8)

----|||| extra   (1 - 18)

----|||| old aug05   (0 - 27)

----|||| old feb7   (0 - 4)

---||| responsitivities   (0 - 9)

--|| ULVS_descent_feb16   (3 - 21)

---||| input   (0 - 10)

---||| make crosstalk factors   (0 - 14)

---||| output   (2 - 11)

----|||| extra   (0 - 8)

----|||| old feb7   (0 - 4)

--|| ULVS_descent_feb9   (2 - 14)

---||| input   (0 - 1)

---||| output   (1 - 8)

----|||| extra   (0 - 7)

--|| VIMS data   (0 - 21)

--|| VIMS models   (0 - 21)

--|| VIMS_ir_Aug2007   (1 - 8)

---||| idl   (3 - 7)

----|||| input   (0 - 15)

----|||| model   (0 - 339)

----|||| output   (1 - 23)

--|| VIMS_vis   (4 - 11)

---||| input   (2 - 22)

----|||| Normalized phase functions 5-7-2007   (0 - 15)

----|||| old   (0 - 3)

---||| model   (0 - 223)

---||| output   (0 - 9)

---||| paulo   (2 - 4)

----|||| input   (0 - 6)

----|||| model   (0 - 6)

--|| VIMS_vis_Aug2007   (3 - 13)

---||| VIMS_TB_Huygens   (0 - 21)

---||| idl   (3 - 16)

----|||| input   (1 - 12)

----|||| model   (1 - 244)

----|||| output   (1 - 26)

---||| more of the same   (1 - 1)

----|||| VIMS_TB_1   (0 - 21)

--|| crosstalk   (8 - 0)

---||| dlvs   (5 - 0)

----|||| input   (0 - 21)

----|||| maybe   (0 - 3)

----|||| output   (0 - 2)

----|||| reduction   (1 - 15)

----|||| zenith   (3 - 13)

---||| excel   (0 - 16)

---||| input   (1 - 22)

----|||| old input   (0 - 2)

---||| input_programs   (2 - 18)

----|||| Lyn   (0 - 10)

----|||| old   (0 - 4)

---||| old programs   (0 - 2)

---||| old programs 2 ulvs   (0 - 14)

---||| ps   (0 - 2)

---||| ulvs   (4 - 1)

----|||| descent   (0 - 6)

----|||| find_factor   (0 - 20)

----|||| reduction   (3 - 13)

----|||| useless   (0 - 1)

--|| descent_input   (0 - 22)

--|| dlis_ulis_disr2   (1 - 10)

---||| output   (0 - 4)

--|| input   (0 - 15)

--|| matrix   (3 - 15)

---||| excel   (0 - 11)

---||| input   (0 - 2)

---||| original   (0 - 6)

--|| more_programs   (1 - 7)

---||| convert_xls   (0 - 8)

--|| namlists   (0 - 7)

--|| old_programs   (7 - 7)

---||| Oct10,02   (0 - 6)

---||| Sept11,02   (0 - 2)

---||| Sept12,02   (0 - 5)

---||| Sept18,02   (0 - 15)

---||| Sept25,02   (0 - 1)

---||| Sept4,02   (0 - 5)

---||| Sept9,02   (0 - 2)

--|| output   (2 - 5)

---||| save output   (0 - 27)

---||| sorting   (0 - 24)

--|| sep25 old   (2 - 0)

---||| 2ndtry   (0 - 2)

---||| they work!!   (0 - 2)

--|| test_tip   (0 - 27)